## Slide 1
EduGrid MicroGrid Demonstrator
ECE 445: Group 70
Ahmet Colak
Jason Hart
Srijan Kunta
TA: Abdullah Alawad
25 April 2026

## Slide 2
Our Project
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Power grid protection/design is not taught enough in early education
We believe everyone should know how grid reliability and fault isolation works
We wanted to build a supplemental tool to aid Power Engineering education
Objective

## Slide 3
Design Overview
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Changes from original design:
OLED display to 5V LCD
7.4V Li-ion Battery pack was replaced with a 9.6 V Li-ion Battery pack
The 5V and 3.3V power rail is now being directly stepped down from the battery pack via 2 buck converters

## Slide 4
Schematic
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 5
Schematic
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
Schematic
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
PCB design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Lots of research for proper buck converter design.
Hot loop size minimized
Buck converter isolation
Thick power rail traces
PMOS footprint debugging

## Slide 8
Requirements and Verification
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
High Level Requirements
The user can select and clear the five available fault scenarios (permanent faults, transient faults, power factor correction, load shedding, selective generation).
The component identification circuit accurately computes and displays the value on the screen within 15% error.
The on-board display shows the relevant information for each fault scenario (power factor current state and target, frequency, voltage, and current simulation values).

## Slide 9
Video
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 10
Results and Analysis
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Real capacitance | Measured Capacitance Range | Error
10 µF | 9.24 µF | 7.6%
33 µF | 31.64 µF | 4.1%
47 µF | 45.88 µF | 2.4%
Reasons for error include:
- Voltage divider for the tau threshold is slightly lower than 63.2% of V_in
- Small leakage current charging capacitors before the user presses the button
- 555 timer frequency deviation from 10kHz changes the pulse width for calculations
​

## Slide 11
RC Capacitor Voltage Charging Cycle
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
V
t
63.2% tau threshold from voltage divider
+/- 7.6% error
User's second press of rotary switch begins charging

## Slide 12
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Lessons learned
Ensure all PCB footprints match ordered part's dimensions and pinouts
Review team contract schedule often to better predict future workload
Maximize PCB prototypes by designing alongside our breadboard
Design PCB layout with ease of construction and repairability in mind

## Slide 13
We would like to thank the course staff for all the guidance they have provided us throughout the building of our project.
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING