## Slide 1
ECE 445 Final Presentation
Team 46
Snooze-Cruiser
Electrical & Computer Engineering
Team members: Alex Wang, Jiachen Hu, Jizhen Chen
DATE 05/01/2026

## Slide 2
Introduction
Sleep inertia reduces alertness after waking
Users often dismiss alarms unconsciously
Existing alarms rely only on sound
Snooze-Cruiser! – a robotic alarm requiring physical interaction to disable
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 3
Develop a robotic alarm system that enforces physical user interaction
Ensure reliable alarm activation at the programmed time
Enable autonomous indoor navigation with obstacle avoidance
Require pickup detection to disable the alarm
Maintain safe operation in confined environments
Objectives
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 4
System Demonstration
Alarm triggered at setup time (user side)
Robot initiates motion and audio output
Autonomous navigation with obstacle avoidance
Rolling the alarm to shut down the process
Key Test Observations
Stable movement
Performing obstacle avoidance
Alarm is terminated only by user feedback
Accurate time counting and enough lasting power
Description of the Project
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 5
Block Diagram
System Overview
Central MCU
Motion subsystem
Sensors
IMU(Gyroscope)
Audio - alarm
Original Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
Original Design
Multiple laser sensors - 3 sensors providing full view for obstacle evasion
IMU / Stop Condition: Alarm stops when robot is lifted
Hardware Integration: Fixed configuration after initial soldering
Final Implementation
Single laser sensor: Enough, mutiple sensors configuration is hard to tune to fine
IMU / Stop Condition: Alarm stops when robot is rolled over
Hardware Integration: Replaced modules and adjusted wiring for stability
Design Evolution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
Microcontroller (STM32F446RCT6)
Resoponsible to sending signal and navigate for ALL the other subsystems
Connects between subsystems (e.g. OLED and Sensors)
Support real-time navigation decisions
Functional Block Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
MCU

## Slide 8
Time counting subsystem
Accurate time counting over long period of time
User Interface (Buttons and OLED)
Accurately display the necessary parameters (e.g.time counting)
User inputs smoothly and accurately
Functional Block Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Crystal Oscillator
OLED

## Slide 9
Motion Subsystem
Enable stable and controlled robot movement
Capable of moving in regular indoor environments
Sensing Subsystem (Laser Sensors/Photodiode)
Detect obstacles
Provide reliable distance measurements
Detect light condition
Functional Block Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Motor
Laser sensor

## Slide 10
IMU(gyroscope)
Detect condition of the alarm (user interference)
Avoid false triggering from vibration
Audio Subsystem
Generate sufficient alarm volume
Power Source
7.4V from Li-ion battery
5V and 3.3V step down for other subsystems
Functional Block Requirements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Gyroscope
Speaker
Battery

## Slide 11
Requirements versus Results
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
 | Requirements and verification | Test results
Motion Subsystem | Continue operation > 5 minutes | Successfully operated over 20 minutes at least
Obstacle Avoidence | Seldom crashes in regular indoor condition | Successfully performed with barely any crashes
IMU / Stop Condition | Response in < 5 seconds | Responding in 3 seconds +/- 750 miliseconds
Time Counting | Accuracy < 2 seconds | Error is within 100 milisecond
Battery last | Over 12 hrs | Can last over 48hrs

## Slide 12
Success
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Reliable time counting
Accurate user inputs
Stable motion and continuous operation
Effective obstacle avoidance
Accurate pickup detection response
Battery last more than 48hrs

## Slide 13
Challenges & Engineering Solutions
Power Regulation Failure:
Power Regulation burnt → replaced with external regulator on different board
IMU Detection Issue:
Lift detection unreliable → switched to flip-based detection
Sensor Tolerance:
Huge errors generated with multiple sensor → single senor
Hardware Integration:
Component replacement and wiring adjustments for stability
Challenges
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 14
Conclusion
Successfully build up a robotic alarm
sensing, navigation, movement, audio, display, button control, and time counting
It serves the purpose as a traditional alarm
Moreover, it achieves our objectives of making a “Snooze-cruiser”
Designing -> Assemble -> Debugging -> Fining
Most importantly, team working
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 15
Future Work
- Improve navigation (more sensor & finer programming)
- Concrete body for the alarm bot
- Adding battery load detection
- Fining the mechanical design of the alarm bot
- More features on the user interface
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING