## Slide 1
Ant-Weight Battlebot – DC Hammer
Carson Sprague, Ian Purkis, Gage Gathman
Group 37

## Slide 2
Create a battle-bot that’s immune to inversion and uses a hammer as the primary attack method
Develop a custom system to replace the function of a motor driver
Compete (and hopefully win) in the battle-bot competition
Project Objective

## Slide 3
Develop an antweight (<2 lb) 3D printed battle bot capable of maintaining functionality when inverted
Use Bluetooth enabled MCU to pilot bot with external controller (laptop)
Combine a crushing hammer with a lifting wedge
Use ultrasonic sensor to automate attacks
Use accelerometer to trigger control inversion
Implement Control Using ESP32-S3 Driving Custom H-Bridges through Gate Drivers
Original Design Fundamentals

## Slide 4
Block Diagram

## Slide 5
No dedicated wedge mode
Switch from Dual NMOSFETs to Complementary N & P MOSFETs
Switched 5V Rail from an LDO to a Buck Converter
Created a custom packet format with built-in safety redundancy for motor control
High Level Design Changes
W | A | S | D | SHIFT | TAB | SPACE | DUP

## Slide 6
Includes: ESP-32, Onboard Software systems (BLE, scheduling, boot)
Apache NimBLE Stack initialization and teardown
Input decoder (BLE callback)
Event loop which reads sensor input (daemon)
Leverage both cores on the ESP32-S3-WROOM-1
Control Subsystem

## Slide 7
Includes: Control Device (laptop), Status Lights, Software Kill Switch
User Interface Subsystem

## Slide 8
Includes: MC3479 Accelerometer, Adafruit 4007 Ultrasonic Sensor, Voltage Divider
Takes in information from environment to be used in automation/adaptation of control
Ultrasonic sensor drives hammer action
Accelerometer adjusts control inputs and “rehomes” hammer resting position (SPI)
Sensor Subsystem

## Slide 9
Includes: PWM Signal Generation, 2 12V 600rpm Motors, 12V 50rpm High Torque Motor, Motor Device Driver
Configure 3 Distinct Motor Objects: 2 Drive, 1 Arm
Each motor has its own timer, comparator, and operator module and 2 generators
Timer counts up to length of period (ticks) then resets
Comparator triggers generator level based on current tick
Generator outputs voltage signal
Operator is connective tissue
Drive + High Torque Motor Subsystem
via Espressif Peripheral API Documentation
Notes: 12 V 600 RPM geared brushed DC motors,
Current Draw 10 mA unloaded, stall current 60 mA
Wheel 60 mm -> 188 mm / rotation
867 mm/s / 188 mm, 4.6 rotations/sec -> 276.7 RPM under load

## Slide 10
Input handler feeds current directional input to a drive control function
Based on combo of keys we set a drive motor to forward, backward, or off
  Direction = Forward? -> Set left and right drive motors to forward
  Direction = Tank Left? -> Set left to backward, and right to forward
How do we handle dead time and prevent shoot through?
  Conflicting inputs: do nothing
  On packet change (state transition) hold motors low for a small delay
Input handler only updates drive control if packet is new or inversion flag has changed
Drive + High Torque Motor Subsystem Cont.
Drive Control Software
Notes: 12 V High Torque Motor
According to Spec Sheet
2.3 A Stall Current
~100-250 mA run current
50 RPM -> 16 kg-cm of torque
20 cm lever arm -> 0.8 kg lifting power, plenty to flip a bot
5/6 Rotations/sec -> 300 degrees/sec at no load,
Observational -> real performance slightly lower
Torque limited by Plastic Fixturing.

## Slide 11
Manual input from input handler sets hammer flag
Ultrasonic sensor threshold check in processor task also sets this flag
Last item in processor task checks this flag and calls hammer swing protocol
If inversion flag has changed, we reset the default position of the hammer
Reset (rehome) cancels any queued hammer action
Inside hammer swing protocol we perform an inversion check
  Cancel swing, and call “rehome” if check fails
Drive + High Torque Motor Subsystem Cont.
Hammer Control Software
Notes: 12 V High Torque Motor
According to Spec Sheet
2.3 A Stall Current
~100-250 mA run current
50 RPM -> 16 kg-cm of torque
20 cm lever arm -> 0.8 kg lifting power, plenty to flip a bot
5/6 Rotations/sec -> 300 degrees/sec at no load,
Observational -> real performance slightly lower
Torque limited by Plastic Fixturing.

## Slide 12
Requirements
  Minimum 2.3 A sustained (High Torque Stall Current)
  Capable of Switching at 20 kHz
  Protects MOSFET Body diodes
  Step Between 3.3 V MCU signals and 12 V Gate Signals
As Designed
  Voltage Loss
  3 A x (43 mΩ + 36 mΩ) = 0.237 V Drop
  Current Maximum
  Limited by 2 x 1 mF capacitors having 1.5 A Rated Ripple Current (> 300 Hz Frequency)
  Max Switching Frequency
  Gate Rise + P/N FET Rise + Gate Fall + P/N FET Fall
  25 ns + 50 ns + 10 ns + 25 ns + 55 ns + 62 ns = 227 ns
  Theoretical Switching Frequency in the MHz
H-Bridges

## Slide 13
Requirements
  5 V, >1 A, ±10% tolerance
  3.3 V, >0.5A, ±10% tolerance
Power Subsystem
As Designed
  5 V, 3 A, ±3% tolerance
    TI MOSFET-int Buck 1.2 MHz Switching Freq., ±1% voltage ref. accuracy, 100 µA Quiescent Current
  3.3 V, 1 A, ±1% tolerance
    Diodes Inc. LDO, 70 dB PSRR, 6 mA Quiescent Current, Thermal Protection

## Slide 14
Project Build

## Slide 15
Project Testing – Drive & Power
Requirement | Verification | Results
The battlebot should achieve a top speed of 1 m/s | Drive the battlebot 1 m, and record the resultant time | FAIL – 0.86 m/s achieved under full speed
5V Buck Converter Should have less than 3% voltage ripple | Measuring the output voltage via oscilloscope under standard load | PASS – 2.7% voltage ripple
Battery Voltage Sensing should provide ±5% accuracy across the input voltage range | Measure and Plot the Voltage Output while powering the battlebot with benchtop DC supply | PASS – Within ±3% Accuracy

## Slide 16
Project Testing – Drive & Power
Requirement | Verification | Results
H-Bridge Should Not Experience Shoot-Through | Measure Voltage Trace on Motor Terminals to watching for Overlap when going from one input to another | Pass – No Signs of Overlap, Deadtime is apparent, & No Voltage Collapse Behavior
Battery Duration must Exceed 3 minutes of run time – Coordinate with a round, with time to spare. | During Development and Testing, Record Battery Voltages after being used. | Pass – During the testing period, no battery has been depleted beyond 78% discharge.

## Slide 17
Project Testing – Sensors & Software
Requirement | Verification | Results
The system shall detect when the bot is inverted and apply motor control state changes within 500ms | Flip the bot over and measure the time for motors to change direction | FAIL – Detection time closer to 1s
The ultrasonic sensor shall detect objects at 25cm with an accuracy of +- 2cm | Slowly move an object closer along a meterstick and log ultrasonic data to the terminal | PASS – The ultrasonic sensor detected objects at 25cm with an accuracy of +- 1cm
Must achieve a latency of under 1ms from receiving a keypress to driving the motors | Initialize a software timer and track the time from receiving a packet to driving the motors | PASS – Our packet handler had an average latency of 0.5ms

## Slide 18
Circuitry and PCB design (Omission of Pull-Down Resistors)
Software synchronization (hammer swing action, BLE packet handling, h-bridge shoot-through)
3d Modeling (integration & tolerance, accessibility)
Challenges

## Slide 19
Fully functional PCB and power system to support two drive motors, one high torque motor, three sensors, and an MCU
Responsive software that manages BLE connections/packets, sensors, motor control, and drive inversion
Rugged chassis with hot-swappable components that is resilient to inversions
Successes

## Slide 20
Communication is important especially in cross-functional teams to avoid integration issues
Save working states to come back to if needed
Much less stressful to work and finish early
Order PCBs & Parts Early
Begin 3D Printing Early
Pay Attention to the Basics
Conclusions

## Slide 21
Robotics and Motors Drivers are well established systems, with extensive documentation and options for set solutions.
Sensing and Automation are interesting avenues, that pose more integration issues, which is more of a design challenge, and provides a requirement for more creativity.
Using a higher-performance MCU with more cores allows for more complicated and sophisticated designs.
Recommendations for Further Work

## Slide 22
Thank You!
Carson Sprague, Ian Purkis, Gage Gathman
Group 37

## Slide 23
Additional Slide for Data on H-Bridges