## Slide 1
Facial Quantum Matching Mirror
An interactive prototype for the Illinois Quantum & Microelectronics Park
ECE 445 · Senior Design · Spring 2026 · Team 8
Akhil Morisetty
Alex Cheng
Ethan Zhang
Teaching Assistant: Wesley Pang

## Slide 2
01 · INTRODUCTION
What we are building
The Facial Quantum Matching Mirror is an interactive display that uses a one-way mirror and facial recognition to pair the user with a well-known figure they visually resemble.
When idle, 70% reflective glass behaves like a normal mirror. When the user selects a category — scientists, engineers, or entrepreneurs — the system illuminates, captures their face, and overlays the matched figure on the monitor behind the glass.
THE EXPERIENCE
“You are face-to-face with a figure who resembles you.”
One-Way Mirror
70% reflective glass — a mirror at rest, a window when the display is active.
Face Embeddings
MobileFaceNet generates a 512-D vector capturing the visual identity of each face.
Closest Match
Cosine similarity finds the most similar figure from a precomputed database.

## Slide 3
02 · PROBLEM & OBJECTIVE
Why it matters
THE PROBLEM
Public engagement for Illinois Quantum Park
Chicago is investing $500M in the Illinois Quantum & Microelectronics Park. Professor Kwiat needs a viable, museum-grade prototype for investors — one that turns abstract science into a personal, memorable interaction.
$500M
Chicago's investment in the Illinois Quantum & Microelectronics Park
OUR OBJECTIVE
Build a working prototype that proves the concept
01
Reflect & reveal
A surface that is a mirror at rest and a display when active.
02
Recognize & match
Identify the user's facial features and find the closest figure in a curated database.
03
Inspire & represent
Connect users to diverse STEM pioneers across science, engineering, and entrepreneurship.

## Slide 4
03 · SYSTEM DESIGN
Block diagram & subsystem flow
Four subsystems coordinate every interaction. The Start-Scan button triggers the cycle; data flows from ESP32 to Raspberry Pi via Bluetooth, and the Pi drives the display.
POWER SUBSYSTEM
Distributes voltage
· USB-C 5V (Pi)
· 5V → 3.3V regulator (ESP32)
· 5V rail (Monitor)
STARTUP SUBSYSTEM
ESP32 + buttons
· Scientists / Engineers / Entrepreneurs
· Start-Scan button
· Bluetooth SPP → Pi
DISPLAY SUBSYSTEM
Camera + monitor + glass
· Logitech C270 webcam (USB)
· 21.5" IPS monitor — 350+ cd/m²
· 70% reflective glass
BACKEND (Raspberry Pi 4)
Facial recognition pipeline
· OpenCV face detection
· MobileFaceNet 512-D embedding (ONNX Runtime)
· Cosine similarity match
BT
HDMI / USB
ACTIVATION Start-Scan button → ESP32 → Bluetooth → Pi → Capture → Match → Display

## Slide 5
04 · Schematic Design
PCB Schematic

## Slide 6
05 · PCB Layout
PCB Layout

## Slide 7
06 · DESIGN DEEP-DIVE
Backend: facial recognition pipeline
Once the Pi receives the START signal, six stages run end-to-end in roughly 4.5 seconds — well inside our 10-second requirement.
1
CAPTURE
Webcam → frame
~1000 ms
2
DETECT
Crop face
~50 ms
3
EMBED
MobileFaceNet
~400 ms
4
MATCH
Cosine similarity
~3000 ms
5
DISPLAY
Pygame fullscreen
~20 ms
6
ACK
DONE → ESP32
<10 ms
PER-STAGE TIMING
Chart: milliseconds
| Capture | Detect | Embed | Match | Display | ACK
Latency (ms) | 1000 | 50 | 400 | 30 | 20 | 8
END-TO-END LATENCY
~4.5 s
vs. 10-second requirement
Comfortable headroom for retries

## Slide 8
07 · ALGORITHM
How a face becomes a vector
112×112
MobileFaceNet
v ∈ ℝ⁵¹²
[ 0.12, −0.04,
0.81, …,
0.27 ]
512-D embedding
cosine sim.
Best match
A face is reduced to a 512-dimensional vector. Faces that look similar produce vectors that are close in this space — exactly what cosine similarity measures.
COSINE SIMILARITY
sim(u, v) = (u · v) / (∥u∥ · ∥v∥)
match = argmaxᵢ sim(v_user, v_database[i])
WHY THESE CHOICES
Optimized for an edge device
Model
MobileFaceNet — < 1M params, ~4 MB
Runtime
ONNX Runtime — fast on ARM, low memory
Embedding
512-D float vector per face
Database
Precomputed offline → embeddings.npy
Search
Single vectorized cosine pass per category
Loaded once
Model + DB held in RAM at startup

## Slide 9
08 · TOLERANCE ANALYSIS
Will the monitor be visible?
The mirror must reflect when idle and reveal the display when active. We bound the required monitor brightness from ambient lighting and a desired contrast ratio.
VARIABLES & TARGETS
Symbol | Meaning | Value
L | Ambient lighting | 500 lux
R | Mirror reflectance | 0.7
T | Mirror transmittance | 0.3
B | Monitor brightness | 350 cd/m²
ρ | Effective reflectance | 0.3
K | Contrast factor (target) | 3
Standard museum lighting (~500 lux); glass spec'd at 70% reflective; monitor at 350+ cd/m².
Samsung S22D304 — 350 cd/m² nominal, exceeds requirement.
STEP 1 · AMBIENT LUMINANCE OF REFLECTION
L_ambient = (L · ρ) / π = 47.7 cd/m²
STEP 2 · REQUIRED DISPLAY LUMINANCE
L_display ≥ (L_ambient · K · R) / T
= 333.9 cd/m²
CONCLUSION
Need ≥ 334 cd/m² monitor with ≤ 70% glass reflectance.
Our 350 cd/m² Samsung IPS + tempered glass meets this with margin.

## Slide 10
09 · REQUIREMENTS & VERIFICATION
How we know it works
Each subsystem has measurable requirements with a defined verification procedure. Highlights below — full R&V tables in the design document.
SUBSYSTEM | REQUIREMENT | VERIFICATION METHOD | TARGET
Display | Camera captures user's face after activation | Time activation → first valid frame across repeated trials | < 3 s
Display | Glass behaves as a mirror in idle | Visual inspection under multiple ambient lighting levels | 70% R
Startup | ESP32 → Pi message delivery without loss | 20-trial test logging button-press and Pi-receive timestamps | < 100 ms
Startup | Continuous operation without reset | 2-hour soak test with periodic START signals | 0 resets
Power | 5V → 3.3V regulator stable across loads | Multimeter at no-load, half-load, full-load | 3.3 V ± 0.1
Backend | Top-1 match accuracy across validation set | Run validation images per category; compare top match to ground truth | ≥ 85%
Backend | End-to-end pipeline latency | Time 25 captures → matched-result delivery | < 10 s

## Slide 11
10 · RESULTS
Where we landed
~4.5 s
End-to-end pipeline latency
Bench-tested on Pi 4 with MobileFaceNet
3
Categories live in the database
Scientists · Engineers · Entrepreneurs
PCB v3
Final hardware revision
ESP32 + AP62250 regulator + button input
WHAT WE BUILT
PCB designed, ordered, and soldered (final revision)
5V → 3.3V regulator verified within ±0.1 V across loads
ESP32 ↔ Pi Bluetooth SPP communication established
Camera → face detection → embedding pipeline running on Pi
Per-category embedding databases precomputed offline
Wooden frame, monitor, and one-way mirror glass mounted
HIGH-LEVEL REQUIREMENTS — STATUS
Full interaction cycle within 20 s
Met (~4.5 s)
70% reflective glass, 30% transmittance
Met (Samsung S22D304 + tempered glass)
≥ 85% top-match accuracy
Met on validation set

## Slide 12
11 · CONCLUSION
From prototype to museum installation
We built a working prototype that pairs a one-way mirror with a real-time facial recognition pipeline. The system reliably matches a user with a STEM pioneer in roughly 4.5 seconds — a fraction of our 10-second requirement — and the optical analysis confirms a 350 cd/m² monitor is visible through 70% reflective glass under museum lighting.
FUTURE WORK
Quantum context
Add a short biographical card or animation about each matched figure's contribution to quantum science.
Fine-tuned model
Replace MobileFaceNet with a model fine-tuned on our specific database for higher top-1 accuracy.
Museum hardening
Industrial enclosure, anti-vandalism mounting, and thermal management for 8-hour-a-day public use.
Thank you · Questions welcome