## Slide 1: Adaptive Baby Monitoring System
Team 56
Michael Qiu, Luis Ramirez, Yueyang Lin
ECE 445 Senior Design
May 3, 2016

## Slide 2: Motivation

## Slide 3: Introduction
Purpose
  Notify parents or guardians with hearing disorders whenever their
  baby cries
  Provide quick, automated solution to ease baby’s crying
Features
  Cry detector
  Mobile notifications through Bluetooth
  Music player

## Slide 4: System Overview

## Slide 5: Project Setup

## Slide 6: Cry Detector
Apply MFCC Filter
SVM Classifier
Cry
No Cry

## Slide 7: Mel-Frequency Cepstrum Coefficients
Purpose: Obtain average power distributed across frequency components in compact form
1) Divide the signal into 25ms frames
2) Take Discrete Fourier Transform of windowed excerpt of signal
3) Obtain power spectral estimate

## Slide 8: Mel-Frequency Cepstrum Coefficients (continued)
4) Compute Mel-spaced Filterbank and filterbank energies (26 filterbanks)

## Slide 9: Mel-Frequency Cepstrum Coefficients (continued)
5) Take Discrete Cosine Transform of log filterbank energies to obtain
cepstral coefficients (13 MFCC coefficients)

## Slide 10: MFCC Results

## Slide 11: Support Vector Machine Classifier
Define optimal separating hyperplane based on training data
Minimize distance between hyperplane and data points from training data
2 categories: “cry” and “no cry”
Optimization Problem
Minimize
Subject to

## Slide 12: Cry Detector Results
10-fold Cross Validation Accuracy: 94.8453%
Resubstitution Loss: 4.9088%
Testing Set:
50 cry samples: 100% accuracy
50 no-cry samples: 88.89% accuracy
False Detection Rate: 11.11%

## Slide 13: Digital Signal Processor
Export SVM Classifier from MATLAB onto on-chip memory of DSP
Implement MFCC process
Send signal to microcontroller based on classification result
Challenges:
On-chip memory not big enough to store SVM classifier parameters
Instruction set very limited

## Slide 14: Microcontroller
An atmega328p is used as the microcontroller for the system
Controls when to start and stop the audio playback
Sends serial data to the Bluetooth to send the notification to phone

## Slide 15: Audio Playback
Purpose
Used for playing lullabies to calm down a baby
Only triggered once the a cry has been detected
Challenges
Had to playback an audio file once a cry was detected
Minimize the amount of audio artifacts

## Slide 16: Audio Playback
Requirements
Needed to minimize audio popping and other artifacts
Less than 5 artifacts/minute
Solution
Disable audio before audio file was done playing
Include a delay during the playback to prevent slow down

## Slide 17: Audio Amplifier
Why do we need an audio power amplifier?
Microcontroller output has low voltage levels and current limitation.
Speakers requires a lot of current to drive because of their low impedance.

## Slide 18: Audio Amplifier
Implementation
Differential input stage to compress common mode noise
Class A voltage amplification to minimize distortion
Class AB output stage for high current output

## Slide 19: Audio Amplifier
Challenges and Solutions
Power dissipation vs. distortion
  Use a controllable voltage spreading network to achieve optimal balance
Output stability
  Add Miller capacitor to lower the frequency of output pole
Ripple rejection
  Use regulated power supply
  Change the topology to increase power supply rejection in the future

## Slide 20: Audio Amplifier

## Slide 21: Audio Amplifier
Output at least 8Vp-p to 8Ω load with 1Vp-p input at 1kHz
  Ensure enough power for sound pressure level
  Ensure at least 8V/V overall gain
Vin
Vout

## Slide 22: Audio Amplifier
Other requirements and Tests:
3dB bandwidth covers 20Hz-20kHz
  Gain drops by 0.14dB at 20Hz and 0.06dB at 20kHz
Idle power less than 2W
  At idle, power dissipation = 12V*0.066A+|(-12V)|*0.081A=1.764W
DC offset less than 1V
  DC offset is -0.13V
Adjustable gain
  Achievable with a potentiometer

## Slide 23: Power Supply
Component | Voltage | Current | Power | Test Results
Amplifier | +12V | 1A | 12W | +11.8V
 | -12V |  |  | -12.2V
Microcontroller | +5V | 4mA | 20mW | +5.04V
SD Card | +3.3V | 100mA | 330mW | +3.29V
Bluetooth | +5V | 30mA | 150mW | +5.04V
Total |  |  | >13W | 

## Slide 24: Power Supply

## Slide 25: Further work
Possible features include
On/Off command support from Bluetooth.
Volume control command from Bluetooth.
Full range of lullabies to pick and choose from.
Using a DAC for better sound quality.
Wider range of training data for classifier.
Sending microphone audio through Bluetooth.

## Slide 26
Thank you!