## Slide 1
Solar Patio Umbrella
Final Presentation
May 3rd, 2016
Team #37
ECE 445 – Spring 2016
Notes: ECE Main Slide

## Slide 2
Presentation Agenda
1
Introduction to Project
2
Modular Design
3
Conclusion and Future Work

## Slide 3
Solar Patio Umbrella
The Idea
  Benefit our environment using renewable energy
  Save Money
  Develop a patio umbrella entirely powered by solar energy
Features
  Maximum Power Point Tracking (MPPT) built in
  Controllable dimming LED lighting system
  USB port to charge phone
  Sun tracking ability

## Slide 4
Block Diagram
Power Module
Execution Module
Signal Output
Power Lines

## Slide 5
Power Module

## Slide 6
Power Module
  Solar panel:
    Maximum Power: 10 W
    Open Voltage: 22 V
    Short Current: 0.61 A
  Genasun GV-5
    Solar Charge Controller
    MPPT
  Battery:
    Voltage: 12 V
    Charge Current: 7 Ah
Notes: Solar Panel:
Genasun GV-5: It includes a Solar Charge Controller with MPPT. The solar charge controller is a DC-DC converter which will step down the solar panel output voltage to 14.5-14.9 which is Cycle Use voltage needed to fully charge the battery.
Battery:

## Slide 7
Power Module - MPPT Solar Charge Controller
  Battery Charge Controller
    DC-DC converter which will convert the voltage to 14.5-14.9 (Cycle Use Voltage)
Maximum Power Point Tracking
  Calculates the voltage at which the module is able to produce maximum power
  Regulates the current accordingly
  Increases the power production by around 40%

## Slide 8
Power Module – Results
Time to fully charge the battery (Cloudy day): 2.5 hours +/- 0.5 hour
Total consumption:
Time to fully consume the battery power: 4 hours +/- 0.5 hours
Module | Voltage (V) | Current (A) | Power (W)
Dimming Module | 13,2 | 0,8 | 9,6
Charging Module | 13,2 | 2,2 | 6
Tracking Module | 5 | 1 | 5
Total |  |  | 20.6

## Slide 9
Charging Module
Input Voltage
  12V +/- .2v
Phone Charging Required Output:
  Output voltage: 5V +/- .25V
  Output Current: 1A +/- .25V
Desire Operating Points
  Switching Frequency: 200 kHz
  Efficiency: 90%

## Slide 10
Charging Module
  Component Sizing
  Duty Ratio
  Inductor min:
  Capacitor min:
Parts
1x Power Mosfet
  (IRF520A)
1x Power Diode
  (Schottky Barrier Rectifier-
  MBRB1045)
1x High Side Gate Driver
  (IRS2186)
1X Power Resistor
  (15W – 35
1x Micro-Controller
  (MSP430)

## Slide 11
Charging Module
Courtesy of MaximIntegrated

## Slide 12
Charging Module (DC-DC converter)
  Buck Converter close loop Circuit
Close loop path

## Slide 13
Charging Module
  P-Control loop Flow Chart

## Slide 14
Result
Fully Functional Buck Converter on Proto-board

## Slide 15
Result
Gate Driver
Micro-Controller
Resistor Network
Buck Converter on PCB

## Slide 16
Result – No Load
Blue – PWM output
Yellow– Output Gate
Purple – Output Voltage
Green – Input Current

## Slide 17
Result – With Load
Blue – PWM output
Yellow– Output Gate
Purple – Output Voltage
Green – Input Current

## Slide 18
Result
Chart: Charging Module Efficiency (No Load) ƞ (%)
| 0.24780701754385964 | 0.2673913043478261 | 0.34130434782608693 | 0.34042553191489366
ƞ (%) | 0.96308 | 0.92572 | 0.91159 | 0.91325
Chart: Buck Converter Efficiency
| 0.126 | 0.495 | 0.80100000000000005 | 1 | 1.2 | 1.5
ƞ (%) | 0.79116 | 0.78396 | 0.69998 | 0.66784 | 0.63684 | 0.56319
Chart: Charging Module Efficiency (With load) ƞ (%)
| 0.72587719298245612 | 0.73877551020408161 | 0.98494623655913982 | 1.0717391304347825
ƞ (%) | 0.87354 | 0.88226 | 0.85055 | 0.88406

## Slide 19
Lighting Dimmer
Control the light intensity of the LEDs
Using a PWM signal generated by an Analog Timer (LM555)
Light intensity controlled by a Potentiometer adapting the Duty Cycle
Frequency fixed by the 1K (R1) resistor
  Limit frequency for LEDS is 200Hz
  Frequency adjusted from 260 Hz to 320Hz

## Slide 20
Lighting Dimmer – Final Result

## Slide 21
Sun Tracking Module
Purpose: Track the position of the sun using light dependent resistors (LDRs)
As light is shown on the LDR, the resistance drops
This information is sent to the Microcontroller (MSP430) which will position the umbrella towards the most light

## Slide 22
Sun Tracking Setup
Solar Panel
LDRs
S1
S2
S3
S4
S5
S6
S7
S8

## Slide 23
Sun Tracking Circuit Setup

## Slide 24
LDR conditions
Conditions | Resistance (Ω)
No light | 10k
Normal Room conditions | 700
Value that activates the motor | 550

## Slide 25
Flow Chart
Compare all sensors

## Slide 26
Requirements, Verifications and Results For Sun Tracking
Requirements
  Position Umbrella to maximum light
Verifications
  Shine light of different sensors and see if the solar panel moves to the correct location
Results
  Solar panel positioned itself with an accuracy of +/- 2 degrees

## Slide 27
Conclusion
What we learned?
  Building DC-DC converter
  Troubleshooting and finding potential problems
  Developing and soldering PCBs using Eagle CAD
  TEAM WORK!
What to do next time?
  Conduct testing for extended period of time
  Improve PCB layout
  Implement the PID control for Tracker and Buck converter

## Slide 28
Questions?