## Slide 1: Requirements and Verification
ECE445

## Slide 2: What is RV table?
A two-column table with requirements on the left, and verification on the right
A checklist for both modular goals and modular debugging
If all requirements have been verified by your verification for every module, you should have a fully functioning project.

## Slide 3: Requirements
A technical definition of what each and every module in your system block diagram must be able to do
Quantitative (tolerance range)
Thorough and detailed
Driven by project goals
Design requirements ≠ purchase requirements

## Slide 4: Verification
A set of procedures that you will use to verify that a requirement has been met
Equipment
Test procedures
Presentation of results
Explicit

## Slide 5: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.

## Slide 6: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
What is battery voltage?

## Slide 7: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
Do I fail if the output is 3.25V?

## Slide 8: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
Do we miss any requirements? e.g, current draw?

## Slide 9: Bad RV Example
Voltage Regulator
Requirements | Verification
1. Step down battery to 3.3VDC | 1. Take oscilloscope measurements to make sure that voltage output is 3.3V.
How to measure?

## Slide 10: Good RV Example
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0 -300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.

## Slide 11: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Quantitative measurable ranges
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 12: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Very detailed and thorough
requirements
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 13: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Step-by-step procedure
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 14: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Equipment
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 15: Good RV Example
Requirements | Verification
Provide 3.3V +/- 0.5% from a 3.7V-4.2V source Can operate current within 0-300mA Maintain thermal stability below 125°C | 1A. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 2A. Connect the output of the voltage regulator to VDD node in the constant-current test circuit in Figure 3. 2B. Adjust Rs in Figure 3 to deliver at most 300mA to the load, measured by a multimeter. 2C. Measure the output voltage using an oscilloscope, ensuring that the output voltage stays within 5% of 3.3V. 3A. During verification for Requirement 1 and 2, use an IR thermometer to ensure the IC stays below 125°C.
Explicit set-up/configuration
Voltage Regulator
(adapted from SP16 Wireless IntraNetwork)

## Slide 16: Bad RV Example
Personal Rain Detector
Requirements | Verification
Raspberry Pi is functional. Raspberry Pi GPIO pins can produce outputs. Speaker produces sound when powered. Moisture sensor can survive manufacturer-specified weather conditions. | 1A. Provide 5V power to Raspberry Pi. Inspect status lights to ensure it is operating. 2A. Toggle GPIO pins and measure with oscilloscope. 3A. Drive speaker with 9V power supply and listen for sound to ensure it works. 4. Put sensor outside on a rainy day and test that it works after.
It is raining; put on a jacket.

## Slide 17: Bad RV Example
Personal Rain Detector
Requirements | Verification
Raspberry Pi is functional. Raspberry Pi GPIO pins can produce outputs. Speaker produces sound when powered. Moisture sensor can survive manufacturer-specified weather conditions. | 1A. Provide 5V power to Raspberry Pi. Inspect status lights to ensure it is operating. 2A. Toggle GPIO pins and measure with oscilloscope. 3A. Drive speaker with 9V power supply and listen for sound to ensure it works. 4. Put sensor outside on a rainy day and test that it works after.
It is raining; put on a jacket.
ISSUE: Padding your RV table.
Each of these is “guaranteed” by the manufacturer. You aren’t testing any new designs of your own.

## Slide 18
If you have any questions, contact your TA!