## Slide 1: PCB Design Guidelines and Tips

## Slide 2: PCB Design Guidelines and Tips
Every project must have a PCB design.
Think carefully about your project and its PCB design and ask the following questions:
  What will be the function of my PCB?
    Example: acquire data from sensors, control motors and actuators, communicate with a PC or cloud, display information on a screen/LEDs, acquire inputs from keyboard/switches, etc.
  Protype your idea before designing your PCB.
  How much time would be required to design, fabricate, solder, test and redesign the PCB?
  Every PCB board should have a processor
    Typical projects have microcontrollers (ESP, Atmega, STM, PIC, etc).
    Raspberry Pi board okay but needs to interface with your custom PCB that also has a microcontroller
    FPGA board okay but needs to interface with your custom PCB that also has a microcontroller
  Carefully choose PCB components
    Size and soldering leads (through hole pins preferred, surface mounts components okay but we careful)

## Slide 3: Prototyping Stage
Before designing your PCB, test your idea with discreate components and development boards.
Validate the functionality of your design before designing your PCB.
If your first PCB does not work, trouble shoot it (add, remove wires on your PCB) before refabricating.
    Senior design projects, Fall 2022

## Slide 4: Designing your project with custom PCB
    Senior design project #11, Fall 2022
    Final Project Demo
    Motors and Sensors in each drawer
    Custom PCB

## Slide 5: Single PCB board design
    Senior design project #11, Fall 2022
PCB board has the following parts:
  Microcontroller
  Microcontroller programmer (don’t forget it)
  Power regulator circuits
  Sensor (on a separate PCB)
  Motor controller (h-bridge)
  Buttons and LEDs
  Pay attention to the size of the components (print your PCB on a paper)
  Pay attention on the types of surface mounts pads

## Slide 6: Single PCB board design does and don’t
    Senior design project #11, Fall 2022
Voltage regulator – large size which will be easy to solder
Large connectors and wide wires are necessary for large current drives
Microcontroller. Pins are on the side and about 1mm in size which will be easier to solder.
Very small resistors are very difficult to solder. Avoid them
Creative debugging. You can remove (cut) and add wires on your PCB
Do not forget the programming circuit for your microcontroller

## Slide 7: PCB board with Development Board Interface
Main PCB contains many components (sensors, camera, LEDs, buttons).
Main PCB should also contain a microcontroller.
Main PCB has to interface with your development board
  In this example, FPGA dev board from OpalKelly is interface with a custom PCB.
  The development can be used for image processing or more complex signal processing (for example, machine learning algorithms on FPGA such as mobile net.)
ECE437 sensors board
sensors
camera
Connectors
to FPGA
FPGA board
from OpalKelly

## Slide 8: PCB board with Development Board Interface
Main PCB has an interface with Raspberry PI and display monitor (left image).
You can use Raspberry PI with camera (right image) but you will need a main PCB that interface with the Raspberry PI and has microcontroller.
Main PCB contains many components (sensors, camera, LEDs, buttons).
Main PCB should also contain a microcontroller.
arducam.com
researchgate.com