## Slide 1: PCB Design Guidelines and Tips

## Slide 2: PCB Design Guidelines and Tips
Every project must have a custom PCB
Think carefully about your project and its PCB design and ask the following questions:
  What will be the function of my PCB?
    Example: acquire data from sensors, control motors and actuators, communicate with a PC or cloud, display information on a screen/LEDs, acquire inputs from keyboard/switches, etc.
  Prototype your idea before designing your PCB.
  How much time would be required to design, fabricate, solder, test and redesign the PCB?
    This course orders PCBs in waves
    It takes about 7-10 days to go from PCB wave deadline to delivery
  Every PCB should have a processor
    Typical projects have microcontrollers (ESP, ATmega, STM, etc).
    Raspberry Pi board okay but needs to interface with your custom PCB that also has a microcontroller
    FPGA board okay but needs to interface with your custom PCB that also has a microcontroller
  Carefully choose PCB components
    Size and soldering leads (through hole pins preferred, surface mounts components okay but we careful)

## Slide 3: Prototyping Stage
Before designing your PCB, test your idea with discrete components and development boards.
Validate the functionality of your design before designing your PCB.
If your first PCB does not work, trouble shoot it (add, remove wires on your PCB) before refabricating.
Senior design projects, Fall 2022

## Slide 4: Designing your project with a custom PCB
Senior design project #11, Fall 2022
Final Project Demo
Motors and Sensors in each drawer
Custom PCB

## Slide 5: PCB Design
Senior design project #11, Fall 2022
PCB board has the following parts:
  Microcontroller
  Microcontroller programmer (don’t forget it)
  Power regulator circuits
  Sensor (on a separate PCB)
  Motor controller (h-bridge)
  Buttons and LEDs
  Pay attention to the size of the components (print your PCB on a paper)
  Pay attention on the types of surface mounts pads

## Slide 6: PCB Design: Do’s and Don’ts
Senior design project #11, Fall 2022
Voltage regulator – large size which will be easy to solder
Large connectors and wide wires are necessary for large current drives
Microcontroller. Pins are on the side and about 1mm in size which will be easier to solder.
Very small resistors are very difficult to solder. Avoid them
Creative debugging. You can remove (cut) and add wires on your PCB
Do not forget the programming circuit for your microcontroller

## Slide 7: PCB Design: Common IC Packages
wikipedia.com
pcbway.com
ti.com
Quad Flat No-lead (QFN)
Quad Flat Package (QFP)
Ball Grid Arary (BGA)
Easy to solder
Joints are inspectable
Easy to fix bridging with flux and wick
Stencil required for soldering
Joints are difficult or impossible to inspect
Hard to fix mistakes
Thin, electropolished stencil required for soldering
Impossible to inspect joints

## Slide 8: PCB Design: Other IC Packages
There are many kinds of IC packages available
When you import a footprint into KiCAD, compare it to a part you know the size of (like your microcontroller)
Print out your PCB design to get a sense of component size

## Slide 9: PCB Design: Poor IC Package Choice
Example: DRV8837 H-Bridge
Plastic Outline No-lead Package (WSON)
Part is 2.1 mm x 2.1 mm!
Lead pitch is 0.5 mm!
Leads under package made debugging very difficult

## Slide 10: PCB Design: Passive Component Packages
https://weatherhelge.wordpress.com/smd/
https://passive-components.eu
Can you guess what the problem with this is?
Passive components like resistors, low value capacitors, and low value inductors are packages as small rectangular prisms with metal ends
0805 Imperial is usually a good size
You can use larger sizes for shunt resistors and bulk capacitance
Don’t try to use anything smaller than 0603 Imperial
Remember to order extra!

## Slide 11: Any questions so far?

## Slide 12: Processor Policy
Microcontroller ICs and modules are permitted
Development boards are not allowed*
Single board computers (e.g. Raspberry Pi, Nvidia Jetson, etc.) are allowed under certain circumstances

## Slide 13: Processor Policy: Single-board Computers
You may use a Raspberry Pi as a secondary processing unit
Operating a camera and handling image processing loads is a popular task for single-board computers
Your custom PCB must still contain a microcontroller along with the rest of your circuit
arducam.com
A PCB acting as a “Pi Hat”
This is a good way of interfacing a custom PCB with a Raspberry Pi

## Slide 14: Processor Policy: Development Board
Main PCB contains many components (sensors, camera, LEDs, buttons).
Main PCB should also contain a microcontroller
Main PCB has to interface with your development board
  In this example, FPGA dev board from OpalKelly is interface with a custom PCB.
  The development can be used for image processing or more complex signal processing (for example, machine learning algorithms on FPGA such as mobile net.)
ECE437 sensors board
sensors
camera
Connectors
to FPGA
FPGA board
from OpalKelly

## Slide 15: Design Resources
The ECE 445 wiki has example projects available for microcontrollers kept in stock by the electronics service shop
ATMega
STM32
ESP32

## Slide 16
The wiki contains information on:
  Regulator selection
  Connectors
  Importing parts into KiCAD
  Microcontroller programming

## Slide 17: Getting Parts: Senior Design Lab
You may borrow development boards, programmers, autotransformers, sensors, etc. from the white cabinets
These items should be returned at the end of the semester
Any TA can check out parts to a student

## Slide 18: Getting Parts: Supply Center and E-Shop
ECE Supply Center
Near the loading dock
Stocks through-hole components, project boxes, sensors, etc.
Not free
Electronic Services Shop
Near the north exit to Wright Street
Stocks connectors, potentiometers, through-hole components, etc.
Also stocks surface-mount components deliverable by your TA
Surface mount components include microcontrollers, passive components, and oscillators

## Slide 19: Getting Parts: my.ECE Ordering
You may use your budget of $50 per student to order parts from Digikey, Mouser, etc. through the business office
A CFOP number for this course will be shared shortly
Note that Digikey is short staffed at the moment so they are slow to send out orders
During the middle of the semester, orders may take many days to be placed

## Slide 21: Clean Your Lab Bench! (Radar Enforced)
Please keep the lab benches and the soldering stations clean
When you finish working:
  Remove any bits of solder, wick, or wire clippings on the table
  Turn off equipment (e.g. soldering irons, extraction fans)
Untangle cables that tie tools down
Wind up unspooled solder and wick
We will have to shut down the lab if it gets too messy

## Slide 22: Any questions?