## Slide 1
Zhejiang University-University of Illinois Urbana Champaign Institute
A DODGEBOT SYSTEM
Team 27
Chiming Ni
Feiyang Wu
Kai Wang
Nichen Tian
Yiyang Bao
May 25, 2025
Final Presentation

## Slide 2
Content
Introduction
Mechanical Design
Software Design
Conclusion

## Slide 3: Part 1: Introduction

## Slide 4
Introduction
Background and problem statement:
Dodgeball is a high-intensity sport that demands sharp reflexes, pinpoint targeting, and agile evasion, yet traditional training relies on human partners for throwing and dodging drills—posing challenges for athletes who want consistent solo practice; meanwhile, current automated launchers borrowed from sports like tennis or baseball lack the adaptability, precision, and interactive responsiveness needed to replicate realistic dodgeball scenarios, underscoring the need for a more advanced, adaptive, and interactive training system.

## Slide 5
Work Demonstration
A short video to show our work

## Slide 6: Part 2: Mechanical Design

## Slide 7
Mechanical Design
Overview:
Goal:
Enable rapid-response, high-precision launching while gimbal is moving.
Structure:
Dual-Axis Gimbal
Friction-Wheel Launch & Feed
Sensors& Motors

## Slide 8
Mechanical Design
Structural Design:
Yaw Assembly:
Three-plate stack; hard stop prevents cable twist
yaw axis front view
yaw axis structure
yaw axis structure

## Slide 9
Mechanical Design
Structural Design:
Pitch Assembly:
Clamping plates + thrust bearings; 30 ° elevation
pitch axis structure
pitch axis structure

## Slide 10
Mechanical Design
Structural Design:
Ammo Container & Feeder:
Multi-ball rotating disc; pushes balls into inlet. Light weight PLA+ topology structure
head connection structure
ball feeder- block plate
ball feeder arm, a pusher

## Slide 11
Mechanical Design
Launcher:
Launcher Barrels
squeezes 72 mm Wiffle ball into 68.216 mm wheel spacing inlet to gain more friction power
Hit-Stop Board
4 mm PLA plate + microswitch → immediate emergency stop
motor holder and the barrel structure
hit-stop board structure

## Slide 12
Mechanical Design
Motor Selection:
Torque Required due to Friction or Gravity
  Yaw: ≥ 2 N·m peak (1.5 – 2 kg head)
  Pitch: gravity torque dominates → ≥ 2.34 N·m required
Selected motors satisfy margins:
  M3508 (3 N·m cont.) for wheels & feeder
  DM-J6006 (9 N·m cont.) for gimbal axes
Anti-Jamming:
  Feeder reliability reached 100 % after 5 iterations

## Slide 13
Overview in Work of DodgeBot Launcher
  Focus: High-performance launcher subsystem for autonomous dodgeball robot
  Replaced pneumatic prototype with friction-wheel mechanism.
  Modeled major structures: barrel, dial shell, connectors, motor base, yaw/pitch interfaces.
  Core focus: effect of wheel spacing on launch speed – identified optimal spacing (68.216 mm).
Mechanical Design

## Slide 14
First version of Dodgebot system
The compressed air version of Dodgebot
Mechanical Design

## Slide 15
The final version of Dodgebot
Mechanical Design

## Slide 16
Mechanical Design & Optimization
Created all launcher components using Fusion 360:
  Friction wheel mounts, motor base, rotatable yaw support, modular shell
Introduced metal slip ring for improved yaw axis stability
Converted dial shell into a fully modular structure
Mechanical Design

## Slide 17
The adjustable distance motor base of Dodgebot
The Dial Plate Loading System of Dodgebot
Mechanical Design

## Slide 18
The Rotatable base of Dodgebot
Dodgeball launcher
Mechanical Design

## Slide 19
Prototyping and Assembly
Coordinated laser cutting and 3D printing of mechanical parts
Procured fasteners, M3508 motors, and fabricated components
Built adjustable motor base for wheel spacing tests
Finalized prototype with detachable electronics tray
Mechanical Design

## Slide 20
Install the prototype machine
Mechanical Design

## Slide 21
Final demo of Dodgeball system
Mechanical Design

## Slide 22
Experimental Validation
Executed spacing vs. velocity tests using 300+ shots
Analyzed results using regression, ANOVA, RSM
Found 68.216 mm as optimal spacing (peak ~7.42 m/s)
Confirmed spacing effect through confidence interval analysis
Mechanical Design

## Slide 23
Ball trajectory under high speed lens
Huge Recoil form Too Narrow IWD
Mechanical Design

## Slide 24
Launch Velocity vs. Inter-Wheel Distance
Model Fitting Comparision by Motor Speed
Mechanical Design

## Slide 25
The final regression equation for launch velocity is:
Where:
: Launch velocity (m/s)
: Inter-wheel distance (mm)
: Motor speed (rad/s)
Mechanical Design

## Slide 26
Key Takeaways and Impact
Designed, validated, and optimized a modular launcher for DodgeBot
Solved issues in pneumatic actuation, torque shortage, and inconsistency
Laid foundation for adaptive sports robotics and scalable projectile systems
Methodology and findings generalizable to other robotic platforms
Mechanical Design

## Slide 27: Part 3: Software Design

## Slide 28
Software Design
Why ROS2?
ROS2 (Robot Operating System 2) is an open-source robotics middleware that provides tools, libraries, and frameworks for building complex, real-world robotic systems. ROS2 uses Data Distribution Service (DDS) as its default middleware for reliable, low-latency, and scalable messaging.
Why ROS2-Control?
Hardware Abstraction. Encapsulate hardware and controllers by exporting interfaces to use.
Compatibility: Compatible with ROS2 programs.
Faster Transmissions. Information passing though reference and command interfaces are much faster than ros2 topic transmission.
Realtime Capability. Designed with real-time control in mind, making it suitable for high-performance robotic applications.
Built in Controllers. Default PID controllers to use.

## Slide 29
Software Design
Design Overview
Perception Layer:
Robot perception related components, including cameras and hit detection.
Decision Layer:
Policy decision of the robot. Include game logic and computer vision related code. It sends out command to the execution layer.
Execution Layer:
Drivers and hardware interfaces for ros2-control.
Decomposition Layer:
Other non ros2-control components.

## Slide 30
Execution Layer & Decomposition Layer
Peak-CAN system can be inserted into the computer with USB port. All 5 motors are controlled by CAN.
CH340 serial to USB convertor can help computer read the serial communication information from Wfly remote control.
Software Design

## Slide 31
Execution Layer-Controller Design
Damiao motor MIT mode controller
Software Design

## Slide 32
Execution Layer-Controller Design
M3508 position-to-velocity, velocity-to-effort cascaded PID controller
Software Design

## Slide 33
Perception Layer
Dodgebot IO
Armor switch connect to pin 7 with a pull up resistor.
Realsense D435 Depth Camera
Run on 60 fps, 640x480 resolution.
Infrared depth image stream enabled.
Software Design

## Slide 34
Robot
Enable/Disable
Friction Wheel
& Loader Enable/Disable
Reset
Easy Mode
Hard Mode
Vision
Enable/Disable
Robot
Yaw
Robot
Pitch
Decision Layer: Gaming Logic
Software Design

## Slide 35
Decision Layer: Gaming Logic Flow Chart
Software Design

## Slide 36
Dodgebot Electrical System
Power Supply (AC2DC)
Main Chassis Board
24V 5A
Gimbal Board
Yaw Motor (DM6006)
Edge Computing Platform
CAN
24V 5A
Pitch Motor (DM6006)
Friction Wheel Motors x2 (DJI M3508)
Feed Motor (DJI M3508)
24V
24V
CAN
24V
CAN
24V
CAN
Camera Module (RealSense)
USB 3.0
CAN
CAN
24V
Software Design

## Slide 37
PCB Layout
Chassis Board
Gimbal Board
Software Design

## Slide 38
Dodgebot Vision System (original idea)
person
YOLO11-POSE
3D Coordinates
from RealSense
Kalman Filter & Simple Tracker
3D Coordinates
but more stable and tracks only one target
Projectile Angular Solver
Downstream Motor Controllers
Yaw Pitch
This idea doesn’t work well.
Potentially because RealSense cannot provide reliable depth info. Anyway, our final version is much simpler.
Software Design

## Slide 39
Dodgebot Vision System (final ver.)
person
YOLO11-POSE
Core Algorithm: PID Feedback based on YOLO
Goal: Rotate the gimbal such that matches
will adapt with distance of human measured from RealSense.
Goal: Aim higher when the person is standing further away.
Very simplified tracking: Only track the target closest to the image center.
Software Design

## Slide 40
Center Coordinate Adaptation
The adaptation of is implemented as follows
Software Design

## Slide 41
Human Tracking Algorithm
YOLO11-POSE
We track the head of a human:
Head is the most visible feature of human.
Dodgebot aims higher than human head (most people stand far from the device).
Head is (probably) the only visible feature of human.
Safety considerations:
Unless a person is standing very close to the robot (below ~2m), the dodge ball will never hit on any critical human organs.
*: This result may vary depending on shoot velocity.
person
Software Design

## Slide 42
Human Tracking Algorithm (in practice)
Software Design
right eye
left eye
nose
target center

## Slide 43
The magic behind high-speed inference
Jetson Orin Nano is a low-power platform
Relatively Low Performance
Writing high-performance inference software is required.
Triple buffering synchronization
Applied extensive optimization tricks to gain full performance advantage.
This software stack can reach up to 210 FPS running YOLO11n. For our case, the RealSense camera only captures image in 60 FPS, the performance is quite sufficient.
List of optimization tricks used:
TensorRT with FP16
GPU Postprocessing (with custom hand-written CUDA kernels)
GPU Preprocessing (with NPP library from CUDA)
CUDA Graph and Stream
Software Design

## Slide 44
Software Design
Our method is the best among all three implementations
Baseline Zero-Copy (Simple single-threaded while loop)
ROS2 Topic (Networking-based)
Triple Buffering (Our Method)
The result is stable across different models and camera FPS
The Power of Triple Buffering

## Slide 45: Part 4: Conclusion

## Slide 46
Conclusion
Project Recap & Scope:
Goal: build an affordable, autonomous training partner that launches dodge-balls with game-like realism and adapts to athlete movement.
Prototype Delivered:
  2-DoF gimbal + friction-wheel shooter
  YOLO-based vision stack on Jetson Orin Nano
  Closed-loop accuracy demoed in-lab
Focus of this section: accomplishments, safety framework, and the shelved active-dodging feature.

## Slide 47
Conclusion
Safety Architecture & Next-Step Roadmap:
Built-in Protections
Hardcoded speed limiter.
Remote-controlled launch enable; mechanical guards on gimbal.
Future Work: Re-introducing Active Dodging
Mobility platform: omni-wheel base ≥ 7 m s⁻¹ with torsion suspension.
Incoming-ball perception: 240 FPS global-shutter cam
Evasion planning: MPC seeded by neural flight-time predictor → 0.4 m sidestep in 250 ms.

## Slide 48
Thank you!