## Slide 1
ECE 470/ME 445 Presentation
Team 21 Continuous Vehicles Capture
Team Member
Yining Guo| Binyang Shen | Jiawei Zhang | Zijin Li

## Slide 2
Introduction
A portable traffic monitoring system powered by Raspberry Pi for real-time vehicle detection
Utilizes computer vision and YOLO neural networks to identify and classify vehicles
Captures traffic flow data and provides real-time analysis
Delivers interactive web dashboard with live statistics, charts, and customizable traffic alerts
Notes: introduce our system first.
We have built a real-time traffic monitoring system based on the raspberry Pi.
It detect and classify different types of vehicles - cars, trucks, and buses.
The system captures traffic flow data and provides real-time analysis of vehicle density and traffic patterns.
Finally, we use a visualization dashboard to dynamically display all the data.

## Slide 3
System Overview
Three Core Subsystems
Mechanical - Power & Protection
Image Processing - Detection & Analysis
Visualization - Web Dashboard & Alerts
Notes: let's look at how the system works. The architecture consists of three core subsystems working together:
First, the Mechanical subsystem provides power supply and protective housing for the hardware components.
The Image Processing subsystem receives video streams from the camera module, performs operations, and then sends JSON data to the visualization subsystem.

## Slide 4
High-level Requirements
Accuracy: Vehicle detection and counting accuracy should be ≥ 90%.
Real-time performance: The system should be capable of near real-time video anal ysis and rapid data visualization.
Robustness: The system should operate reliably under different weather, light, and traffic flow conditions.
Early warning effectiveness: The system should effectively identify and warn of congestion status, assisting traffic management decisions.
User-friendly interface: The visualization dashboard should be intuitive and easy to use for relevant personnel.
Compatibility: The system should be compatible with common traffic management software and hardware
Notes: For our high-level requirements: Accuracy is important - we initially targeted 90% or better vehicle detection accuracy. And the system must perform near real-time video analysis with rapid data visualization. Also, to support outdoor deployment, it needs to operate reliably under various weather and traffic conditions. The system should identify congestion and provide alerts, and maintain an intuitive and concise user interface.

## Slide 5
🚗 Parts sizes
 | Raspberry Pi | Camera Base | Battery | Camera
Length(mm) | 82.5 | 64 | 133 | 25
Width(mm) | 55 | 59 | 68 | 24
Height(mm) | 25 | 42 |  | 

## Slide 6
🚗 Device Housing size

## Slide 7
🚗 Design Details
Incorporate rubber strips in the grooves
Using screws to hold the two parts together
Ensure the Sealability of the Device
Notes: In order to ensure the sealing of the whole device, I added two structures in the design process. The first one is the groove on the side, where we can ensure a seal by stuffing it with rubber strips. The second one is a screw hole. Considering that the whole unit will last for a long time, we are not going to use strong adhesive to bond the two parts, but rather use screws for the combination.

## Slide 8
🚗 Design Details
Rainproof design
Prevent rainwater from the shortfall for the camera
Notes: Where the camera is placed, taking a page from the canopy design, I added an extra rain stopper.

## Slide 9
🚗 Concrete Figure

## Slide 10
🚗 DC power supply
Get power directly from the mobile device
Get power from the battery
Notes: One of the power supply methods is to directly connect the whole Raspberry Pi to a mobile device with a USB port and power it through the mobile device. However, the internal operating voltage of the Raspberry Pi is 5V; therefore, we have included a step-down converter (buck module) from high voltage to 5V (LM2596S module) in the circuit to ensure a stable output of 5V over a wide input range.
The LM2596 is a buck switching regulator, which achieves voltage conversion through high-frequency switching (PWM control) and inductor energy storage: when the internal switch is on, the input voltage supplies power to the inductor and the load, and the inductor stores energy; when the switch is off, the inductor releases energy through the continuity diode to maintain the output.
To prevent service interruption in case of primary power failure, a rechargeable Li-ion battery backup system was integrated. The system uses a Li-ion battery pack (rechargeable) supporting >2 hours of system uptime during power failure. A DC-DC buck converter regulates battery output to consistent 5V input for the Raspberry Pi.

## Slide 11
The power of charging: 20 W
Assume the maximum time for charging is 24 hours per day
Total energy:
Assume the efficiency of converting heat to electricity is 20%
Total heat needed:
Assume sun peak hour is 4 hours,
We can get
🚗 Energy Calculation for PV panels

## Slide 12
🚗 Introduction of Image Processing module
Notes: Now, I will be introducing our Vehicle Detection and Tracking system.
The Image Process module aims to develop an efficient and accurate system for vehicle detection and tracking.
It leverages the YOLO model for real-time detection of various vehicles such as cars, trucks, and buses, and uses a Kalman filter-based algorithm for multi-target tracking.
The system can automatically classify different vehicle types, record their movement trajectories, and generate annotated videos with bounding boxes and IDs for visualization.

## Slide 13
🚗 Flowchart of the image processing module (Block diagram)
Notes: 1. The process starts with the video source, where we first acquire the video feed, either from a video file or a live camera, to prepare it for further processing.
2. Next, we extract each frame from the video, performing frame acquisition, and apply preprocessing steps. After preprocessing, YOLO detects vehicles in real-time, marking them with bounding boxes. To ensure accuracy, we focus only on relevant vehicle class labels such as cars, buses, and trucks.
3. Once the vehicles are detected, the system moves on to tracking. We use a Kalman filtering algorithm to track each detected vehicle, assigning a unique ID to each and recording their movement trajectory over time. This allows us to continuously track the location and movement of each vehicle in subsequent frames.
4.1 After tracking, the system visualizes the detection and tracking results. We draw bounding boxes around the vehicles, display their trajectories, and overlay ID and class labels to ensure that the movement and classification of each vehicle are clearly visible. This visualization allows users to see the movement path and classification of each vehicle in real-time.
4.2 Additionally, the system processes and analyzes the detection and tracking data, counts the vehicles, and stores the information in JSON format for future analysis or data export.
5. Finally, the processed video frames can either be saved as an output video or displayed in real-time, depending on the configuration.

## Slide 14
🚗 R & V and Quantitative Results
Notes: We demonstrate the system's effectiveness through three validation aspects:
Vehicle Classification Accuracy
Vehicle Tracking & ID Consistency
Accuracy Comparison with the MOT17 Dataset
First, we validated the vehicle classification accuracy. We tested the system on vehicle types from the MOT17 dataset, including Car, Truck, and Bus. The goal was to check whether the system could classify them with an accuracy of over 80%.
Our method:
We used video sequences from the dataset to perform classification tests, ensuring the classification accuracy exceeded 80%.
The results show that the system's classification accuracy for Car and Bus was 85% and 84.9%, and Truck achieved 81.5%, all slightly above the 80% threshold.
Next, we validated the vehicle tracking & ID consistency. We tested the system on 5 video sequences from the MOT17 dataset, evaluating whether it could correctly track targets and maintain 90% ID consistency across different sequences.
Validation method:
We performed target tracking on the video sequences from the dataset, ensuring that ID consistency remained above 90%.
The results show that the system's ID consistency exceeded 90% in all video sequences, meeting our predefined standard.
Finally, we validated the system by performing an accuracy comparison with the MOT17 dataset. We compared the system's accuracy across different video sequences with the annotations in the dataset.
Validation method:
We calculated the detection accuracy for each video sequence from the MOT17 dataset, comparing the results with the MOT17 annotations.
The results showed that the system's accuracy for the 5 video sequences was 86.5%, 87.2%, 85.9%, 86.7%, and 87.4%, all slightly exceeding the required 85%, demonstrating stable performance in real-world applications.

## Slide 15
Green = real-time detection Orange = Kalman prediction
🚗 Output of the image processing module
Notes: The Kalman filter helps maintain consistent vehicle IDs by continuously predicting movement trajectories. When a vehicle is temporarily undetected (e.g., due to occlusion), the algorithm predicts its current position based on previous motion patterns. Upon reappearance, the system matches new detections with predicted trajectories using the Hungarian algorithm to find optimal associations. This prediction-matching mechanism ensures the same vehicle retains its ID across frames, significantly reducing ID switching issues and maintaining tracking continuity even during brief disappearrances from the surveillance area.
卡尔曼滤波器通过连续预测运动轨迹来帮助保持一致的车辆id。当车辆暂时未被检测到时（例如，由于遮挡），该算法根据之前的运动模式预测其当前位置。在重新出现时，系统使用匈牙利算法将新检测与预测轨迹相匹配，以找到最佳关联。这种预测匹配机制确保同一车辆跨帧保留其ID，显着减少ID切换问题，即使在监视区域短暂消失期间也保持跟踪连续性。

## Slide 16
Data visualization

## Slide 17
Implement of Yolov5 on Raspberry-Pi
Method1: Multi-threads
Main start
prepare model/ initialize threads
CSI Camera capture frames
Select frames for capturing
recognition
Output
queue
Queue back to original sequence
Write to the generated video
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 18
Implement of Yolov5 on Raspberry-Pi
Method1: Multi-threads
Thread FrameCaptureThread(fps, record_output, show_window):
(Initialize camera, local variables)
while not stop_event.is_set():
(frame capture, frame counting)
-if frame_count % DETECT_EVERY_N == 0:
(queue for current frame)
-with result_lock:
(success box and drawing)
-if record_output or show_window:
(try to queue for additional box drawing frame)
-sleep(1 / fps)
(release and close thread)
Thread DetectionThread(model, confidence_threshold):
while not stop_event.is_set():
frame = frame_queue.get
detections = model.detect
boxes = filter_vehicle_boxes(detections)
-with result_lock:
(update the detection boxes)
Thread WriterThread(output_path, fps):
video_writer = init_video_writer
while not (stop_event.is_set() and write_queue.empty()):
frame = write_queue.get
video_writer.write(frame)
video_writer.release()
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 19
Implement of Yolov5 on Raspberry-Pi
Method2: Multi-process
Method Overview: Compared with previous Multi-threads methods or other technical improvements in
Coding, multi-process method is much more robust, it fully utilize the computation resources of the Ras-
pberry-Pi, with 93% of CPU usage and more accurate detection box onlocking, we choose this implement
as final platform of our system.
Main start
Camera frame capture
Queue for all frame
Activate 4-process
(Process all selected frame)
requeue
output
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 20
Implement of Yolov5 on Raspberry-Pi
Method2: Multi-process
FUNCTION process_frame(event, model, in_queue, out_queue):
while not event.is_set():
(queue=>detection=>annotate=>output in queue)
log("process_frame exiting")
FUNCTION video_writer(event, output_path, fps, size, write_queue):
, fps, size)
while not event.is_set():writer = VideoWriter(output_path
(write frame based on queue)
writer.release()
MAIN FUNCTION main():
(model initialize, queue initialize)
event = new Event()
in_queue = Queue(maxsize=4)
result_queue = Queue()
write_queue = Queue(maxsize=10)
// Start writer process
writer_proc = start_process(video_writer, args=(event, "output.mp4", fps, CAPTURE_SIZE, write_queue))
// Start multiple detection workers
workers = []
for i in 1->4:
(starting recognition process, append work)
release
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 21
Visualization
Detection result for current frame
Accumulated counting results plot
Accumulated data flow
Occupation visualization
Current target information
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 22
Visualization
// Type Definitions (Vehicle type, History point, Distribution data)
// Main Dashboard Routine
// 1. State Initialization
(initialize connection_status, Vehicle, Historypoint, DistributionDatum)
// 2. Open WebSocket Connection
(establish connection from seudo backend or real raspberry-pi input)
// 3. Compute Derived Statistics
(totalCars, totalTrucks, totalBuses, totalVehicles)
// 4. Determine Connection Icon
(update statusIcon & statusText based on connection condition)
// 5. Render UI
(Header: title, icon, text;
Stats Cards Grid: 4 types of vehicles;
Active Vehicles Section: each vehicle information;
Charts Section: x,y-axis, pie-chart;
Accumulated dataflow Table: latest 7 entries)
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 23
Data transfer
Backend:
1 Real-time WebSocket channel
Added a websockets server and a push() broadcaster; Launch the websocket server on raspberry-Pi’s
ip and exposed its event loop for downstream pushes.
2 Richer payload
Switched from simple frame calls to model.track() to preserve object IDs; Built a vehicle list of {id, type}
maintained cumulative counts, a time-series and a distribution summary for pie charts.
3 Broadcast logic
Every inference invocation packs {vehicle, history, distribution} into JSON and push() it immediately
over the open websocket.
4 Performance tuning
Ensured the raspberry-pi’s limited resources and network constraints still yield a smooth data stream.
Summary:
The backend now performs “detect → aggregate → broadcast,” feeding live JSON data to any websocket client.
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 24
Data transfer
Frontend:
1 WebSocket URL
Change from localhost to raspberry-pi’s id for dataflow endpoint matching.
2 React robustness
Update key={vehicle.id} to key={${vehicle.id}-${idx}} to avoid duplicate key warnings when ID collide or
the history is not cleared.
Summary:
The dashboard now connects seamlessly to the Pi over local network connection, renders dynamic vehicle cards,
real-time line charts, and distribution pies—all updating live.
Notes: (插图：两天曲线对齐图，突出误差时段)

## Slide 25
Thank you