## Slide 1
浙江大学伊利诺伊大学厄巴纳香槟校区联合学院
Zhejiang University-University of Illinois Urbana Champaign Institute
The Smart Fitness Coach Team #11
Yuxuan Lin (yuxuan42@illinois.edu) Xingyu Li (xingyul6@illinois.edu) Lishan Shi (lishans3@illinois.edu) May 25, 2025
Sponsor: Bruce Xinbo Yu
TA: Xiaoai Wang

## Slide 2
1.Introduction
Contents
2.Objectives
3.Design, Build & Tests
4.Successes and challenges
5.Future Development
Notes: So we will break into 5 sections to introduce our project

## Slide 3
1
Introduction

## Slide 4
Introduction
Background: Rising public interest in fitness and home workouts
Existing solutions rely on: • Wearable sensors (intrusive, uncomfortable) • Video tutorials (passive, no feedback)
Project Concept:
A camera-based, real-time exercise tracking system • No wearables needed • Provides live feedback • Enables interactive training without supervision
Notes: Background: With the growing attention to fitness, the demand for convenient and interactive fitness equipment is increasing. Existing products are based on either intrusive attachment sensors or passive video tutorials, which have certain limitations.
Project Concept:
Introduce the concept of the Smart Fitness Coach, which uses a camera for real-time motion tracking and feedback without the need for wearable devices or human supervision.

## Slide 5
2
Objectives

## Slide 6
Objective
Overall Objective:
An AIoT-based real-time motion tracking system that provides an affordable, portable, and intelligent fitness guidance solution.
Real-time Movement Detection Accurately detect and classify common fitness movements (e.g., squats, push-ups) in real time.
Timely Feedback Provide visual feedback and servo responses within 1 second of detecting incorrect posture or user commands.
Dual Video Source Support Support both local camera and ESP32-CAM, ensuring stable Wi-Fi within 5 meters.
Notes: Overall Objective: To design and implement an AIoT-based real-time motion tracking system that provides an affordable, portable, and intelligent fitness guidance solution for home fitness users. Specific Objectives: Achieve real-time and accurate detection and classification of common fitness movements such as squats and push-ups, with an accuracy of at least 90 %. Provide visual feedback and servo responses within 1 second after detecting incorrect postures or user commands to ensure a smooth user experience. Support both local and ESP32-CAM video sources and maintain stable Wi-Fi connectivity within 5 meters of a standard router. The mobile frontend should provide essential control features, including start/stop buttons, session reset, and real-time feedback, and properly handle camera permission status. Automatically count valid exercise repetitions during each session and notify the user via the UI, resetting the count at the start of each session. Record each workout's type, duration, and repetition count, and display this history in an accessible format. Generate personalized training advice based on historical performance data and suggest changes in training strategies in three categories: increase, maintain, or balance. The advice should be presented in user-friendly JSON or natural text form.

## Slide 7
Objective
Mobile Frontend Features Include start/stop, session reset, and real-time feedback; properly handle camera permissions.
Repetition Counting Automatically count valid repetitions per session; reset count at session start and display results in UI.
Workout Logging Record exercise type, duration, and repetition count; present history in a clear and accessible format.
Personalized Training Advice Generate advice based on historical data, suggesting to increase, maintain, or balance training. Display advice in user-friendly format.
Notes: The mobile frontend should provide essential control features, including start/stop buttons, session reset, and real-time feedback, and properly handle camera permission status. Automatically count valid exercise repetitions during each session and notify the user via the UI, resetting the count at the start of each session. Record each workout's type, duration, and repetition count, and display this history in an accessible format. Generate personalized training advice based on historical performance data and suggest changes in training strategies in three categories: increase, maintain, or balance. The advice should be presented in user-friendly JSON or natural text form.

## Slide 8
3
Design, Build & Tests

## Slide 9
System Overview
Power Supply
Control Unit
Angle Regulator
Camera
Software
Review of Original Design
Notes: System Architecture: Present a system architecture diagram showing the interaction between hardware and software components. Hardware Design: Power Supply: Uses USB-Mini input and a low-dropout linear regulator (LDO) to provide a stable 5 V output. Control Unit: Centers on the AI-M61-32S microcontroller, which is responsible for coordinating component operations and executing application-level logic. Angle Regulator: Utilizes two SG90 servo motors, controlled by PWM signals, to achieve precise angular positioning. Camera: An installed RGB camera captures users' movements during workouts. Software Design: Describe the shift from embedded local inference to a cloud-assisted modular architecture, explain the comparison and selection of YOLO and MediaPipe, and introduce the development frameworks and communication methods of the front-end and back-end.

## Slide 10
Power Supply
Power bank
Send stable current to voltage regulator
Voltage regulator
Provide stable 3.3V voltage to other module

## Slide 11
Control Unit & Camera
Use AI-M61-32S as microcontroller to control
Camera
Capture user's posture
Wi-Fi
Send video stream through HTTP
Angle regulator
Adjust the angle of the smart fitness coach to ensure the user is in the screen
Light
Light the scene if the environment is dim
Camera
OV2640
CSI interface
Notes: Connect the OV2640 to the CSI interface to provide video stream

## Slide 12
Angle Regulator & Light
Angle Regulator
Two servo motor
Light
LED
Notes: Sliding the slider, we can adjust the direction and light amount of smart fitness coach, ensuring the user is well-seen in the screen.

## Slide 13
Angle Regulator
Two servo motor
Light
LED
Quick Validation through HTTP: 1. Send commands to http://<ip>/servo?pan=...&tilt=... and visually verify servo angles
2. Send commands to http://<ip>/light?value=... and visually verify light condition
Angle Regulator & Light

## Slide 14
Physical Components
One part is the top, the other is the bottom.
The shell is modeled with SolidWorks and made by 3D printing.
Top​ component
Bottom component
Notes: There is a square window on the top component, allowing the camera to capture the posture while protecting other component on the bottom component, there is a circular window, allowing the servo to adjust the angle unlimitedly.

## Slide 15
Project Build – Hardware Construction
Hardware Cost Control: Actual cost expenditure of hardware costs, emphasizing the strategy of reducing costs through simplified design.

## Slide 16
Project Build – Software Implementation
Software Development
Back-end: Flask server handles video input and pose estimation
Model: Integrated MediaPipe for real-time posture tracking
Front-end: Built with Vue 3 and UniApp for cross-platform UI
AI Suggestion: Send historical data to Deepseek API
Notes: So here’s a quick look at our software setup. On the back-end, we’re running a Flask server that takes in video and runs pose estimation using MediaPipe. The front-end is built with Vue 3 and UniApp, which lets us build a clean and responsive UI across devices. And for smart suggestions, we send users’ workout history to the Deepseek API to get personalized fitness tips based on their past sessions.

## Slide 17
Project Build – Software Implementation
Software Development
Back-end: Flask server handles video input and pose estimation
Model: Integrated MediaPipe for real-time posture tracking
Front-end: Built with Vue 3 and UniApp for cross-platform UI
AI Suggestion: Send historical data to Deepseek API
Notes: So here’s a quick look at our software setup. On the back-end, we’re running a Flask server that takes in video and runs pose estimation using MediaPipe. The front-end is built with Vue 3 and UniApp, which lets us build a clean and responsive UI across devices. And for smart suggestions, we send users’ workout history to the Deepseek API to get personalized fitness tips based on their past sessions.

## Slide 18
Project Build – Software Implementation
Notes: Here you can see how we handle camera permissions and switching. On the left, the app clearly asks the user for camera access, explaining that it’s only used for pose recognition and no data is stored. Once permission is granted, the interface on the right lets users choose between multiple local cameras, or even network cameras like the ESP32-CAM. This gives users flexibility and makes the system compatible with different devices and setups.

## Slide 19
Project Build – Software Implementation
Notes: This part shows the main workout interface. Here you can choose a workout type—like squats, push-ups, or hammer curls—and set their desired number of sets and reps. Once the workout starts, as shown on the right, the camera tracks the user’s movements in real time. It counts reps, detects body angles, and even shows the stage of motion—like ascent or descent during a push-up. This allows users to get instant, visual feedback on their posture and performance throughout the session.

## Slide 20
Project Build – Software Implementation
Why MediaPipe?
Notes: So why did we choose MediaPipe? As shown in the table, although YOLOv7 and YOLO11 are more recent and powerful, their models are much larger and support fewer keypoints—only 17. MediaPipe, on the other hand, supports 33 keypoints and has a very lightweight model, just 7.5 MB. It’s also optimized for CPU and works well on both web and native platforms, which fits perfectly with our real-time, cross-platform needs. That’s why it was the best choice for our pose tracking module.

## Slide 21
Project Build – Software Implementation
Notes: This shows how we track and display training history. On the left, we give users a high-level overview—total workouts, exercise types, weekly frequency, and even a streak counter. Below that is a breakdown of which exercises they’ve done most. On the right, we log each individual session with timestamps, set and rep counts, and duration. This helps users reflect on their progress and allows our AI module to generate personalized suggestions based on long-term patterns.

## Slide 22
Project Build – Software Implementation
Notes: Finally, based on the training records, we generate personalized AI suggestions. On the left, users can check their weekly activity and request recommendations by clicking the Get AI Suggestions button. Once generated, as shown on the right, the app provides targeted advice—like increasing hammer curl volume, balancing upper and lower body training, or maintaining workout frequency. These suggestions are generated using Deepseek API based on user history, aiming to guide smarter, safer, and more effective training.

## Slide 23
Requirements & Validations
Notes: This slide lists the main requirements for both hardware and software, and how we verified them. For example, the microcontroller had to boot up correctly, respond to commands, and connect to Wi-Fi. The camera needed to stream clearly, and the app had to count exercises accurately and store training history. We also tested AI suggestions, making sure they respond fast and show up correctly in the UI. Each function was verified through logs, UI feedback, or manual checks.

## Slide 24
Functional Tests Example – Real-Time Validation
A Python timer / Chrome DevTools: track average and worst-case runtimes.
Under different lighting conditions & configurations defined by choice of keypoints.
Notes: A Python timer wrapped the primary inference loop to track average and worst-case runtimes. This test was performed across frames under different lighting conditions and configurations defined by choice of keypoints.
As you can see, frames shown in graph demonstrated that our inference module is kept under 200ms threshold.

## Slide 25
4
Successes and challenges

## Slide 26
Success and Challenges​
Success
Successfully implemented an AIoT-based real-time motion tracking system.
Adopted MediaPipe-based server-side pose estimation and a Flask-built backend service.
Developed a cross-platform UniApp mobile frontend.
Low-cost and simple hardware system.
Notes: Successfully implemented an AIoT-based real-time motion tracking system that provides accurate fitness guidance.
Adopted MediaPipe-based server-side pose estimation and a Flask-built backend service to achieve efficient real-time data exchange and dynamic feedback.
Developed a cross-platform UniApp mobile frontend that offers a good user experience with an attractive interface and comprehensive functionality, supporting Web, Android, and WeChat platforms.
After multiple iterations of hardware design optimization, a low-cost and simple hardware system was achieved, and all functional verification tests were passed

## Slide 27
Success and Challenges​
Challenges
Limitations in Action Type Expansion.
Occasional Real-time Fluctuations.
Unstable Wi-Fi connections.
Notes: Limitations in Action Type Expansion.The current system is primarily optimized for a few common fitness actions. For more complex or diverse new action types, model parameters may need to be retrained or adjusted
Occasional Real-time Fluctuations.Despite meeting real-time requirements in most cases, frame latency may exceed expectations under extreme conditions such as network congestion or simultaneous access by a large number of users.
Wi-Fi. Weak Wi-Fi signals may result in the failure in connection between the mobile app and the camera on PCB. The mobile phone cannot detect and connect to the camera sometimes.

## Slide 28
5
Future Development

## Slide 29
Functional Expansion
More fitness actions and sports.
Develop social features.
Add virtual coach functionality.
Future Development​
Notes: Expand the system's library of exercise types to include more fitness actions and sports.
Develop social features to allow users to share their training achievements and experiences with friends or fitness enthusiasts.
Add virtual coach functionality to provide more personalized training plans and real-time guidance, offering voice or text prompts based on users' real-time performance.

## Slide 30
User Experience Optimization
Better frontend interface design.
Enhance user feedback mechanisms.
More tools for training data visualization and analysis.
Future Development​
Notes: Improve the frontend interface design for greater simplicity, intuitiveness, and ease of use, while providing more customization options to meet individual user preferences.
Enhance user feedback mechanisms to promptly collect user opinions and suggestions, and continuously refine system functions and services based on user needs.
Offer richer tools for training data visualization and analysis to help users better understand their progress and performance, enabling more targeted training adjustments.

## Slide 31
Technical Improvements
Advanced pose estimation algorithms and models.
Optimize network transmission protocols and data compression algorithms.
More efficient on-device inference method.
Future Development​
Notes: Explore advanced pose estimation algorithms and models, such as deep learning-based 3D pose estimation, to enhance the system's adaptability to complex actions and different scenarios.
Optimize network transmission protocols and data compression algorithms to further reduce latency and improve real-time performance.
Investigate more efficient on-device inference methods to reduce reliance on servers and enable broader offline usage scenarios.

## Slide 32
Q&A
Zhejiang University-University of Illinois Urbana-Champaign Institute

## Slide 33
THANK YOU!
Zhejiang University-University of Illinois Urbana-Champaign Institute