## Slide 1
Team #23
Jiarong Xu, Haojun Li, Jiaming Ma, Xinyu Zhan

## Slide 2
Background & Motivation
Notes: Power electronics circuits are everywhere.
Boost converter are widely used.
For example, boost converters are used in renewable energy, EVs, portable devices, USB chargers and many other systems.
They are important because they can step up voltage with high efficiency, simple structure, and easy control.
But the design is not always easy. If we only use a normal GPT, which is a black-box, the result may look reasonable, but it can not understand real circuit physics. Therefore, it doesn't help us very much in real-world circuits. More importantly, I might be quite dangerous because of the hallucination.
So our idea is to combine AI with real-world hardware.
In this demo, we focus on a boost converter, but this framework can also be extended to other circuits, like buck, RLC

## Slide 3
Overview
Notes: The process contains five main steps.
So in short, our solution is not just asking GPT for an answer. It is a closed-loop design platform. It uses AI for planning, physics for prediction, hardware data for verification, and PANN for diagnosis. This makes the design more reliable, more explainable, and closer to real circuit behavior.

## Slide 4
Free Chat Mode-can answer electrical problems
Frontend and main workflow
Assistant-can generate a guided engineering workflow.
Notes: This slide shows the frontend interface of our project.
At the lower-left corner, PE-GPT provides two operating modes.
The first mode is the Free Chat mode.
This mode accepts natural-language input and helps users answer questions related to power electronics.
It works like a chatbot with electrical engineering knowledge.
The second mode is the main part of our project, called the Circuit Build Assistant.
This mode can generate a guided engineering workflow for power electronics circuit design.
Instead of only answering questions, it helps users go through the complete design process step by step.

## Slide 5
Workflow-step1 Describe Circuit
Step 1 — Workflow Initialization
Select or describe target converter topology
Initialize corresponding engineering workflow automatically
Combine flexible interaction with structured workflow design
Prepare downstream planning and validation stages
Notes: This slide shows the main interface after entering the Circuit Build Assistant mode.
Currently, we have developed guided design workflows for three different circuit topologies:
Boost Converter
Buck Converter
RLC Oscillator
The system can also accept natural-language circuit descriptions and automatically infer the target topology.
Since our hardware platform is based on a boost converter, the following presentation will focus on the workflow of the boost-converter design agent.

## Slide 6
Workflow-step2 Al Planning
Step 2 — AI Workflow Planning
Analyze selected topology and operating conditions
Generate physics-aware engineering workflow automatically
Connect planning, validation, and
diagnosis stages
Prepare downstream analytical
design calculations
Notes: This slide shows the AI planning stage.
After the user selects the target circuit, the agent analyzes the topology.
The system then generates a guided engineering workflow, including:
circuit understanding
parameter design
hardware validation
diagnosis and correction
Before continuing, the agent asks the user whether to follow the proposed workflow.After confirmation, the current workflow stages are displayed on the left side to help users track the system status and progress.

## Slide 7
Workflow-step3 Circuit Understanding
Step 3 — Circuit Understanding
• Present physical circuit model for selected topology
• Explain key components and power-flow behavior
• Help users identify required design parameters
• Prepare analytical understanding before numerical calculations
Notes: In this stage, the AI presents the physical circuit model of the target topology.
The system can list and explain the important physical parameters needed for the design process.
This step helps users build a basic understanding of the converter before starting numerical calculations.
It also connects the AI-generated workflow with the analytical model and prepares the later design and validation stages.

## Slide 8
Workflow-step4 Requirement Input
Step 4 — Requirement Input
Accept structured or natural-language circuit requirements
Parse operating targets and engineering constraints automatically
Detect invalid inputs and unrealistic parameter combinations
Prepare validated inputs for downstream analytical design
Notes: In this step, users provide the circuit design parameters.
The system supports both structured form input and natural-language input.
Users can either fill in the parameter table directly or describe the design target using natural language.
The AI assistant can automatically recognize and parse the required engineering parameters for later analytical calculations and validation

## Slide 9
Workflow-step5 Requirement Check
Step 5 — Requirement Validation
Continue verification from previous requirement-input stage
Detect missing parameters or invalid topology configurations
Check physical consistency and engineering feasibility automatically
Proceed only after valid and safe requirements are confirmed
Notes: In this step, the system verifies whether the input parameters are complete and physically reasonable.
If users enter invalid topology settings or missing parameters, the agent will detect the problem, explain the reason, and guide users back to the previous step for correction.
After all requirements pass validation, the workflow proceeds to the next analytical design stage automatically.

## Slide 10
Circuit Parameter Design
Uses a non-ideal boost model with losses/parasitics.
Outputs are first-pass targets for PCB and simulation.
workflow-step6 Non-ideal Boost Design
Notes: In Step 6, PE-GPT builds a non-ideal Boost Converter tool based on the real physical model. Instead of assuming an ideal circuit, it considers practical effects such as voltage drops, parasitic resistance, and power losses. Then it calculates the key electrical parameters, including D, L, and C, and stores them for later hardware implementation.

## Slide 11
Hardware Preparation
1.replace the actual inductor and capacitor according to the calculated values.
2.turn on the power supply.
3.Set the calculated duty command into the controller
workflow-step7 Hardware Preparation
Notes: In Step 7, the workflow moves to hardware preparation. The system asks the user to replace the actual inductor and capacitor according to the calculated values and then turn on the power supply. After that, the agent communicates with the CH340 control board. It first resets the GD32 duty cycle to zero for safety, and then writes the calculated duty command into the controller.

## Slide 12
Hardware Setup & Sampling
A
B
C
D
A: Power supply
B: Oscilloscope
C: Hardware Setup
D: Design Agent

## Slide 13
Hardware Setup & Sampling
A
B
C
D
A: Power supply
B: Oscilloscope
C: Hardware Setup
D: Design Agent
Notes: Hardware setup

## Slide 14
Hardware Setup & Sampling
Half-bridge module
L
Cout
R
Driving
voltage
Sampling Module
CH340
USB-to-UART Bridge
GD32
Control Board
Notes: Design and build the main PCB board

## Slide 15
Hardware Setup & Sampling
Half-bridge module
L
Cout
R
Driving
voltage
Sampling Module
CH340
USB-to-UART Bridge
GD32
Control Board
Notes: Topology

## Slide 16
Hardware Setup & Sampling
Half-bridge module
L
Cout
R
Driving
voltage
Sampling Module
CH340
USB-to-UART Bridge
GD32
Control Board

## Slide 17
Hardware Setup & Sampling
Driving
voltage
Sampling Module
CH340
USB-to-UART Bridge
GD32 Microcontroller Control Board
Current &
voltage data
Sending duty ratio command for PWM
Reading current/voltage data

## Slide 18
Hardware Validation
Reads measured Vout and current, then compares with prediction.
Observed mismatch: 21.46 V and 0.224 A.
Treats mismatch as engineering evidence, not simply failure.
workflow-step8 Hardware Validation
Notes: In Step 8, the system performs hardware validation. The GD32 samples the real output voltage and current, and PE-GPT compares these measured values with the predicted results.

## Slide 19
Diagnosis
Uses the measured mismatch to diagnose likely error sources.
Keeps L/C unchanged if component targets are plausible.
workflow-step9 Diagnosis
Notes: In Step 9, PE-GPT analyzes the possible causes of deviation between the measured and predicted results. For example, the mismatch may come from Sampling accuracy, sensor offset, load variation, or duty-cycle implementation error.

## Slide 20
Parameter Correction and Re-Validation
1.Control circuits Calibrate Duty
2.Re-sample or rerun validation to verify that the updated results improve upon the original design.
workflow-step10 PANN-Guided Duty Correction and Re-validation
Notes: Finally, in Step 10, the system corrects the duty cycle based on the diagnosis result. Then it re-samples the circuit and runs validation again to check whether the updated result improves the original design.

## Slide 21
Successes and Challenges
Challenge: There was a significant deviation in the measured current.
Cause:
Unstable initial current
Previous:
Power supply →sampling → EN=1(unstable I)
Solution:
modifying and reprogramming
Now:
Power supply→EN=1(unstable I) → wait → sampling(stable I)

## Slide 22
Recommendations for Further Work
Features:
circuit learning
topology understanding
component sizing
circuit building
simulation
validation
troubleshooting.
Educational circuit design software
Other branches can be further implemented and expanded.

## Slide 23
Thank you for listening!
Q&A