## Slide 1
Smart Foot-Controlled Mouse with UI-Aware Assistance
Team number: 27 Team members: Zhihao Cheng, Chaoxiang Yang, Hao Liu, Jiongye Liu
浙江大学伊利诺伊大学厄巴纳香槟校区联合学院
Zhejiang University/University of Illinois at Urbana Champaign Institute
Advisor: Wee Liat, Ong TA: Ruolin Zhao
Date: 2026/5/23
ECE 445
Notes: Hello everyone，we are group 27

## Slide 2
Introduction & Objective
The generation and development of ideas
ZJUI
ECE 445

## Slide 3
Introduction & Objective
The generation of ideas
ECE445 3
Product demand
Industry gap
We need a mouse that is convenient for people with limited upper limb mobility！！！
Notes: Our idea is quite simple. Many people around the world have difficulty controlling computers with a mouse. So we need a device that can allow users to move the cursor with their feet and perform single and double clicks.

## Slide 4
System Block Diagram
Use for block diagram or workflow
ECE445 4
Notes: The overall process is to convert the pressure of the feet into a voltage signal, which is then processed and transmitted by USB to the computer.

## Slide 5
Frame & Hardware Design
Use this slide to separate major parts of the talk
ZJUI
ECE 445

## Slide 6
Mechanical Architecture
Frame & Hardware Design
ECE445 6
Silicone roof panel
Encapsulation board
USB adapter cable
Force Sensing Resistor (FSR)
Sensor Interfece Board
Arduino development board
Pedestal
Explosion
Product
Silicone gasket
Notes: Our product is divided into two layers. The upper layer can be replaced according to your needs, and the lower layer can be disassembled, which includes sensors and PCB.

## Slide 7
Ergonomic design
Frame & Hardware Design
ECE445 7
Foot-shaped design
Asymmetric sensor distribution
Rubber anti-slip base and silicone insoles
Notes: In order to enhance comfort，we have Foot-shaped design for lighter, Asymmetric sensor distribution for easier control, Rubber base for anti-slip and silicone insoles for more comfortable.

## Slide 8
Final Arduino-Based Architecture
Problem background and project goal
ECE445 8
Sensor Interfece Board
Sensor Interfece Board
Arduino development board
Force Sensing Resistor (FSR)
Notes: Our final solution is based on an FSR and an Arduino Leonardo development board. As a prototype, this solution offers high stability. The top-right corner shows our FSR performance tests, while the bottom-left corner displays a PCB we designed to convert the FSR’s resistance into a voltage.

## Slide 9
Distributed ADC–RS485 Architecture Exploration
Problem background and project goal
Why Explore a Distributed ADC–RS485 Architecture?
Scalability Problem
Cost Challenge
Wearable System Challenge
Advantages：
High Scalability
Low Cost
Distributed Sensing Nodes
ECE445 9
Notes: We also explored a lower-cost, in-house designed PCB. This design relies on RS-485 for communication between the master and slave devices. Using the STM8’s ADC interface, we convert analog signals into TTL digital signals. The TTL signals are then converted to RS-485 signals via the MAX485. RS-485 provides high-fidelity analog signal transmission and supports multiple slave devices connected to a master via a single bus. It offers these advantages. However, due to limitations in PCB soldering capabilities, this board exhibited low stability, so we did not use this solution in our prototype.
Translated with DeepL.com (free version)

## Slide 10
UI & Functional implementation
Use this slide to separate major parts of the talk
ZJUI
ECE 445

## Slide 11
Pressure - Cursor movement converter logic
UI & Functional implementation
ECE445 11
Notes: This section explains how cursor movement is achieved. First, we sample the voltage of each FSR at a specific frequency and treat these values as 1,023 distinct height levels. These correspond to the absolute pressure values at each position. When the USB connection is first established, an automated initialization process is triggered, which records the foot’s own pressure. When we want to move the mouse, the pressure on the FSRs differs from the initial state, and the difference in the absolute readings of each FSR is mapped to the magnitude of a corresponding direction vector, thereby determining the final movement.
Translated with DeepL.com (free version)

## Slide 12
Pressure - Click converter logic
ECE445 12
UI & Functional implementation
Notes: Our click operation is based on sudden changes in FSR pressure. When such a sudden change is detected, cursor movement is locked, thereby preventing accidental cursor movement during the click operation. Additionally, we have established reasonable trigger conditions for click detection.

## Slide 13
Edge Extension Architecture
The browser layer turns raw HID mouse motion into UI-aware pointer behavior.
ECE445 13
Foot Sensors
FSR pressure input
converted by MCU
USB HID Mouse
Standard cursor events
recognized by OS
Content Script
Injected on web pages
captures trusted events
Assist Engine
Finds nearby clickable
DOM targets
Simulated Click
Dispatches corrected
MouseEvent objects
Manifest V3 Integration
content_scripts inject content.js and content.css on all URLs; background.js handles Alt+Shift+F as a lightweight service worker.
Page-Local Overlay
A fixed root layer draws the virtual cursor, raw dot, snap ring, and small settings dock without changing page layout.
Persistent Settings
chrome.storage.sync stores enabled state, radius, strength, and raw-point visualization across popup and page UI.

## Slide 14
Magnetic Targeting Algorithm
The extension searches real web controls and smoothly biases the cursor toward the closest target.
ECE445 14
Snap Field Model
raw HID point (mx, my)
Button
Correction grows as distance decreases inside radius R.
For every mousemove, the content script computes:
1. Candidate DOM Targets
button, anchor, role=button, and input controls that are visible and not part of the extension UI.
2. Nearest Center
Each target center is compared to raw pointer position using Euclidean distance.
3. Strength Factor
t = strength x (1 - d / R), so strong snapping only happens near the target.
4. Virtual Cursor
cx, cy are updated to the corrected coordinate while the raw point remains visible for debugging.

## Slide 15
Pointer Event Redirection
Clicks are intercepted before the page handles them, then replayed at the assisted coordinate.
ECE445 15
Capture Phase
mousemove updates rawX/rawY;
click events are observed with useCapture=true.
Safety Checks
ignore extension dock UI;
process only trusted user events.
Hit Testing
elementFromPoint(cx, cy)
finds the corrected page target.
Replay Event
dispatch MouseEvent(type)
with clientX/clientY set to assisted position.
Why this matters
The browser still sees normal MouseEvent semantics, but at a coordinate adjusted for foot-control accuracy.
Compatibility boundary
No native driver is required; the extension works with the standard HID mouse stream from the foot hardware.

## Slide 16
Controls and User Feedback
A small overlay makes tuning visible during testing while keeping the page interactive.
ECE445 16
In-Page Assist Dock
Enable assistance
checked / unchecked
Magnetic snap
assistOn
Show raw point
debug visualization
Radius
32-180 px
Strength
0.00-1.00
Popup Panel
popup.js reads and writes the same storage keys, so global settings remain synchronized with the in-page dock.
Keyboard Toggle
background.js listens for Alt+Shift+F and sends a toggle message to the active tab.
Visual Feedback
The custom cursor changes state, the raw point can be displayed, and a ring highlights the active snap target.
Failure Mode
When disabled, the overlay hides the virtual cursor and restores the page's normal pointer behavior.

## Slide 17
Result
Use this slide to separate major parts of the talk
ZJUI
ECE 445

## Slide 18
Requirements & Results
Quantitative evaluation layout
Recommended: show latency, accuracy, or other key metrics with simple bar charts or tables.
ECE445 18
Latency (ms)
Chart: 
| Requirement Max | Measured
Latency | 20 | 12
12 ms → 40% below the 20 ms design limit
Selection Accuracy (%)
Chart: 
| Requirement Min | Measured
Accuracy | 75 | 85
85% → exceeds the 75% requirement

## Slide 19
Verification Table
ECE445 19
Verification Matrix
Requirement | Target | Verification Method
Cursor latency | < 20 ms | 50-trial delay test
Selection accuracy | > 75% | 100 trials
FSR sampling rate | ≥ 100 Hz | Debug output / oscilloscope
Snap radius | 32–180 px | Software setting validation
Compatibility | Windows / MacOS | Functional system test

## Slide 20
Future Work & Conclusion
Use this slide to separate major parts of the talk
ZJUI
ECE 445

## Slide 21
Future Work
The next stage is to move from a functional prototype toward a stable, ergonomic product.
ECE445 21
Compact Electronics
Design a smaller custom PCB to replace loose wiring, improve reliability, and reduce assembly complexity.
Adaptive Calibration
Add user-specific pressure threshold tuning so different foot habits, shoe shapes, and placements remain stable.
Ergonomic Enclosure
Improve the slipper-like frame for comfort, stable foot placement, safe edges, and adjustable sizing.
Software Refinement
Tune cursor mapping, click thresholds, visual feedback, and UI-aware assistance to lower the learning cost.
Prototype to Product Path
PCB
Enclosure
Calibration
Product
Goal: reduce cost and improve comfort without changing the standard USB HID compatibility.

## Slide 22
Conclusion
The system demonstrates a practical foot-controlled mouse with software-side UI assistance.
ECE445 22
What We Achieved
Integrated Prototype
FSR sensors, Arduino processing, USB HID output, and Edge extension assistance work as one system.
Core Mouse Functions
The prototype supports smooth cursor movement, left click, double click, and right click.
Driver-Free Compatibility
The computer receives standard mouse events, so no custom native driver is required.
UI-Aware Assistance
Magnetic targeting helps compensate for the lower precision of foot-pressure input.
Main Limitation
The remaining gap is mostly usability: new users need adaptation time, and pressure habits can affect control comfort.
Ethical Safety
Low-voltage USB operation, insulated connections, safe enclosure design, and adjustable thresholds reduce risk.
Privacy
The device only converts local foot-pressure signals into mouse commands; it does not collect or transmit personal data.
Final Takeaway
A low-cost assistive input device becomes more practical when hardware sensing is paired with intelligent software assistance.

## Slide 23
Teamwork Distribution
The division of labor within the group is quite even.
Chaoxiang Yang: Arduino-Based Architecture & Distributed ADC–RS485 Architecture
Hao Liu: UI-cursor-assistance
Jiongye Liu: Mechanical Architecture & Ergonomic design
Zhihao Cheng: Arduino-Based Architecture
All group members participated in the literature creation work and group discussions
ECE445 23

## Slide 24
Thank You
Questions & Answers
浙江大学伊利诺伊大学厄巴纳香槟校区联合学院
Zhejiang University/University of Illinois at Urbana Champaign Institute