## Slide 1
ECE 445 · Senior Design Laboratory
Intelligent Basketball
Retrieval & Return Robot
Detect · Aim · Launch
Team 36
Jinghui Zheng · Libo Zhang · Zichao Lin · Linzhi Du
TA: Jianzu Zhang · May 2026
UIUC 2026
Notes: Good morning, everyone, we are team 36. Our design is Intelligent Basketball Retrieval and Return Robot. The core idea is a system that can detect where a player is, aim itself at the player, and pass the ball back automatically. Let's get started. (25s)

## Slide 2
Problem & Motivation
The Problem
Individual basketball training is disrupted by manual ball retrieval
Existing machines have fixed direction and cannot track player movement
Player must stop drill to reposition machine when changing locations
Training rhythm and consistency are significantly reduced
Our Solution
Adaptive robot that dynamically detects player position via Bluetooth
Stepper motor rotates launcher to align with target direction
Dual friction-wheel mechanism launches ball at controlled speed
Software safety interlocks inhibit launch when signal is lost
Notes: Let me start with the problem we're trying to solve. When a player is training alone, he typically move around the court and every time he shoot, if there's no assistant, the player has to stop, walk over, and retrieve it. This makes it very hard to build consistent shooting form.
Existing machines do help, but they have a critical limitation. They are fixed direction. When the player moves to a new spot, the machine is still pointing at the old one.
Our design solved the problem. The player just moves — the machine follows. (55s)

## Slide 3
System Overview
Bluetooth Low Energy
(BLE) Sensing
Player carries
Bluetooth locator
▶
ESP32
Controller
Target estimation
& control logic
▶
Aiming &
Rotation
Stepper motor
rotates base
▶
Friction
Launcher
BLDC motors
accelerate ball
▶
Ball
Passed!
To player within
0.6 m radius
Detect → Aim → Launch
Notes: Here's the big picture of how the system works.
First, the player carries a small Bluetooth locator. The bluetoothbase will continuously tracking it.
Second, the Controller takes angle and distance information from the base, and translates that into commands for motors.
Third, a stepper motor rotates the laucher to align it with the player's direction.
Fourth, two counter-rotating friction wheel will accelerate the basketball to the target speed.
Then Ball Passed. (55s)

## Slide 4
System Design
BLE Localization
RSSI-based distance estimation
UUID/MAC filtering, player-specific lock
Path-loss model calibrated indoors
3–7 m operating range
Aiming & Rotation
Friction-Wheel Launcher
Dual BLDC motors + ESCs
Counter-rotating wheels compress ball
Configurable speed: 4–8 m/s
Projectile-motion ballistic model
Power & Safety
Notes: Here is a more precise overview of our system, indicating how the signals and electrical power flow. We can devide our system into four parts.First is the Localization module, mainly cove rthere blocks(指向player with bluetoth;BLE sensing和ESP32模块), it uses bluetooth signal to locate the angle of the player and send the signal to the controller; Then we have Aiming & Rotation module (指向aim command部分, it compute the signal from the bluetooth and command rotation motor to drive the robot into suitable angle. Another important part is Launching Module (指向speed command), use two friction-Wheel to launch te basketball out to the player. Finally, we have the power module which can provide electricity for our device

## Slide 5
Design Deep-Dive: Localization & Targeting
BLE Subsystem
Why Bloutooth?
Lower hardware & computation complexity vs camera-based tracking
UUID filtering — locks onto player's specific locator only
Camera alternatives: sensitive to lighting, occlusion
Targeting Logic & Angular Error
eθ = θ_target − θ_launcher
Tolerance Analysis at Max Range (7 m):
Angular Error | Lateral Deviation | vs 0.6 m Limit
3° | ≈ 0.37 m | ✓ Safe
5° | ≈ 0.61 m | ⚠ At Limit
7° | ≈ 0.86 m | ✗ Exceeds
Angular Error Lateral Deviation vs 0.6 m Limit
Notes: This slide focuses on our localization and targeting subsystem.
First, we chose BLE because it has lower hardware and computation complexity compared with camera-based tracking. It does not require an extra camere and image processing pipeline.
second,, we use UUID filtering to identify the player’s Bluetooth beacon. Here, the UUID is like an ID for the beacon, so the robot only responds to the locator carried by the player, instead of reacting to other Bluetooth devices nearby.
In contrast, a camera-based system could be more sensitive to lighting conditions, player occlusion .
On the right side, we calculate angular error. The key point is that even a small aiming error can create a large lateral deviation at longer distance. At our maximum range of 7 meters, a 5-degree angular error already causes about 0.61 meters of deviation, which is right at our 0.6-meter accuracy limit.

## Slide 6
Design Deep-Dive: Aiming & Rotation
Fig. CAD View — Rotating Base & Launcher Mounting Structure
⚙
Mechanical Design
Launcher mounted on rotating base; rotation axis centred on upper assembly
Centering reduces eccentric load & wobble during aiming
Stepper motor + dedicated driver → high-res angular steps
PWM step & direction signals from ESP32
No limit switches — initial heading set manually or by software reference
Torque Requirement
T = I·α + T_f
▶
Control State Flow
① Detect Target
▼
② Calculate Error eθ
▼
③ Send PWM to Driver
▼
④ Rotate Base
▼
⑤ eθ < tol → Ready ✓
Reorientation target: < 2 s · ESP32 PWM step & direction signals → motor driver → high-resolution angular adjustment
Notes: For this part, we focus on how the robot physically aims at the player.
The launcher is mounted on a rotating base, and we designed the rotation axis to be close to the center of the upper structure. This reduces wobble and makes the system more stable when it turns and launches the ball.
We use a stepper motor with a motor driver for rotation. The ESP32 sends step and direction signals, so the launcher can rotate to the desired angle with good precision.
For motor selection, we considered the weight and moment of inertia of the upper structure, the required rotation speed, and friction. Our goal is to aim within 2 seconds.
The control process is straightforward: the robot detects the target, calculates the angle error, rotates the base, and stops when the launcher is aligned. Then the system is ready to launch.

## Slide 7
Design Deep-Dive: Launching & Ballistic Design
Launch Subsystem
Dual Friction-Wheel Mechanism
Two counter-rotating BLDC wheels compress and accelerate the ball
Wheel spacing critical: too large → insufficient traction; too small → excess motor load
Manual ball loading chosen for reliability during prototype phase
Motor & Wheel Speed Estimation
n = Kv · V
v_wheel = 2πrn / 60
Kv = motor speed constant (rpm/V) · r = wheel radius
Actual release speed < no-load estimate (slip, compression)
Projectile-Motion Ballistic Model
v₀ = √[ gD² / (2cos²θ · (D·tanθ − (H−h))) ]
D
= Horizontal distance to target
θ
= Launch angle
h
= Launch height
H
= Target receiving height
g
= Gravitational acceleration
Assumes no air resistance. Model used for first-order estimation
only — calibrated experimentally for actual launch conditions.
Notes: The key mechanism in the launcher is two counter-rotating friction wheels that compress the ball and accelerate it forward.
Wheel spacing is one of the most critical parameters. Too wide, the wheels cannot grip the ball. Too narrow, it will overloading the motors and deforming the ball.
Motor speed is estimated from the supplied voltage, then converted to wheel surface speed. However the actual ball release speed is always lower than the theoretical value, due to motor loading, and wheel slip.
The model gives us the estimate of release speed. We assume no air resistance and treat the basketball as a point mass. we correct it through experiments. (60s)

## Slide 8
Design Deep-Dive: Control, Power & Safety
System State Machine
Power Architecture
Main Battery
↓ High-current path ↓ Step-down
ESCs + BLDC Motors
(Launch)
Stepper Driver
(Rotation)
ESP32 + Logic
(5V / 3.3V)
Common GND reference between
controller & motor circuits ensures
clean PWM signal transmission
Safety Design Summary
SW interlock: launch blocked if BLE RSSI drops below valid threshold
Isolated power paths: high-current motors cannot inject noise to ESP32
Manual ball loading: operator always in control of launch sequence
No hardware e-stop in v1 — future work: physical fail-safe circuit
Notes: Finally, let's look at the control , power , and safety system.
The controller systm runs a nine-state state machine. We've descibed how it works before and if in any of these states the bluetooth signal is lost, the motor will stop.
For power, we use a split-path architecture. The main battery feeds high current directly to motor ad motor drivers. Then a step-down voltage regulator converts that to 5V and 3.3V for the ESP32 and logic circuits.
A common ground reference ties both paths together to ensure clean signal transmission.
To summarize the safety design: we have a software interlock on bluetooth signal , isolated power paths to protect the controller, and have a swict to start an stop all process.

## Slide 9
Prototype
[Insert Robot Photo 1]
Overall Assembly
[Insert Robot Photo 2]
Launcher & Friction Wheels
Notes: Here you can see the result of our design. On the left is the overall assembly — you can see the rotating base on the bottom and the launcher body mounted on top. On the right is a video of our practical presentation. You can see it's rotating towards the player's dirction, and launch the ball.

## Slide 10
Verification Results
3–7 m
Operating
Range
✓ PASS
< 2 s
Aiming
Response
✓ PASS
4–8 m/s
Launch
Speed
✓ PASS
>85%
Passing
Accuracy
✓ PASS
✓
Signal-Loss
Protection
✓ PASS
Requirement | Target | Result | Status
Operating Range | Valid BLE detection 3–7 m | Detected at all test distances | ✓ Pass
Passing Accuracy | ≥85% within 0.6 m radius | Over 85% success rate | ✓ Pass
Launch Speed | 4–8 m/s configurable | Configurable across full range | ✓ Pass
Aiming Response | < 2 s reorientation | Within 2 s under normal conditions | ✓ Pass
Signal-Loss Safety | Inhibit on Switch & BLE loss | Motor inhibited correctly | ✓ Pass
Requirement Target Result Status
Notes: Now let's talk about results. We defined five high-level requirements at the beginning of the project, and I'm pleased to report that all five were verified as Pass.
First, Operating Range: The system maintained reliable Bluetooth target detection across the full 3-to-7-meter range. At all tests with the range can consistently achieved.
For Aiming Response: If the player is going to another place, the macine can relocated that position within 2 seconde.
As for Launch Speed: we confirmed that release speeds across the 4-to-8 meters-per-second range are achieveable.
For Passing Accuracy: We tested at the operating range as we discussed above, over 85% of passes arrived within a 0.6-meter radius of the players.
Signal-Loss Protection: When we disabled the Bluetooth locator mid-sequence, the motor correctly entered the Inhibited state. Also, the switch can successfully start and stop the machine.
And we successfully repeated aiming and launching cycles with no mechanical or electrical failures.

## Slide 11
Limitations & Future Work
Current Limitations
Manual ball loading — limits repeat rate, requires human intervention
Open-loop launch control — wheel slip & motor load cause speed variation
No limit switches — heading reference requires manual initial alignment
Need to use computer as a transfer station — since ESP32 is not compatible with the bluetooth module
Future Development
Automatic ball-feeding mechanism for high-repetition drills
Add rotary encoders + limit switches for reliable homing
Implement closed-loop PID speed control on friction wheels
Dedicated hardware emergency-stop circuit for fail-safe power-off
Developed the communication protocol for reliable communication between ESP32 and bluetooth module
Notes: Now we'll talks about limitation and future work, the biggest limtation is that we have to load th ball manually, whih means limied repeat rate and humn intervention.
We also have open-loop launch control, inconsistencies in wheel slip and motor loading can cause shot-to-shot speed variation.
The absence of limit switches means we rely on manual initial alignment, which introduces a heading reference error that accumulates if the base is moved.
For future development, the top priorities are: design an automatic ball-feed mechanism; adding closed-loop PID controll; add limit switches.

## Slide 12
Team & Project Cost
Libo Zhang
Rotating Base Design
Jinghui Zheng
Launcher Body Design
Linzhi Du
PCB & Electrical Circuit
Zichao Lin
Control Code & Firmware
Project Cost Breakdown
Total: 4,750
Chart: 
| Launch Motors | ESP32 & BLE | Labor | Mech. Frame | Rotation Motor | Friction Wheels | Power Electronics
Cost | 1000 | 1100 | 1500 | 1500 | 400 | 100 | 50
Notes: Here is our team contribution and project cost summary.
Libo Zhang was responsible for the rotating base design. Jinghui Zheng designed the launcher body. Linzhi Du worked on the PCB and electrical circuit, and Zichao Lin developed the control code and firmware.
The total project cost is about 4,750 yuan. The main costs come from the mechanical frame, launch motors, ESP32 and Bluetooth hardware, and labor. Overall, this budget allowed us to build a functional prototype that includes sensing, aiming, launching, and safety control.

## Slide 13
Conclusions
Reliable Detection
BLE target locked at 3–7 m with UUID filtering
Accurate Passing
>85% passes within 0.6 m, aiming < 2 s
Controlled Launch
4–8 m/s configurable, software safety interlock
The prototype successfully demonstrated the core Detect–Aim–Launch workflow, meeting all five high-level requirements and validating Bluetooth-guided adaptive basketball training as a feasible and effective system.
Thank You!
Questions & Discussion
Notes: To conclude, our robot successfully completed the main goal of this project: detect the player, aim at the player, and launch the ball.
It can detect the player from 3 to 7 meters, rotate within 2 seconds, and pass the ball with over 85% accuracy.
Overall, the prototype met our main requirements and showed that this design is feasible.
Thank you. We are happy to take any questions.