## Slide 1
Smart SoftBall UWB Positioning
Team 7
Chenhan Yang (chenhan7) Yuxing Wu (yuxingw2)
Tianyang Sun (ts30)
Advisor: Timothy Lee TA: Jianzu Zhang
May 16, 2026
Motion Analysis and Trajectory Reconstruction

## Slide 2
Content
1. Motivation and project goal
2. System overview
3. Hardware and TWR communication
4. Reconstruction algorithm and GUI
5. Verification results
6. Power, cost, and future work
7. Conclusion
Final embedded prototype
Notes: The figure shows the final version of our project. We use the different colors of LED beads to represent the different power consumption levels.

## Slide 3
1 Background
Motivation:
Camera-based softball analysis is expensive and is highly depended on a specific site. For daily training, we aim to built a portable and lower-cost Smart SoftBall System that embeds a UWB tag in the ball and reconstructs ball-motion from four anchors around the field.
- Goal: recover usable trajectory from noisy UWB range measurements, landing/out-of-bounds judgment verification..
- Final scope: power module, localization, data filtering, and GUI visualization.
Notes: We wanna make the power consumption data more visible and raise the sensitivity of saving electrical power for the students and faculty.

## Slide 4
2 Overview
A portable loop: UWB ranging in the ball, PC-side filtering, and live trajectory replay.
Smart
SoftBall Tag
4 UWB
Anchors
A0 Gateway
Node
PC Filtering
+ Constraints
GUI
Replay
TWR sequence: TAG -> A0/A1/A2/A3; range vector is forwarded through A0 serial gateway.
20 cm range offset correction
Least-squares position solve
Residual / velocity filters
Ground-mode reconstruction
Figure 1: Final Smart SoftBall UWB system architecture

## Slide 5
3.1 Hardware Implementation
Ball-integrated prototype
C2764088 + DW1000 / BU01 UWB module
Anchor/tag firmware board
Power-management PCB

## Slide 6
3.2 Communication - TWR Ranging
The final implementation uses sequential TWR because it was more stable than TDoA on BU01.
Tag initiates
ranging
A0
A1
A2
A3
Range vector
to A0
PC serial
receiver
20 Hz
stable live configuration
25.55 Hz
firmware stress-test equivalent rate
0 drops
no observed packet loss or disconnects
TAG -> A0, TAG -> A1, TAG -> A2, TAG -> A3, then A0 forwards one RANGE4D frame to the PC.

## Slide 7
4.1 Data Processing - Trajectory Reconstruction
Layered filtering converts biased UWB ranges into a delayed but stable trajectory.
The report's final software path keeps raw acquisition separate from reconstruction. This made the same GUI usable for live serial input, CSV replay, and post-test analysis.
- 20 cm fixed range offset correction
- RMS and local-RMS residual checks
- Velocity / acceleration constraints
- Interpolation with a 1 s delay buffer
- free3d, ground_z_cap, and ground_fixed_z modes
RANGE4D serial / CSV frame
Offset-corrected distances
Least-squares 3D solve
Residual + motion gates
Interpolation buffer
Trajectory GUI output
Notes: Through iterative calculations, power flow calculations provide valuable insights into many system parameters, including active and reactive power flow, voltage stability, and line loading, thus providing engineers and operators with a comprehensive understanding of the system's behavior and performance.

## Slide 8
GUI
GUI

## Slide 9
4.2 Data Processing – A Fantastic GUI and Visualization
GUI screenshot from final report
Functionality
Trajectory Acquisition
Data file management.
Raw Data Processing
Trajectory Display
Replay Functions

## Slide 10
Click to start collecting real-time data and display the trajectory in real time. automatically reads real-time data and saves the raw CSV file.
can open pre-processed 3D coordinate CSV files and play the trajectory point-by-point in sequence/index order.
import raw CSV files and automatically perform offset correction, distance filtering, 3D reconstruction, and coordinate filtering within the GUI.
Supports real-time trajectory display using delay buffering, RMS judgment, local neighborhood judgment, velocity threshold, and light smoothing.
Supports two raw data import methods: offline_filter and live_replay_filter.
4.2 GUI Data Management and Processing

## Slide 11
Supports setting four anchor point coordinates A0/A1/A2/A3 for different experimental site layouts.
Supports different motion filtering modes, such as walking, running, and ball motion modes, with different speed/acceleration thresholds for different modes.
Supports setting RMS filtering thresholds, such as 0.30 m.
Supports setting whether to filter or delete points with z=0.
Supports ground scrolling modes, including free3d, ground_z_cap, and ground_fixed_z.
4.2 GUI Raw Data Processing

## Slide 12
4.2 GUI RMS Threshold
RMS < 0.15
RMS < 0.3
Raw 3D data

## Slide 14
The 3D graph displays the anchor point names A0/A1/A2/A3.
The starting point is displayed in green,
The ending point in red,
The currently selected point in blue.
The trajectory line color gradually changes from the starting point to the ending point, making it easy to observe the direction of movement.
Supports one-click display of the complete trajectory, skipping the point-by-point playback process.
Supports locating points using a global index.
Supports locating trajectory points by clicking on a table.
When a point is selected, it displays the point's sequence, index, 3D coordinates, RMS, and 3D velocity.
The arrows in the graph indicate the velocity direction of the selected point, and the color intensity represents the velocity magnitude
4.2 GUI Trajectory Display and Replay Functions

## Slide 15
Supports setting the field range (Xmin/Xmax/Ymin/Ymax.)
After the trajectory points are projected onto the ground,
points within the field are displayed in gray
points outside the field range are displayed in red.
4.2 GUI Out of bounds detection

## Slide 16
5. GUI Involution

## Slide 18
5. Verification - Experimental Setup
Indoor field and anchor setup
Anchor | Coordinate (m)
A0 | (1, 0, 0.75)
A1 | (3.75, 0, 0)
A2 | (3.75, 3.9, 0)
A3 | (0, 3.9, 0)
3.75 m x 3.9 m test field
A0 z=0.75
A1 z=0
A2 z=0
A3 z=0
75 measurements across 5 reference points were used for final error analysis.

## Slide 19
5. Verification - Positioning Accuracy and Error Analysis
10.10 cm
horizontal RMSE
8.44 cm
mean horizontal error
7.73 / 6.49 cm / 27.33 cm
X / Y / Z RMSE
Horizontal positioning performance is the strongest part of the final system and supports portable trajectory visualization.

## Slide 20
5. Verification - Positioning Accuracy and Error Analysis
24.26 cm
mean 3D error
48.33 cm
maximum 3D error
Main limitation: anchors are mostly coplanar, so vertical geometry is weak. The next version should elevate anchors or add stronger vertical baselines.

## Slide 21
6. Implementation - Power and Cost
Type-C charging and TP4056-based power management
Power profile
Module | Current
A1/A2/A3 anchors | 120-180 mA
A0 gateway | 150-220 mA
Ball tag | 160-240 mA
1000 mAh
battery capacity used in prototype
1204.28 RMB
parts total, about $167.26
Including labor, the report estimates total project cost at about $19,067.26.
Notes: The WS2812 LED strip uses a single-wire communication protocol to transmit data between integrated circuits (ICs) embedded in each RGB LED. Each LED on the strip requires a 24-bit color value, which consists of three groups of 8 bits representing red, green, and blue color intensities. Data is sent in a serial format (one bit after another). A single long string of bits for an entire strip starts with the data for the first LED, followed by the second, and so on. Each LED has a small IC that reads the first 24 bits of the incoming data stream, sets its own color accordingly, and then passes the rest of the bits down the line to the next LED.

## Slide 22
7. Conclusion
A Picture of Our Model
Accomplished
- Four-anchor TWR localization pipeline
- Live/CSV GUI with trajectory replay
- Layered filtering and ground modes
- Horizontal RMSE around 10 cm
Future work
- Complete landing judgment
- Use higher-rate UWB or binary serial at higher baud
- Elevate anchors to improve Z-axis accuracy

## Slide 23
Thank You!
ECE445/ME470 SP26
Team 7
Smart SoftBall UWB Positioning