## Slide 1: Smart Vacuumed Rice Dispenser ECE 445 Final Presentation
Team #22: Gaoning Zhao; Shining Wang; Yuyang Liu; Zixin Yang
Zhejiang University - University of Illinois Urbana-Champaign Joint Institute
May 2026

## Slide 2: Overview
Introduction
Objective
Design Review
Subsystems & Functional Tests
Successes & Challenges
Future Work

## Slide 3: Introduction
Current Challenges
Quality Issue:
Long-term exposure to air and moisture may affect rice equality
User Inconvience:
Manual dispensing requires opening the container, scooping rice, and measuring the amount
Our Solution

## Slide 4: Objective
Main Objective:
Build a smart rice dispenser that automatically dispenses a user-selected amount of rice and restores vacuum storage after dispensing.
Technical Objectives: • Allow the user to select target rice weight using a rotary encoder • Display system status on an OLED screen • Ignore the weight of the empty receiving container using tare operation • Dispense rice using a DC gear motor • Stop dispensing based on load cell weight measurement • Detect abnormal dispensing when weight does not increase • Activate the vacuum pump after dispensing • Stop the pump when the pressure reaches the target threshold

## Slide 5: Block Diagram
Figure: Top-Level Block Diagram of the System

## Slide 6: Rice Bucket Structure Layout
Lower Section:
The main storage chamber that holds the rice and fixes the Archimedes screw pump.
Upper Cover:
The interface hub containing the screw cap (for refilling), the rice outlet, and routing holes.
Capacity Requirement:
Designed to hold 1500 gram of rice.

## Slide 7: Internal Dispensing Structure (Archimedes Screw)
Dispensing Mechanism: A fixed Archimedes screw pump located in the lower storage section.
Actuator: Driven by a 24 V DC motor.
Provides high torque to overcome the internal friction of rice grains.
Effectively prevents granular jamming.
Smoothly transports rice upwards to the dispensing outlet on the upper cover.

## Slide 8: Vacuum Sealing Structure
Upper Cover Interfaces:
Screw Cap: Features an O-ring seal and a through-hole for the vacuum pump tube.
Wire Routing: Two dedicated holes for the motor and pressure sensor cables.
Manual Dispensing Port: Sealed with a removable silicone stopper during storage.
Main Flange Seal: 12 M8 bolts tightly compressing a rectangular silicone gasket.

## Slide 9: Power Subsystem & PCB
The PCB connects the MCU (Arduino Nano) with:
  Rotary encoder
  OLED display
  HX711 load cell amplifier
  BMP280 pressure sensor
  Relay control signal
  MOSFET motor control signal
The 5 V input powers the Arduino Nano and low-power modules.
The 24 V DC geared motor uses a separate power supply because it requires higher voltage and current.
The 5 V air pump is controlled by a relay module to avoid directly driving pump current from the Arduino.
Notes: This slide explains the power subsystem and PCB design. The main controller of our system is the Arduino Nano, and the PCB is used to organize the electrical connections between the controller and different modules. The PCB connects the Arduino Nano with the rotary encoder, OLED display, HX711 load cell amplifier, BMP280 pressure sensor, relay control signal, and MOSFET motor control signal.
The control board is powered by a 5 V input. This 5 V supply is used for the Arduino Nano and other low-power modules, such as the sensors and OLED display. However, the dispensing motor requires higher voltage and current, so the 24 V DC geared motor uses a separate power supply. The Arduino does not directly drive the motor; instead, it sends a control signal to the MOSFET circuit.
For the air pump, we use a 5 V pump controlled by a relay module. This allows the Arduino to switch the pump on and off safely without directly providing the pump current. Overall, this design separates the low-power control circuit from the higher-current actuator parts, which makes the system more stable and reliable.

## Slide 10: Sensors
Load Cell
HX711 Amplifier
Weight Feedback
BMP280 Sensor
Pressure Monitoring
Closed-loop Control
Motor Stop
Pump Stop
Notes: In this part, the system mainly uses two sensors for feedback control. The first one is the load cell with the HX711 amplifier. The load cell measures the rice weight during dispensing, and the HX711 converts the signal into digital data for the Arduino Nano. During the dispensing process, the Arduino continuously reads the weight value. When the measured rice weight reaches the target amount, the motor stops automatically. The second sensor is the BMP280 pressure sensor. It monitors the internal pressure of the rice container after dispensing. When the vacuum pump is running, the Arduino checks the pressure reading and stops the pump when the preset pressure threshold is reached. Therefore, these two sensors help the system achieve both accurate rice dispensing and pressure-based storage control.

## Slide 11: User Interface
Rotary encoder is used to select the target rice amount
Each step changes the target value by 10 g
Target range: 10 g to 1000 g
Push button starts one dispensing cycle
OLED displays target weight, current weight, pressure, and system status
Notes: For the user interface, we use a rotary encoder and an OLED display.
The user can rotate the knob to select the target amount of rice, and each step changes the value by 10 grams.
The allowed range is from 10 grams to 1000 grams.
After selecting the target amount, the user presses the button to start the process.
The OLED displays the selected weight, current dispensing weight, pressure value, and current system status, such as Ready, Taring, Dispensing, Vacuuming, or Error.

## Slide 12: Control Logic (Finite State Machine)
IDLE: wait for user input
TARE_CONTAINER: remove empty container weight
DISPENSING: motor runs and load cell measures rice weight
STOP_MOTOR: motor stops when target weight is reached
ERROR_TIMEOUT: triggered when weight does not increase for 15 seconds
RE_VACUUM: pump turns on until the pressure reaches the target
Notes: The Arduino software is implemented as a finite state machine.
The system starts in the IDLE state, where the user selects the target rice amount.
After the button is pressed, it enters the TARE_CONTAINER state.
This step performs a tare operation, so the empty container weight is ignored.
Then the system enters the DISPENSING state.
The motor turns on, and the load cell continuously measures the rice weight.
If the measured weight reaches the target amount, the motor stops.
If the weight does not increase for a certain period of time, the system enters the error state.
This helps detect an empty rice container or a blocked outlet.
After dispensing, the system enters the RE_VACUUM state.
The vacuum pump turns on until the pressure reaches the target threshold, and then the system returns to IDLE.

## Slide 13: Functional Tests
User Interface Test
Load Cell and Tare Test
Motor Dispensing Test
No Rice Detection Test
Vacuum Pump and Pressure Test
Full System Cycle Test
Notes: For functional testing, we tested each subsystem separately first, and then tested the complete system cycle. The main tested functions include user input, weight measurement, motor control, no-rice detection, vacuum pump control, and the full automatic dispensing process.

## Slide 14: Successes & Challenges
Successes
Automatic dispensing worked.
Weight-based stop achieved.
OLED interface functioned.
Control circuit worked reliably.
Challenges
Vacuum sealing failed.
Needs additional ball valve to stop air backstreaming
Extra 24 V supply was needed.
Notes: For the successes, the system achieved automatic rice dispensing, and the load cell feedback allowed the motor to stop when the target weight was reached. The OLED interface also worked properly, so users could see the system status clearly. In addition, the main control circuit worked reliably with the Arduino, sensors, relay, and motor control.
For the challenges, the biggest issue was vacuum sealing. Because the container was not fully airtight, the pressure could not drop as expected. We also found that an additional ball valve may be needed to prevent air backstreaming. Finally, since the original motor did not provide enough torque, we used a 24 V motor, which required an extra power supply.

## Slide 15: Thank You!