## Slide 1
ECE 445 / FINAL PRESENTATION / TEAM 50.2
Automatic Sorting
Robotic Arm
for Table Tennis Balls
TCS34725 color sensing | Arduino control | five-servo sorting
Verified result: 49 / 50 correct
Siqi Pan | Zhonghao Wang | Xucheng Wu
TA: Jianzu Zhang | May 2026
Notes: Speaker: Siqi Pan
Introduce the project title, team number, and final verified result. State that the presentation focuses on the completed color-sorting prototype for white and yellow/orange table tennis balls.

## Slide 2
Team Roles & Roadmap
Xucheng Wu
The 12-minute talk divides the system by ownership: structure, sensing/software, power, and verification.
Siqi Pan
Ownership
Color sensor, software, power wiring and soldering
Presentation coverage
Intro, architecture, TCS34725 design, classification logic, software flow, power wiring
Wu Xucheng
Ownership
Mechanical structure
Presentation coverage
Prototype overview, feeder tower, arm geometry, servo motion and mechanical limitation
Zhonghao Wang
Ownership
Power verification and testing records
Presentation coverage
Verification setup, trial-by-trial results, voltage measurements, data interpretation
Flow: project goal -> design -> implementation -> verification -> demo
Notes: Speaker: Siqi Pan
Use this slide to make the division of labor explicit. Siqi covers sensing, software, and power wiring; Wu covers the mechanical structure; Zhonghao covers verification data, power measurements, and records.

## Slide 3
Problem & Motivation
Xucheng Wu
Mixed table tennis balls create inconsistent visibility and repetitive manual sorting work.
White / yellow-orange balls
are both official, but contrast
changes with environment.
Training consistency
Players and coaches may want one controlled ball color for a drill.
Manual sorting overhead
After repeated use, mixed balls must be separated before the next session.
Embedded-system opportunity
A compact sorter demonstrates sensing, control, actuation, and verification in one system.
Notes: Speaker: Siqi Pan
Explain the motivation: mixed balls create inconsistent visual contrast in training and require repetitive manual sorting. Emphasize that this is both a practical sorting problem and a compact embedded-systems demonstration.

## Slide 4
Final Objective
Xucheng Wu
Build a low-cost prototype that sorts common white and yellow/orange table tennis balls by color.
Feed
Advance one ball into the sensing region
->
Sense
Read TCS34725 red, green, blue, and clear values
->
Classify
Use RGB/C ratios to decide white, yellow/orange, or unknown
->
Sort
Actuate the servo arm and release into the target output region
Verified result: 49 of 50 balls were correctly sorted across five 10-ball trials.
Notes: Speaker: Siqi Pan
Walk through the final objective as a four-stage process: feed one ball, sense color, classify using RGB/C ratios, and actuate the sorting mechanism. Mention the headline result, 49 out of 50 balls correctly sorted.

## Slide 5
High-Level Requirements
Siqi Pan
Requirements were narrowed to the final demonstrable prototype: color sorting, repeatable timing, and stable motion.
Color classification
Classify balls as white, yellow/orange, or unknown; achieve at least 90% sorting accuracy over the mixed test set.
Sorting action
Route white and yellow/orange balls to their output regions; release unknown readings instead of forcing a color bin.
Timing
Complete a 10-ball trial in approximately 70-80 seconds after initialization during normal operation.
Power and motion reliability
Run from the LM2596-regulated rail without visible servo stall, abnormal jitter, or controller reset.
Test protocol: five trials; each trial used 5 yellow/orange + 5 white balls.
Notes: Speaker: Siqi Pan
Define the final requirements used for verification. These are the requirements the final prototype actually demonstrates: classification, sorting action, timing, and power/motion reliability. Clarify the test protocol: five trials, each with five yellow/orange and five white balls.

## Slide 6
Design Choices
Siqi Pan
Component choices were kept simple, low-cost, and easy to verify in a live tabletop prototype.
Controller
Arduino Uno R3
Enough PWM outputs for servos and I2C support for the color sensor.
Color sensing
TCS34725 RGB/C
Clear channel enables normalized ratios, reducing brightness sensitivity.
Actuation
4 positional + 1 continuous servo
Separates sorting motion from feeder advance while keeping control logic simple.
Power rail
LM2596 buck module
Regulates the 12 V input to a stable 5 V rail for controller and servos.
Design emphasis: repeatable demo behavior over unnecessary mechanical or software complexity.
Notes: Speaker: Siqi Pan
Explain the main component choices. The project favors a simple and verifiable prototype: Arduino control, TCS34725 RGB/C sensing, servo actuation, and LM2596 voltage regulation.

## Slide 7
System Architecture
Siqi Pan
One Arduino controller coordinates color sensing, servo motion, and the regulated 5 V power rail.
TCS34725 I2C
Arduino PWM
5-servo motion
LM2596 5 V rail
Unknown release
Notes: Speaker: Siqi Pan
Describe the system architecture. The 12 V input is regulated by the LM2596 to the 5 V rail. The Arduino reads the TCS34725 over I2C, drives the servos with PWM, and commands the final sorting action.

## Slide 8
Prototype Overview
Wu Xucheng
The final prototype integrates ball feeding, color sensing, servo sorting, and two collection bins.
Feeder
TCS34725 sensor
Servo arm
Output bin
End-to-end path
1
Feed
Vertical tube presents one ball.
2
Sense
Arm-mounted TCS34725 reads color.
3
Sort
Servo arm selects the output side.
4
Collect
Two bins separate the color classes.
Notes: Speaker: Wu Xucheng
Give a physical overview of the prototype. Point out the feeder tower, the TCS34725 sensor mounted under the receiving arm, the servo arm and gripper, and the two output bins. Keep this visual and concrete.

## Slide 9
Mechanical Structure
Wu Xucheng
Feeder tower
Guides the next ball toward the sensing and release region.
Arm + output bins
Servo arm opens the gripper after selecting the target side.
3D-printed mounts
Acrylic support
Notes: Speaker: Wu Xucheng
Explain the mechanical structure. The frame uses acrylic support and 3D-printed fixtures. The feeder guides balls toward the receiving and release region, and the arm plus gripper releases each ball into an output region.

## Slide 10
Feeder & Sorting Motion
Wu Xucheng
The verified sequence keeps the arm simple: feed, settle, rotate base, open gripper, close, and reset.
Servo mapping
D3
Base rotation
90 center; 45 one side; 135 other side
D4
Upper arm
Initialized and held for repeatability
D5
Forearm
Initialized and held for repeatability
D6
Gripper
100 closed; 45 open
D9
Feeder
Continuous rotation; run 510 ms then stop
1
Feed
D9 runs 510 ms
->
2
Settle
2 s wait
->
3
Classify
RGB/C rules
->
4
Release
Base + gripper
Primary mechanical limitation: single-ball feeding reliability.
Notes: Speaker: Wu Xucheng
Explain the servo roles. D3 rotates the base, D6 opens and closes the gripper, and D9 is the continuous-rotation feeder servo. Mention that the verified feeder command is 510 ms. End by foreshadowing the main mechanical limitation: single-ball feeding reliability.

## Slide 11
Sensor Placement & Calibration
Siqi Pan
The TCS34725 is mounted under the receiving arm, so each ball is read at a repeatable short distance.
TCS34725 under arm
Feeder
Gripper arm
Calibration logic
- Use fixed ball-sensor geometry
- Read raw R, G, B, and clear values
- Normalize as R/C, G/C, and B/C
- Tune thresholds under tested lighting
- Release unknown readings instead of forcing a bin
Why it matters: stable placement makes simple threshold rules reliable enough for the final demo.
Notes: Speaker: Siqi Pan
Explain the actual TCS34725 placement under the receiving arm. The point is that the ball is read at a repeatable short distance, which makes the simple threshold rules more reliable under the tested lighting.

## Slide 12
Color Sensor Design
Siqi Pan
The TCS34725 provides red, green, blue, and clear-channel readings over I2C.
TCS34725 RGB color sensor module
TCS34725 setup
- 50 ms integration time
- 4x gain
- Arduino reads raw R, G, B, C values
- Clear channel acts as brightness reference
R/C
G/C
B/C
C
Why ratios?
Normalizing RGB by the clear channel makes the rule less sensitive to absolute brightness and distance changes.
Notes: Speaker: Siqi Pan
Explain the TCS34725 color-sensing design. The sensor returns red, green, blue, and clear-channel readings. The clear channel is used as a brightness reference, so the software works with R/C, G/C, and B/C ratios rather than raw RGB alone.

## Slide 13
Classification Logic
Siqi Pan
The final Arduino logic uses threshold rules that were tuned for the tested lighting and sensor geometry.
Yellow/orange rule
R/C > G/C > B/C
and
R/C - B/C > 0.055
White rule
B/C - R/C > 0.20
and
G/C - R/C > 0.12
else
Unknown reading
wait briefly, open gripper once, close clamp
Code source: move.ino detectColor()
Notes: Speaker: Siqi Pan
Explain the classification thresholds. Yellow/orange has red greater than green greater than blue and enough red-blue separation. White has blue and green significantly higher than red in the tested geometry. Unknown readings are released instead of being forced into a color bin.

## Slide 14
Control Software Flow
Siqi Pan
Startup
Initialize TCS34725 and servos; move to ready pose and wait 5 s.
Cycle timing
Feeder runs 510 ms, then the ball settles for 2 s.
Decision
Run color thresholds, then actuate the matching sorting action.
Reset
Close gripper and return base servo to the center pose.
Notes: Speaker: Siqi Pan
Walk through the control software flow: initialize, set ready pose, run feeder, wait for settling, read color values, classify, actuate the correct sorting action, and reset. Mention that this flow is what the live demo will run.

## Slide 15
Power Wiring & Regulation
Zhonghao Wang
Servo transients made the regulated supply rail a first-order reliability concern.
12 V input
->
LM2596
regulated 5 V rail
->
Arduino
+ servos
Wiring and soldering
Power distribution was wired and debugged around the LM2596 rail to avoid servo-induced reset.
What mattered
Stable voltage under servo motion, no visible stall, and no controller reset during normal cycles.
Verification is separated from wiring: the next slides report measured voltage and sorting data.
Notes: Speaker: Siqi Pan
Explain the power wiring and regulation. Stable servo power was important because servo motion can cause voltage drops. The wiring and soldering route the 12 V source through the LM2596 to the regulated 5 V rail used by the controller and servos.

## Slide 16
Verification Setup
Zhonghao Wang
Testing measured the complete process, not only isolated color readings.
Five trials
Each trial: 5 yellow/orange + 5 white balls
Recorded for each run:
Sorting result
Correct / attempted balls
Run condition
Perfect, missed ball, or jam/assisted
Timing
10-ball completion time
Power rail
DMM voltage readings
End-to-end means feeder advance, settle, sensing, classification, actuation, and return to ready pose.
Notes: Speaker: Zhonghao Wang
Introduce the verification setup. The tests measured the whole sorting process, not only the sensor. Each of the five trials used five yellow/orange and five white balls, and the recorded data included sorting result, run condition, timing, and voltage.

## Slide 17
Trial-by-Trial Results
Zhonghao Wang
Each run used 10 balls: 5 yellow/orange and 5 white.
Run
Result
Time
Condition
Interpretation
1
10 / 10
71 s
Perfect
Fully completed and correctly sorted all balls.
2
10 / 10
71 s
Perfect
Repeatable timing and sorting behavior.
3
10 / 10
73 s
Perfect
Third complete autonomous 10/10 run.
4
10 / 10
79 s
Feeder jam / assisted
Sorted all balls after intervention; feeder reliability issue.
5
9 / 10
completed
One missed ball
Trial completed, but one ball was missed; not a color-threshold failure.
Summary: 4/5 trials completed without a jam, 3/5 were perfect 10/10, and 49/50 balls were correctly sorted.
Notes: Speaker: Zhonghao Wang
Present the trial-by-trial table. Emphasize that Runs 1 to 3 were perfect, Run 4 had a feeder jam but still sorted 10 out of 10 after intervention, and Run 5 completed without a jam but missed one ball.

## Slide 18
Sorting Accuracy & Timing
Zhonghao Wang
49 / 50
balls correctly sorted
4 / 5
completed without jam
3 / 5
perfect 10/10 trials
Trial summary: 3 perfect runs, 1 completed run with one missed ball, and 1 feeder jam that required intervention.
Notes: Speaker: Zhonghao Wang
Present the sorting and timing results. Three trials were perfect 10 out of 10 runs. One additional run completed without a jam but missed one ball, so it counts as completed but not perfect. One run had a feeder jam and required intervention. The total was 49 out of 50 balls correctly sorted.

## Slide 19
Power Verification
Zhonghao Wang
5.028 V
unloaded
5.008 V
idle
4.997 V
servo motion
Observed behavior
No controller reset, visible servo stall, or abnormal jitter in the measured normal-operation cases.
Measurement caveat
DMM readings do not capture very short transient dips; oscilloscope checks are future work.
Notes: Speaker: Zhonghao Wang
Present the power verification. The measured LM2596 output was 5.028 V unloaded, 5.008 V idle, and about 4.997 V during servo motion. In the measured cases there was no controller reset, visible stall, or abnormal jitter. Note the DMM transient limitation.

## Slide 20
Limitations, Future Work & Demo
Team
The prototype met the final requirements, with feeder reliability as the main remaining constraint.
Mechanical feeder
Jam in one run; one missed ball in another completed run.
Future: constrained single-ball escapement and better guide geometry.
Color sensing
Current thresholds worked under tested lighting.
Future: larger raw RGB/C dataset and controlled lighting tests.
Power rail
Steady DMM values were stable.
Future: oscilloscope validation for short servo transients.
Final takeaway: 49/50 balls were sorted correctly, with 4/5 trials completed without a jam and 3 perfect runs.
Notes: Speaker: Team
Close with limitations and future work. Wu can mention feeder redesign and the one jammed run, Zhonghao can mention the completed run with one missed ball and future oscilloscope checks, and Siqi can deliver the final takeaway. Transition directly into the live demo.

## Slide 21
Thanks for listening
Q&A
Automatic Sorting Robotic Arm for Table Tennis Balls
Team 50.2 | Siqi Pan | Zhonghao Wang | Xucheng Wu
Notes: Speaker: Team
Thank the audience and invite questions.