## Slide 1: Vision-driven Automatic Posture-Following Phone Stand
Group21
XiaoyuXu WeichongChen YilunChen

## Slide 2: Contents
1. Introduction & Objective
2. Review of original design
3. Components & Verification
4. Project Successes & Engineering Challenges
5. Extra Verifications & Robustness
6. Future Work
Group21 AutoFollowPhoneStand

## Slide 3: Introduction & Objective
Real-world Inconveniences of traditional phone stands:
Multitasking Limitations: Difficulties in viewing recipes or videos while cooking and moving around the kitchen.
Presentation Constraints: Awkwardness in manually adjusting phone angles when referencing digital notes during a speech or live stream.
Our Solution: An automatic, face-tracking phone stand that provides a seamless, hands-free viewing experience, ensuring the screen always aligns with the user's dynamic movements.
Group21 AutoFollowPhoneStand

## Slide 4: Review of Original Design
Demand changes:
Origin: Fixed height/angle to make user alternate themselves into the healthy posture.
Now: Will automatically alternate height and angle to meet the position of users to make them comfortable
Group21 AutoFollowPhoneStand

## Slide 5: Review of Original Design
Origin Block Diagram
New Block Diagram
Group21 AutoFollowPhoneStand

## Slide 6: Subsystem 1 -- Power System
Main Supply Input: 12V DC source to power high-torque actuators directly.
Voltage Regulation: DC-DC buck converter steps down 12V to stable 5V.
Power Distribution:
12V Rail: Dedicated to the stepper motor and linear actuator.
5V Rail: Powers the Raspberry Pi 4B logic and 74HCT244 level shifter.
Group21 AutoFollowPhoneStand

## Slide 7: Power System(cont')
Load Calculation（YilunChen)
12Voutput:
Maximum Power(W)=120
Maximum Current(A)=10
Estimated Power(W)=73
Estimated Current(A)=6.08
5Voutput:
Maximum Power(W)=25
Maximum Current(A)=5
Estimated Power(W)=tiny
Estimated Current(A)=tiny
Our 12V DC source and 12to5 convertor satisfy the demand.
Group21 AutoFollowPhoneStand

## Slide 8: Subsystem 2 -- Computer Vision & Signal Generation
Big Picture:
①Camera generates video stream
②RaspberryPi4B chip accepts video stream
via USB port ③The chip classifiy human face with Haar-Cascade classifier, generates a tuple(dx,dy) ④The chip generates a PWM/Dr/En signal ⑤GPIO output to motors
Group21 AutoFollowPhoneStand

## Slide 9: Computer Vision & Signal Generation
⭐Controller: Raspberry Pi 4B with 2GB DRAM
Low cost, easy deployment, universal support
⭐Vision: 1080P30FPS CMOS Camera MJPG stream
Low cost, sufficient for the mission
⭐Face Recognition: OpenCV-Haar-Cascade-Classifier
Lite version, low resource requirement(1GB)
⭐Controll: P-controll
Easy parameters, low sensitivity, higher stability
⭐GPIO output port: 3V3
Group21 AutoFollowPhoneStand

## Slide 10: The need for a voltage buffer chip
RPi-GPIO
UMIP42
⭐(Con't)GPIO output port: 3V3
⭐The pan motor( Umip42 step) fed with 5V PWM/Direction
Group21 AutoFollowPhoneStand
GPIO13
GPIO19
74HCT244
PWM+
DR+

## Slide 11: Subsystem 3 -- Sensor
⭐Vision Input: 1080P CMOS camera capturing real-time streams at 30 FPS.
⭐Pivoted to USB serial control for highly reliable actuation.
⭐Debuging commands: lsusb
⭐Device name: /dev/video0
Well Established device
⭐Causing troubles frequently due weak pin connection on board
Group21 AutoFollowPhoneStand

## Slide 12: Subsystem 4 -- Actuation
⭐Azimuth angle: 42mm stepper motor paired with worm-gear reduction.
⭐Height: 12V Linear Actuator driven by BTS7960 H-Bridge.
⭐Engineering Trade-off:
⭐Primitive Design: High-sensitive azimuth angle control caused severe vibration, while in real world filming and streaming, the camera should keep moving smoothly.
Group21 AutoFollowPhoneStand

## Slide 13: Actuation-UMIP42
⭐Manufacturers provided a driver that transfer PWM and DiRection(DR) signal to correct voltage output.
⭐Two ENable signals defaultly Not Connected. Lock motor when given one high and one low signal on two threads.
⭐DR+ controls the direction of the motor
⭐PWM+ controls motor speed via PWM frequency
⭐DR- an PWM- are grounded so that the driver could tell high signal from low.
⭐DR+ should be high 50μs earlier than risin edge of PWM+ signal.
Group21 AutoFollowPhoneStand
Motor Driver
PWM+
DR+
PWM-
DR-
EN+
EN-
GND
NC
NC
74HCT244

## Slide 14: Actuation-BTS7960 H-Bridge&Linear Acturator
⭐LPWM-LEN-RPWM-REN could detect 3V3-direct GPIO connection
⭐Motor Fed with 12V, but control unit use 5V
⭐Operates when both ENable signal is high
⭐Only detects the Duty Circle of the PWM signal
Differs from the UMIP42 motor
⭐IS returning signal could be up to 5V as VCC, which could not be accepted by GPIO input. 244 chip not sufficient. PCB under shipping-no handling
Group21 AutoFollowPhoneStand
BTS7960
LPWM
LEN
RPWM
REN
VCC
GND
5V
GND
RPi-GPIO
18
15
24
23
B+
B-
VCC
GND
12V
GND
Motor+
Motor-

## Slide 15: Components & Verification: Mechanical Structure
Base Support: 3D-printed H-section base which provides a low center of gravity to prevent tip-over.
Joint Connection: 3D-printed reinforced L-shaped bracket.
Secures the dual-axis (Pan & Tilt) integration.
Verification:
Stress testing confirmed zero structural deformation under the phone's weight.
Physical movements operated smoothly within the designated safety limits.
Group21 AutoFollowPhoneStand

## Slide 16: Main Structural Base
Foundational Anchor: Supports the entire mechatronic assembly and withstands up to a 2.0 kg cantilevered payload.
H-Section Profile for Weight Optimization: Hollowed side wings reduce material weight, while a solid 28mm center spine ensures maximum torsional rigidity.
Internal Channeling: Features an integrated 18mm center slot to discreetly house the linear actuator linkage, ensuring a compact and organized mechanical layout.
Group21 AutoFollowPhoneStand

## Slide 17: L-Shaped Motor Connector
Core Gimbal Interface: Bridges the horizontal pan stepper motor and the vertical pitch mechanism.
Structural Reinforcement: Incorporates a 90° corner gusset and 2.0mm filleted mounting ears to dissipate stress and prevent fatigue-induced cracking under high torque.
Precision & Assembly Tolerance: Features a dedicated motor recess for perfect shaft alignment, along with elongated slotted holes to accommodate manufacturing tolerances and allow fine-tuned adjustments during assembly.
Group21 AutoFollowPhoneStand

## Slide 18: Project Successes & Engineering Challenges
Success
Achieved stable end-to-end tracking latency of < 400 ms.
Successfully isolated high-power motor noise from the 5V logic circuit.
Passed all critical safety verifications
Group21 AutoFollowPhoneStand

## Slide 19: Project Successes & Engineering Challenges
Challenges & Engineering Hindsight
Mechanical: Assembly Clearance (DFA Oversight)
Issue: Fastening screws for the guide rail on the 3D-printed base was physically impossible.
Engineering Reason: Design for Assembly (DFA) failure. The CAD model lacked sufficient spatial tolerance for tool paths (screwdrivers) and manual access.
Software: Asymmetric Control Kinematics
Issue: Integrating horizontal panning and vertical pitching simultaneously was highly unstable.
Engineering Reason: Mismatched control domains. The stepper motor requires discrete angular mapping (Step/Dir pulses), whereas the linear actuator uses time-based, continuous PWM mapping via the H-bridge.
Group21 AutoFollowPhoneStand

## Slide 20: Extra Verifications & Robustness
Multi-Face Edge Case: Prioritizes the largest bounding box area.
Vision Result: Ensures stable tracking with zero motor oscillation in crowded views.
Extreme Payload Test: Tested with 5kg mass to verify high torque margin.
Mechanical Result: No oscillation and component deformation for standard smartphones via worm-gear and actuator thrust.
Group21 AutoFollowPhoneStand

## Slide 21: Future Work
Live Commerce Kit
We plan to integrate an adaptive LED ring light and a microphone mount to expand the commercial potential in the live-streaming industry. The Raspberry Pi will automatically adjust the light's brightness and color temperature via PWM signals based on the ambient lighting captured by the camera. This ensures the user's face remains perfectly illuminated while they are moving around or demonstrating products.
Group21 AutoFollowPhoneStand

## Slide 22: Future Work
Advanced AI & Gestures
Future systems will upgrade to lightweight deep-learning models like MediaPipe to enhance tracking stability in extreme low-light conditions. This upgrade will also unlock hand gesture recognition, significantly improving the touch-free interactive experience. For example, a user can simply open their palm to the camera to pause the tracking, allowing them to hold a product steady in the frame.
Group21 AutoFollowPhoneStand

## Slide 23: Thank you！
Group21 AutoFollowPhoneStand