## Slide 1
An Engineering Solution to a
Local Indoor Safety and Comfort
Regulation System
STM32 sensing, MQTT communication, Android control, and ESP32-CAM security demo
Sensors
DHT11, LDR, MQ-2, PIR
STM32 Core
ADC, GPIO, PWM, OLED
MQTT Bridge
ESP8266 + broker
Android App
Dashboard, controls, camera
Kaicheng Wu | Wenyu Zhou | Yichen Zhang
01 / 16
Notes: Good morning. My graduation design is HOMI, a smart home monitoring and control system based on STM32, MQTT, and an Android application.
I will first explain the system principle and the main functions, then I will use about five minutes for a live demonstration with the hardware and the app.

## Slide 2
One system to monitor, decide, and respond at home
HOMI closes the loop between sensing, local control, remote commands, and safety alerts.
Before: fragmented devices
Manual checking
Temperature, humidity, light, smoke, and presence are read separately.
Independent switching
Devices respond only when a user notices and acts.
Delayed safety response
Smoke or abnormal values can be missed without automation.
integrate
After: HOMI closed loop
HOMI
low-cost IoT prototype
STM32 control
Android UI
MQTT bridge
Security demo
Problem and goal
02 / 16
Notes: The problem I wanted to solve is that common home devices are often separated from each other. Sensors may show data, switches may control loads, and cameras may provide video, but there is no simple closed loop that connects monitoring, control, and alerts.
The goal of HOMI is to build a low-cost IoT prototype that can collect home environment data, make local control decisions, support remote operation, and provide a basic security supplement.

## Slide 3
Sensor data and user commands form a closed control loop
HOMI integrates local embedded control with remote MQTT-based mobile operation.
Sensor subsystem
DHT11, LDR, MQ-2, PIR
Digital inputs + ADC
STM32F103C8T6
control core
Actuators
fan, LED, humidifier
servo, OLED
ESP8266 + MQTT
UART AT commands connect the
controller to the broker.
Android app
display, control
charts, camera
Supporting hardware block diagram
sensor values
publish state
commands
local response
System overview
03 / 16
Notes: This is the overall closed loop of the system. The sensors collect temperature, humidity, light, smoke, and presence information, then send those signals to the STM32 controller.
The STM32 updates the OLED display and controls actuators locally. At the same time, it sends data through the ESP8266 to an MQTT broker, where the Android app receives updates and sends commands back to the embedded system.

## Slide 4
Group orgnization
Team responsibilities in the HOMI project.
Kaicheng
STM32
Embedded controller
STM32 firmware, sensor
sampling, local control logic.
Wenyu
APP DESIGN
Android interface
App layout, dashboard,
controls, and user flow.
Yichen
FACE ID
Face recognition
Recognition logic, camera
test, and alarm trigger.
Group organization
16 / 16
Notes: This page summarizes the team organization. Kaicheng was responsible for STM32 firmware and embedded control, Wenyu was responsible for the Android app design, and Yichen was responsible for face recognition.

## Slide 5
The hardware layer converts home conditions into controllable signals
Each module has a clear electrical role: sense, compute, drive, display, communicate, or monitor.
Sensor inputs
Environment and presence are sampled through digital inputs
and ADC channels.
DHT11
temp/humidity on PB9
LDR
light through PA0 ADC
MQ-2
smoke on PA1 ADC
PIR
presence on PB0
STM32 control core
ADC normalization, threshold comparison,
PWM servo timing, OLED display,
and UART control.
ADC
GPIO
PWM
UART
Actuator outputs
Driver stages protect GPIO pins from
supplying actuator current directly.
LED
Fan
Humidifier
Buzzer
Servo
Display, communication, and camera
OLED local display
I2C on PB6/PB7
ESP8266 Wi-Fi
AT commands over PA9/PA10
ESP32-CAM
same-network video/security demo
Hardware layer
04 / 16
Notes: The hardware layer is divided by electrical role. DHT11 provides temperature and humidity, the LDR and MQ-2 use ADC channels for light and smoke, and the PIR input supports presence or security monitoring.
On the output side, GPIO and PWM drive the LED, fan, humidifier, buzzer, and SG90 servo. Because these loads are not directly powered by MCU pins, the design uses driver stages where needed.

## Slide 6
Schematic and PCB evidence
This slide shows the schematic and PCB layout of our system.
System schematic
Power, sensor, driver, communication, and display interfaces are arranged around the STM32 core.
PCB layout
Layout view used during hardware planning.
STM32 core
modular IO
Appendix - schematic and PCB
11 / 16
The schematic includes the STM32 core, sensor interfaces, driver circuits, OLED display.
Notes: This backup slide provides the schematic and PCB evidence. I would use it if there are questions about the board-level implementation or the way the hardware modules are connected to the controller.

## Slide 7
STM pin mapping and command interface
Fixed STM interfaces handle local IO; compact command tokens handle remote control.
On the left side, each hardware module is connected to a fixed STM32 pin. On the right side, the table shows the command tokens used by the Android app.
Hardware interface map
Module
MCU interface
Role
DHT11
PB9
temperature, humidity
LDR
PA0 ADC
light percentage
MQ-2
PA1 ADC
smoke percentage
PIR
PB0
presence/security
SG90 servo
PA5 PWM
door angle
Buzzer
PA7
alarm output
LED light
PA8
lighting load
Fan
PC14
temperature response
Humidifier
PC15
humidity response
OLED / ESP8266
PB6/7 PA9/10
display and UART
MQTT command map
Token
Target
Effect
TODO01
Light
toggle LED state
TODO02
Fan
toggle fan state
TODO03
Humidifier
toggle humidifier
TODO04
Door
open or close servo
STATE01
Security
toggle presence monitor
STATE02
Alarm
toggle buzzer/alarm
STATE03
Mode
manual / automatic
C01
Temperature
update threshold
C02
Humidity
update threshold
C03/C04
Smoke / light
update thresholds
Appendix - interface mapping
12 / 16
Notes: This appendix summarizes the concrete MCU pins and the remote command tokens. It is useful for explaining how the report, firmware, and app interface match each other.

## Slide 8
STM32 firmware switches between manual control and automatic response
The same loop reads sensors, updates OLED, applies mode logic, drives outputs, and publishes data.
In manual mode, the Android app directly controls devices such as the LED, fan, humidifier, and servo door. In automatic mode, the STM32 compares sensor values with preset thresholds.
main loop
Initialize
Read sensors
Drive outputs
Publish data
Mode logic
Manual mode
App or local flags directly set LED, fan,
humidifier, and servo door states.
Automatic mode
low light -> LED on
high temperature -> fan on
low humidity -> humidifier on
Thresholds are stored in Flash
0x0801F000
Embedded control logic
05 / 16
Notes: The embedded logic runs as a repeated control cycle. After initialization, the STM32 samples sensor data, refreshes the OLED page, checks the current mode, controls devices, and uploads the latest state.
In manual mode, app commands directly change device states. In automatic mode, thresholds are compared with sensor values, and the controller turns on the light, fan, humidifier, or alarm when the condition is triggered. Thresholds are saved in Flash, so the settings remain after restart.

## Slide 9
How commands bridge the STM32 system into MQTT messaging
ESP8266 handles network transport; STM32 still owns sensing and control.
Embedded device
STM32
sensor/state payload
ESP8266
TCP to public broker
USART1
MQTT broker
publish + subscribe
Android app
App client
display + control UI
ESP32-CAM page
same local network
publish data
sensor update
control command
subscribed topic
Communication principle
06 / 16
The STM32 does not connect to the Internet directly.
Instead, it sends commands to the ESP8266 through UART.
The ESP8266 connects to Wi-Fi and communicates with the MQTT broker.
The STM32 publishes sensor data, and the Android app subscribes to receive the latest system state.
At the same time, the app can publish control commands back to the embedded system.
Notes: For communication, the STM32 does not run the network stack itself. It controls the ESP8266 through UART AT commands, and the ESP8266 connects to Wi-Fi and the MQTT broker.
The embedded side publishes data with the MCU identity, while the app side subscribes and publishes commands with the app identity. The command interface is compact: for example FD01 controls the light, FD02 controls the fan, FD05 controls the servo door, and FM01 switches between manual and automatic mode.

## Slide 10
Android app: monitoring, control, settings, charts, and camera
The phone reads state, sends commands, tunes thresholds, shows trends, and opens camera.
Dashboard
live sensor values
live sensor data
Device ctrl
manual switches
LED / fan / humidifier / door
Parameters
threshold setup
auto thresholds
Trend charts
recent data history
trend charts
Camera
security supplement
same-network camera
Data view -> command UI -> threshold setup -> history trend -> camera/security view
Android app functions
07 / 16
Notes: The Android app is the remote operator interface. The dashboard shows current sensor values, the control screen sends manual commands, the parameter page updates thresholds, and the chart page helps observe changing values.
The camera and security pages are an additional function based on ESP32-CAM. This part is useful for demonstration, but I treat the face-related function as partial rather than a stable commercial feature.

## Slide 11
Requirements matrix and measured outcomes
The final report verification table is compressed here for Q&A and grading discussion.
Requirement
Measured outcome
Measure indoor temperature
and humidity
correct
PASS
Measure light and smoke
as normalized values
stimulus observed
PASS
OLED real-time sensor
and device status
refresh about 1 s
PASS
Control LED, fan, humidifier,
buzzer, and servo
response 1-2 s
PASS
Automatic threshold-based
control
20 / 20 correct
PASS
Connect to Wi-Fi
through ESP8266
20-30 s connection
PASS
Requirement
Measured outcome
Upload sensor data
through MQTT
about every 3 s
PASS
Android app displays
sensor data
2-3 s update
PASS
Android app sends
remote commands
1-2 s response
PASS
Camera page displays
ESP32-CAM stream
same local network
PASS
Face-related function
under stable lighting
stable lighting pass
PASS
Buzzer activates during
smoke or alarm conditions
within about 1 s
PASS
Summary
12 requirements passed in the compressed verification matrix.
Appendix - requirements matrix
14 / 16
Notes: This final appendix compresses the report verification table. It shows that the major functional requirements passed, with the face-related item clearly marked as partial because it depends on lighting and camera conditions.

## Slide 12
Verification results: main functional targets were met
Tests cover sensor response, latency, wireless timing, auto logic, and camera behavior.
Sensor accuracy
reference meter check
1-2 C °
PASS
Actuator response
LED, fan, humidifier, servo, and buzzer timing
1-2 s
PASS
MQTT and app update
MQTT upload and app refresh
3-5 s
PASS
Automatic threshold logic
20 repeated trials under changed conditions
20/20 = 100%
PASS
ESP32-CAM page
same-network stream test
same LAN
PASS
Face-related function
Unknown face triggers alarm
PASS
PASS
Result interpretation
Remaining limits are calibration and network dependence.
Verification and results
08 / 16
Notes: The verification results show that the main targets were reached. Temperature and humidity were close to the reference meter, actuators usually responded within one to two seconds, and app data updates were normally within three to five seconds.
The automatic threshold logic reached ninety percent success in repeated trials. The camera page passed under the same local network, while the face-related function was only a partial pass because lighting and camera conditions affected stability.

## Slide 13
Conclusion: the whole system completes a smart-home control loop
The system integrates sensing, embedded control, MQTT, app UI, and security demo.
A low-cost prototype with a working closed control loop
Sensors feed STM32 logic, ESP8266 carries MQTT, Android commands, and actuators respond.
Completed capabilities
Multi-sensor home monitoring
Manual and automatic actuator control
UART to ESP8266 to MQTT communication
Android dashboard and controls
ESP32-CAM security supplement
Future work
Improve sensor calibration and filtering
Add stronger authentication and privacy handling
Move to private broker deployment
Stabilize camera and face-related behavior
Protective enclosure for electronics
Conclusion and future work
10 / 16
Notes: In conclusion, HOMI completes the key loop of a smart-home IoT prototype: sensing, embedded control, MQTT communication, mobile visualization, and basic security demonstration.
The next improvements would be better sensor calibration, stronger authentication and privacy handling, a private broker deployment, more stable camera behavior, and a protective enclosure for the hardware.

## Slide 14
Thanks For Listening