## Slide 1
ECE 445 SENIOR DESIGN
Guided Robotic Manipulator for Chinese Calligraphy
A low-cost system that converts static character images into brush motion through a neural path planner and a three-axis lead-screw gantry.
group 8
Team: Nuoer Huang, Xinyi Shen, Xirui Yao, Yujie Wei
May 23, 2026
01

## Slide 2
PROBLEM FRAMING
The real challenge is not drawing a character. It is reproducing stroke order, pressure, and repeatability on paper
Why existing approaches fall short
Most low-cost calligraphy robots only trace 2D outlines. They miss dynamic brush behaviors such as lifting, pressing, and pausing, while many higher-end systems depend on expensive commercial robotic arms and large expert-labeled datasets.
Objective
The primary objective of this project is to develop a low-cost, Arduino Mega 2560-based three-axis robotic system for automated calligraphy creation. The system aims to achieve high-fidelity writing and maintain traditional stroke styles by using a deep learning pipeline to translate static character images into precise mechanical displacements.
02
Introduction
Traditional Chinese calligraphy relies on the precise coordination of stroke sequence, velocity, and pressure, making its robotic replication a complex multi-disciplinary engineering challenge. This project bridges the gap between AI-driven computer vision and physical mechatronic execution by combining a trajectory-extracting neural network with a 3-axis Cartesian plotter.
Notes: Most people think the main challenge of robotic calligraphy is just drawing the outline of a character.But the real hurdle it’s about reproducing the stroke order, the pressure variations, and consistent, repeatable results on actual paper."
For example, if we want to draw a horizontal line, we need to press down at the start, lift the pen slightly, then move slowly to the right, and finally lift the pen and pull it back a little.
Most low-cost calligraphy robots only trace basic 2D outlines. They completely miss the dynamic behaviors that make calligraphy come alive—things like lifting the brush, pressing down, and pausing at key points.On the other end of the spectrum, high-end systems rely on expensive commercial robotic arms and massive expert-labeled datasets. They work, but they’re neither accessible nor scalable for everyday use.

## Slide 3
SYSTEM ARCHITECTURE
The system is a four-stage chain from character image to brush stroke
03
Notes: This is the full workflow of our system. The process starts with a user’s calligraphy image as the input. In the offline processing stage, the system extracts the character structure and generates a Bézier-curve-based writing trajectory. Then, a reinforcement-learning-based brush simulation environment helps refine the trajectory into 3D coordinates, including the X-Y writing path and Z-axis brush movement.
These coordinates are then passed into the online control stage. The system converts the trajectory into G-code, which is transmitted to the Arduino Mega 2560 and RAMPS 1.4 hardware setup. With Marlin firmware, the G-code is translated into specific stepper motor actions.
At the final stage, the physical manipulator executes the writing task. The gantry structure moves the brush along the X and Y axes, while the Z axis adjusts the brush pressure on the paper. Overall, this architecture connects visual input, trajectory planning, control firmware, and physical calligraphy execution into one complete robotic writing pipeline.

## Slide 4
Mechanical System
Physical framework design for the mechanical system is shown as follows
04
Structure:3-axis Cartesian gantry withlead screwdrive for high torque and stability.
Motors:Three NEMA 17 stepper motors.
Drivers:Three A4988 drivers in 1/16 microstepping mode
The frame is constructed from aluminum
The working envelope of the platform is 300 mm×300 mm×165 mm (X × Y × Z), sufficient for standard calligraphy paper sizes up to A5
Notes: This is the physical framework of our mechanical system. Our manipulator is designed as a three-axis Cartesian gantr system, which is similar to the motion structure of a desktop 3D printer. The X and Y axes control the horizontal movement of the brush across the writing plane, while the Z axis controls the vertical movement of the brush, including contact and pressure on the paper.
For the mechanical transmission, we use lead screw drives to provide higher torque, better stability, and more precise positioning. The whole frame is constructed from aluminum profiles, which makes the structure lightweight but rigid enough for repeated writing motion.
The system is driven by three NEMA 17 stepper motors, one for each axis. Each motor is controlled by an A4988 stepper driver, configured with 1/16 microstepping mode. This allows smoother motion and finer position control, which is important for calligraphy stroke execution.
The working area of the platform is approximately 200 by 300 by 165 millimeters in X, Y, and Z directions. Overall, the mechanical system provides a stable and controllable platform for converting the planned digital trajectory into physical brush movement.

## Slide 5
Contrlol System
Integrating hardware devices and Marlin-based firmware for G-code interpretation and motion control
05
Hardware Device
Arduino Mega 2560 + RAMPS 1.4 are used as the main control hardware.
The Arduino receives G-code commands via serial communication.
RAMPS 1.4 interfaces with the stepper drivers, motors, power supply, and limit switches.
Limit switches define the machine home position (0, 0, 0).
They also provide minimum axis boundaries for safe initialization and motion control.
Marlin Framework
Marlin is used as the firmware layer between G-code commands and physical motor motion.
It interprets commands such as position, speed, and Z-axis movement.
The firmware converts G-code into step/direction signals for the stepper drivers.
It controls coordinated motion along the X, Y, and Z axes.
manages homing, limit switch feedback, acceleration, and motion safety.
This allows the brush end-effector to follow the planned calligraphy trajectory accurately.
Notes: Our control system uses an Arduino Mega 2560 together with a RAMPS 1.4 shield as the main hardware controller. The Arduino receives G-code commands from the host computer through serial communication and converts them into motion control signals for the stepper motors. The RAMPS 1.4 board serves as the interface between the microcontroller, stepper drivers, motors, power supply, and limit switches. Limit switches are installed on each axis to define the machine’s home position (0, 0, 0) and provide minimum travel boundaries, ensuring that the system can initialize its coordinate space safely before physical execution.
In our control system, Marlin acts as the motion-control firmware. It receives G-code from the Arduino Mega 2560 and translates each command into specific motor actions. Marlin also handles homing through the limit switches, acceleration control, and movement constraints, so the robotic manipulator can execute the planned writing path in a stable and repeatable way.

## Slide 6
USER INTERFACE
The UI covers both generation and machine execution, not just parameter entry.
Generation inputs
Text, font, model, output path, spacing, origin, and pen heights are all editable in the UI.
Main generation panel
Send-to-machine panel
06
Validation + debug
The code checks empty inputs and missing font files, then surfaces the command, stdout, and stderr.
Machine send controls
Serial port, baudrate, dry run, progress, pause, resume, stop, current line, and log output are built in.
Notes: We have a user interface to control the whole pipeli
The UI is not only used for entering parameters. It covers both G-code generation and machine execution.
On the left, the main generation panel allows the user to enter text, choose the font and model, set the output path, and adjust layout parameters such as character spacing, origin, and pen heights.
On the right, the send-to-machine panel allows the user to select the serial port and baudrate, run dry-run tests, and send G-code to the machine.
The UI also includes validation and debugging information. It checks invalid inputs, missing font files, and displays command output, standard output, and error logs.

## Slide 7
SOFTWARE WORKFLOW
Chinese character / font → PNG rendering → CalliRewrite inference → NPZ trajectory file → G-code generation → UI / serial transmission
STEP1: Character Image Generation
The system takes a Chinese character and a font file and generates a 256×256 black-and-white PNG image.
STEP3: Simulation Finetuning
The stroke trajectory goes into a simulation environment and do the RL finetuning to make the stroke trajectory more smooth.
STEP4: NPZ to G-code Conversion
The NPZ file stores coarse stroke data, including pen states and Bézier curve parameters. The converter reconstructs each stroke as a 2D trajectory, samples the Bézier curves into discrete XY points, scales the image-space coordinates into millimeter-based machine coordinates, and maps pen-up / pen-down states to Z-axis heights. Finally, the trajectory is written as standard G-code using G0/G1 commands.
STEP5: Multi-character Layout
x_offset = col × char_spacing
y_offset = -row × line_spacing
07
STEP6: Serial Communication
The module reads the G-code file line by line, removes comments and blank lines, sends one command at a time through the serial port, and waits for Marlin to return “ok” before sending the next command.
[1] Y. Luo, Z. Wu, and Z. Lian, “CalliRewrite: Recovering Handwriting Behaviors from Calligraphy Images without Supervision,” arXiv preprint arXiv:2405.15776, 2024. [Online]. Available: https://arxiv.org/pdf/2405.15776v1. [Accessed: Apr. 8, 2026].
STEP2:CalliRewrite Integration
The project mainly uses CalliRewrite’s coarse sequence extraction stage to convert a static glyph image into a stroke trajectory.
Notes: For the software workflow, our goal is to convert Chinese text input into executable G-code for the writing machine.
The pipeline starts from a Chinese character and a selected font. The character is rendered into a 256 by 256 PNG image. Then, we use CalliRewrite to extract a coarse stroke trajectory from the image. The output is stored as an NPZ trajectory file.
Next, our converter reconstructs the trajectory, samples the stroke curves, maps image coordinates into millimeter-based machine coordinates, and generates G-code. For multiple characters, we apply layout offsets at the G-code level.
Finally, the generated G-code can be sent to the Mega2560 through serial communication.

## Slide 8
Software Verification Table
08
Requirement | Verification | Status
The software shall render a user-selected Chinese character and font into a 256 × 256 PNG image. | Input a test character such as 木 with simkai.ttf. Confirm that the generated PNG exists and visually matches the selected character and font. | Verified
The software shall call CalliRewrite and generate a corresponding .npz trajectory file. | Run the pipeline with python ./test.py --input my_imgs --model new_train_phase_2 and confirm that the expected .npz file is generated in the tools/ directory. | Verified
The software shall convert the .npz trajectory into machine-executable G-code. | Run npz_to_gcode.py and inspect the generated G-code for valid commands such as G21, G90, G28, G0, G1, XY motion commands, and Z-axis pen-up/pen-down commands. | Verified
The software shall support multi-character writing through G-code-level layout. | Input a string such as 木林森, confirm that each character is processed separately, and verify that the final merged G-code applies correct X/Y offsets without repeated G28 commands. | Verified
The UI shall allow the user to generate and optionally send G-code to the machine safely. | Use the Streamlit UI to generate G-code, confirm that the output path and previews are displayed, run serial dry-run successfully, and verify that real sending only occurs after the user explicitly clicks the send button. | Verified
Notes: This table summarizes the main software verification results.
First, we verified that the software can render Chinese characters and fonts into PNG images. Then, we confirmed that CalliRewrite can generate the corresponding NPZ trajectory files.
Next, we verified that the NPZ files can be converted into valid G-code with XY movement and Z-axis pen-up and pen-down commands.
For multi-character writing, we checked that each character is processed separately, and the final merged G-code applies correct layout offsets without repeated homing commands.
Finally, we verified the UI and serial sending process. The UI can generate G-code, display previews, perform dry-run tests, and only sends commands after the user explicitly clicks the send button. All key software requirements were verified.

## Slide 9
CONCLUSION
The project proves that AI-guided calligraphy can be implemented on a low-cost, student-built mechatronic platform.
What the team accomplished
Built a lead-screw XYZ gantry that achieved ±0.5 mm accuracy.
Integrated neural stroke extraction, RL-based refinement, G-code generation, and UI control.
Verified homing, communication behavior, and frame stiffness.
Demonstrated that the software and hardware can form one usable calligraphy pipeline.
Most credible future work
Closed-loop control with encoders or camera feedback.
Automatic ink dipping for longer writing sessions.
Spring-loaded or quick-change brush holder for more consistent pressure.
Better damping and lower-wear lead-screw nut materials for lifetime reliability.
09
¥289.58
COST

## Slide 10
VIDEO
10

## Slide 11
THANKS FOR LISTENING
Q&A
08
group 8 Nuoer Huang, Xinyi Shen, Xirui Yao, Yujie Wei