## Slide 1: A World-Model based Infant InteractionRobot
ECE 445 Senior Design Project​
Team #44​
Zishuo Feng (ECE)​
Artha Amanda Sidauruk (ECE) ​
Sylvia Chung Yan Shan (ECE) ​
Ruijin Xu (EE)​
May 2026​
ZJU-UIUC Institute, Zhejiang University, China

## Slide 2: Contents
ZJUI
Project Motivation
System Architecture
Hardware Design
Software & Control
AI Voice Interaction
Verification & Experimental Results
Limitations & Future Work
Conclusion
Demonstration Video

## Slide 3: Project Motivation
ZJUI
Design a safe and engaging robot for infant-oriented interaction
Encourage crawling, chasing, and playful movement through autonomous response
Combine embedded motion control with voice-based AI interaction
Use a low-cost platform while maintaining smooth and safe behavior

## Slide 4: System Architecture​
ZJUI
Two main layers: control/computation and robot hardware.
The ESP32 coordinates sensing, motor control, and interaction behavior.
The platform integrates motion, AI interaction, and power management.

## Slide 5: System Architecture (Detailed)​
ZJUI
Power is distributed to the motion and interaction subsystems.
Sensor data flows to the controller, which generates motion and interaction signals.
A shared ground improves stable operation across all subsystems.

## Slide 6: Hardware Design
ZJUI
Hardware subsystem overview:​
Main Controller: ESP32 DevKit / ESP32-WROOM-32 for reading sensor inputs,generating PWM/GPIO motor-control signals,and coordinating reactive safety logic. ​
Power Subsystem: MB-102 power supplymodule provides selectable 5 V / 3.3 V rails forthe ESP32 and peripheral modules. ​
Motion & Driving Subsystem: TB6612FNGmotor driver controls the dual DC motors andsupports 2WD chassis movement. ​
Sensing Subsystem: HC-SR501 PIR motionsensor detects human/infant motion, while theGP2Y0A21YK0F infrared distance sensormeasures nearby distance for safer avoidancebehavior. ​
AI Voice Interaction Subsystem: INMP441MEMS microphone captures user voice input,and the MAX98357A I2S amplifier drives thespeaker for voice responses and sound effects. ​

## Slide 7: Hardware Components​
ZJUI

## Slide 8: Hardware Components​
ZJUI

## Slide 9: Hardware Components​
ZJUI

## Slide 10: Motion system Control​
ZJUI
Design Goals
👀
Observe safely
Continuously checks human presence and close obstacles before moving.
🤖
Engage gently
Moves forward only after a safety recovery condition, using low speed.
🛡️
Escape / stop
Reverses or turns away when PIR or IR sensors detect risk.
Design principle: the robot should be safe and engaging .
🛡️
safetyTask
Higher priority: reads PIR/IR, decides next state, writes command.
⚙️
motionTask
Lower priority: reads command, computes PWM, writes motors.
Shared Command State

## Slide 11: Algorithm Pipeline​
ZJUI
📡
Sensors
PIR left/right + Sharp IR distance
🧠
Safety Task
Priority logic selects IDLE / ESCAPE / ESTOP / ENGAGE
🔒
Command State
Shared structure with state, motion, linear, angular
⚙️
Motion Task
Clamps velocities, computes differential drive, ramps PWM
🛞
Motors
TB6612FNG driver sends left/right wheel outputs
ESP32 Controller Code

## Slide 12: Sensors​
ZJUI

## Slide 13: States and Logic
ZJUI
Four states
IDLE
No movement
ENGAGE
Slow forward
ESCAPE
Avoid / reverse
ESTOP
Emergency reverse
04
Safety Priority Logic
Priority
Trigger
State
Command
1
Both PIR active
ESTOP
Backward −0.25
2
Left PIR active
ESCAPE
Reverse + turn away
3
Right PIR active
ESCAPE
Reverse + turn away
4
Left IR obstacle
ESCAPE
Turn right
5
Right IR obstacle
ESCAPE
Turn left
6
No risk after escape
ENGAGE
Forward +0.05
Why priority matters
Human proximity overrides obstacle avoidance, and emergency behavior overrides engagement.

## Slide 14: AI Voice Interaction​
ZJUI
ESP32-based XiaoZhi AI voiceassistant enables real-time voiceinteraction.​
ESP32 connects to Wi-Fi for cloud-assisted speech processing andresponse generation.​
INMP441 I2S microphone capturesuser speech input.​
MAX98357A amplifier and speakeroutput the AI voice response.​
OLED displays pairing status andreal-time conversation text.​
The AI platform supports open-ended conversations, but wecustomized the chatbot as “Bobo,” afriendly bunny companion, to keepresponses simple, positive, andchild-safe.​

## Slide 15: Verification & Experimental Results​
ZJUI
The prototype was verified through staged testing, from individual modules to full-system operation.
Motion control passed: ESP32 booted successfully and executed forward, backward, turning, and stop commands.
Reactive behavior passed: PIR detection triggered the expected avoidance responses: turn away or back up.
Safety functions passed: timeout stop and emergency stop reliably halted the robot during testing.
AI voice interaction passed: XiaoZhi setup, Wi-Fi connection, microphone input, and speaker output were successfully verified.
System integration passed: sensing, motion, power, and voice interaction operated together as a complete infant-interaction robot.
Result: The final prototype met all defined functional requirements and demonstrated safe reactive movement with voice-based engagement.

## Slide 16: Limitations and Future Works
ZJUI

## Slide 17: Conclusion
ZJUI
We developed a functional prototype of an infant interaction roboton a low-cost embedded platform.​
The system integrates sensing, motion control, AI voice interaction,and safety-oriented behavior.​
Experimental verification showed reliable reactive motion andsuccessful voice-based interaction.​
This project provides a strong foundation for future intelligent child-robot interaction systems.​

## Slide 18: Demonstration Video
ZJUI

## Slide 19: Questions & Discussion​
ZJUI
Thank You!