## Slide 1: ECE 576 – Power System Dynamics and Stability
Prof. Tom Overbye
Dept. of Electrical and Computer Engineering
University of Illinois at Urbana-Champaign
overbye@illinois.edu
Lecture 13: Exciters, Block Diagrams

## Slide 2: Announcements
Homework 4 is on the website and is due March 6
Read Chapter 4
Midterm exam is on March 13 in class
  Closed book, closed notes
  You may bring one 8.5 by 11" note sheet
    You do not have to write down model block diagram or the synchronous machine differential equations – I'll supply those if needed
  Simple calculators allowed

## Slide 3: IEEE T1 Exciter
This model was standardized in the 1968 IEEE Committee Paper with Fig 1 shown below

## Slide 4: IEEE T1 Evolution
This model has been subsequently modified over the years, called the DC1 in a 1981 IEEE paper (modeled as the EXDC1 in stability packages)
Image Source: Fig 3 of "Excitation System Models for Power Stability Studies," IEEE Trans. Power App. and Syst., vol. PAS-100, pp. 494-509, February 1981
Note, KE in the feedback is the same as the 1968
approach

## Slide 5: IEEE T1 Evolution
In 1992 IEEE Std 421.5-1992 slightly modified it, calling it the DC1A (modeled as ESDC1A)
Image Source: Fig 3 of IEEE Std 421.5-1992
VUEL is a signal from an under- excitation limiter, which we'll cover later
Same model is in 421.5-2005

## Slide 6: Initialization and Coding: Block Diagram Basics
To simulate a model represented as a block diagram, the equations need to be represented as a set of first order differential equations
Also the initial state variable and reference values need to be determined
Next several slides quickly cover the standard block diagram elements

## Slide 7: Integrator Block
Equation for an integrator with u as an input and y as an output is
In steady-state with an initial output of y0, the initial state is y0 and the initial input is zero
u
y

## Slide 8: First Order Lag Block
u
y
Equation with u as an input and y as an output is
In steady-state with an initial output of y0, the initial state is y0 and the initial input is y0/K
Commonly used for measurement delay (e.g., TR block with IEEE T1)
Output of Lag Block
Input

## Slide 9: Derivative Block
Block takes the derivative of the input, with scaling KD and a first order lag with TD
  Physically we can't take the derivative without some lag
In steady-state the output of the block is zero
State equations require a more general approach
u
y

## Slide 10: State Equations for More Complicated Functions
There is not a unique way of obtaining state equations for more complicated functions with a general form
To be physically realizable we need n >= m

## Slide 11: General Block Diagram Approach
One integration approach is illustrated in the below block diagram
Image source: W.L. Brogan, Modern Control Theory, Prentice Hall, 1991, Figure 3.7

## Slide 12: Derivative Example
Write in form
Hence b0=0, b1=KD/TD, a0=1/TD
Define single state variable x, then
Initial value of x is found by recognizing y is zero so x = -b1u

## Slide 13: Lead-Lag Block
In exciters such as the EXDC1 the lead-lag block is used to model time constants inherent in the exciter; the values are often zero (or equivalently equal)
In steady-state the input is equal to the output
To get equations write in form with b0=1/TB, b1=TA/TB, a0=1/TB
u
y
Output of Lead/Lag
input

## Slide 14: Lead-Lag Block
The equations are with then
b0=1/TB, b1=TA/TB, a0=1/TB
The steady-state requirement that u = y is readily apparent

## Slide 15: Limits: Windup versus Nonwindup
When there is integration, how limits are enforced can have a major impact on simulation results
Two major flavors: windup and non-windup
Windup limit for an integrator block
If Lmin  v  Lmax then y = v
else If v < Lmin then y = Lmin, else if v > Lmax then y = Lmax
u
y
Lmax
Lmin
v
The value of v is NOT limited, so its value can "windup" beyond the limits, delaying backing off of the limit

## Slide 16: Non-Windup Limits Integrator Block
With non-windup limits, the value of the integral (v previously) is prevented from exceeding its limit. Thus it can immediately back off its limits
Lmax
Lmin
u
y

## Slide 17: Limits on First Order Lag
Windup and non-windup limits are handled in a similar manner for a first order lag
u
y
Lmax
Lmin
v
If Lmin  v  Lmax then y = v
else If v < Lmin then y = Lmin, else if v > Lmax then y = Lmax
Again the value of v is NOT limited, so its value can "windup" beyond the limits, delaying backing off of the limit

## Slide 18: Non-Windup Limit First Order Lag
With a non-windup limit, the value of y is prevented from exceeding its limit
Lmax
Lmin
u
y

## Slide 19: Lead-Lag Non-Windup Limits
There is not a unique way to implement non-windup limits for a lead-lag. This is the one from IEEE 421.5-1995 (Figure E.6)
T2 > T1, T1 > 0, T2 > 0
If y > A, then x = A
If y < B, then x = B
If A y  B, then x = y

## Slide 20: Ignored States
When integrating block diagrams often states are ignored, such as a measurement delay with TR=0
In this case the differential equations just become algebraic constraints
Example: For block at right, as T0, v=Ku
With lead-lag it is quite common for TA=TB, resulting in the block being ignored
u
y
Lmax
Lmin
v

## Slide 21: IEEE T1 Example
Assume previous GENROU case with saturation. Then add a IEEE T1 exciter with Ka=50, Ta=0.04, Ke=-0.06, Te=0.6, Vrmax=1.0, Vrmin= -1.0 For saturation assume Se(2.8) = 0.04, Se(3.73)=0.33
Saturation function is 0.1621(Efd-2.303)2 (for Efd > 2.303); otherwise zero
Efd is initially 3.22
Se(3.22)*Efd=0.437
(Vr-Se*Efd)/Ke=Efd
Vr =0.244
Vref = 2.44/Ka +Vt = 0.0488 + 1.0946=1.1434

## Slide 22: IEEE T1 Example
For 0.1 second fault (from before), plot of Efd and the terminal voltage is given below
Initial V4=1.0946, final V4=1.0973
  Steady-state error depends on the value of Ka

## Slide 23: IEEE T1 Example
Same case, except with Ka=500 to decrease steady-state error, no Vr limits; this case is actually unstable

## Slide 24: IEEE T1 Example
With Ka=500 and rate feedback, Kf=0.05, Tf=0.5
Initial V4=1.0946, final V4=1.0957

## Slide 25: WECC Case Type 1 Exciters
In a recent WECC case with 2782 exciters, 58 are modeled with the IEEE T1, 257 with the EXDC1 and none with the ESDC1A
Graph shows KE value for the EXDC1 exciters in case; about 1/3 are separately excited, and the rest self excited
  Value of KE equal zero indicates code should set KE so Vr initializes to zero; this is used to mimic the operator action of trimming this value

## Slide 26: DC2 Exciters
Other dc exciters exist, such as the EXDC2, which is quite to the EXDC1; about 41 WECC exciters are of this type
Image Source: Fig 4 of "Excitation System Models for Power Stability Studies," IEEE Trans. Power App. and Syst., vol. PAS-100, pp. 494-509, February 1981
Vr limits are multiplied by the terminal voltage

## Slide 27: ESDC4B
Newer dc model introduced in 421.5-2005 in which a PID controller is added; might represent a retrofit
Image Source: Fig 5-4 of IEEE Std 421.5-2005

## Slide 28: Desired Performance
A discussion of the desired performance of exciters is contained in IEEE Std. 421.2-1990
Concerned with
  large signal performance: large, often discrete change in the voltage such as due to a fault; nonlinearities are significant
    Limits can play a significant role
  small signal performance: small disturbances in which close to linear behavior can be assumed
Increasingly exciters have inputs from power system stabilizers, so performance with these signals is important

## Slide 29: Transient Response
Figure shows typical transient response performance to a step change in input
Image Source: IEEE Std 421.2-1990, Figure 3

## Slide 30: Small Signal Performance
Small signal performance can be assessed by either the time responses, frequency response, or eigenvalue analysis
Figure shows the typical open loop performance of an exciter and machine in the frequency domain
Image Source: IEEE Std 421.2-1990, Figure 4

## Slide 31: Small Signal Performance
Figure shows typical closed-loop performance
Image Source: IEEE Std 421.2-1990, Figure 5
Note system connection is open
Peak value of Mp indicates relative stability; too large a value indicates overshoot
We will return to this when we talk about oscillations