## Slide 1: An LSTM-Based Autonomous Driving Model using Waymo Open Dataset
Presented by Peter Du

## Slide 2: Motivation
Development of robust and reliable autonomous policies is an open problem
  Significant interest in area of autonomous vehicles (AVs)
Advances in in computation/simulation has made simulation-based AV research popular
  LGSVL, Carla, OpenAI Gym
Increase in demand for accurate driver, pedestrian, and AV models
Carla
OpenAI Gym

## Slide 3: Modelling AVs & Environments
Physics based models
  Intelligent Drivers Model
  MOBIL
Rule based models
  Responsibility Sensitive Safety
Learning based
  RNN-based pedestrian prediction
  Behaviour cloning (e.g. Nvidia CNN-based driving policy)

## Slide 4: Modelling AVs
Existing AV test fleets are proprietary and unavailable to researchers
Various assumptions on AV behaviour may not represent realistic interactions in simulation-based research
  Safety validation
  Multi-agent decision making
  Reachability analysis

## Slide 5: Modelling AVs
Precise models are unavailable but data on AV behaviour is available
Learn a model of proprietary AV behaviour using sensor data
  Waymo Open Dataset
Adapt an LSTM model previously used for pedestrian trajectory prediction to imitate behaviour of Waymo’s AV model

## Slide 6: Waymo Open Dataset
Publicly available dataset with rich set of diverse AV behaviours
Collected from Waymo L4 vehicles
~45000 video segments
  Contains lidar, radar, camera data
  Labels include object types, bounding boxes, velocities/accelerations

## Slide 7: Predicting Acceleration
Learn a model for lateral/longitudinal acceleration
Basic features (12 dimensional):
  Vehicle position in global frame
  Lead vehicle velocity
  Lead vehicle acceleration
  Lead vehicle relative distance
  Number of vehicles present
Additional features using image embedding and data from cameras

## Slide 8: LSTM Prediction Network
Basic model adapts an LSTM “encoder-decoder” network previously used for pedestrian trajectory prediction
10 frames are stacked together
Output is acceleration for next 5 frames

## Slide 9
Basic model is augmented with image inputs
Each camera feed is preprocessed with pretrained ResNetV2 to create image embedding
LSTM Prediction Network

## Slide 11: Results

## Slide 13: Summary
Learn a model of proprietary AV behaviour through sensor data
LSTM network works well for time-series problem of acceleration prediction
Task of predicting longitudinal/lateral acceleration is still far from a complete vehicle model
Proposed setup isn’t easily generalizable to other maneuvers (e.g. lane changes, merging)
Possible viable solution for AV modelling as more data is released by AV fleet testers