## Slide 1: Lecture Class Slide Presentation 3-26-2020
Again, no video to go with this lecture, just these slides and the associated assignment - Lecture Class Assignment #10
Today we will return to the Engineering Drawing Notes A and continue from where we left off
Before you work through the notes, look at the example engineering drawings form page B-2 to B-11
You will notice that many dimensions have tolerances on the dimensions and they are not always written in the same format.
On Page B-3 for example you will see some written with Unilateral (aka. Symmetric) tolerance such as the width of the part:
BUT part thickness for this part is written differently in a Bilateral format:
You will learn these different ways of writing these along with standard tolerances for different types of fit.
For the Assignment, you will need to need to look at slide 11 to find out what standard tolerance for each of the hole and shaft is required for a “ISO Close Running Fit”. The 12mm dia of the shaft in the Pin Part Drawing has the required tolerance f7 written correctly in Bilateral format. This format is required by the ISO standard. It is written as -0.016 and -0.034. Use Slide 13 to find these numbers for a shaft between 10-18mm, as 12mm is within this range.
Now to complete the 12mm hole dimension and tolerance in the Collar Part Drawing, you need to look for the required tolerance in Slide 11 (i.e. ISO Close Running fit requires an H8 for the hole). Look on Slide 13 to find the correct value by lining up the 10-18mm size range with the required H8 column. Then write the answer on the drawing written in the same manner as in the Pin Part Drawing for the mating shaft feature.
AND then complete the missing lines and dimensions in the left view.
20.25
+
0.04
-
And don’t forget to complete the Lecture Class assignment within the next 3 days for full credit – you can write on the paper then either scan it or take a picture with your smart phone
2.54
0
-0.03

## Slide 2: Tolerances important to interchangeability and provision for replacement parts
It is impossible to make parts to an exact size. The tolerance, or accuracy required, will depend on the function of the part and the particular feature being dimensioned. Therefore, the range of permissible size, or tolerance, must be specified for all dimensions on a drawing, by the designer/draftsperson.
Nominal Size: is the size used for general identification, not the exact size.
Actual Size: is the measured dimension. A shaft of nominal diameter 10 mm may be measured to be an actual size of 9.975 mm.
General Tolerances:
In ISO metric, general tolerances are specified in a note, usually in the title block, typically of the form: "General tolerances ±.25 unless otherwise stated".
In English Units , the decimal place indicates the general tolerance given in the title block notes, typically:
Fractions = ±1/16, .X = ±.03, .XX = ±.01, .XXX = ±.005, .XXXX = ±0.0005,
Note: Fractions and this type of general tolerancing is not permissible in ISO metric standards.

## Slide 3
Specific Tolerances indicate a special situation that cannot be covered by the general tolerance.
Specific tolerances are placed on the drawing with the dimension and have traditionally been expressed in a number of ways:
Specific Tolerances
40
+0.05
- 0.03
40.01
+0.04
40.05
39.97
Bilateral Tolerance
Unilateral Tolerance
Limit Dimensions
Limits are the maximum and minimum sizes permitted by the the tolerance. All of the above methods show that the dimension has:
a Lower Limit = 39.97 mm
an Upper Limit = 40.05 mm
a Tolerance = 0.08 mm
Manufacturing must ensure that the dimensions are kept within the limits specified. Design must not over specify as tolerances have an exponential affect on cost.
-

## Slide 4: Limits and Fits
1. Clearance Fits
The largest permitted shaft diameter is smaller than the diameter of the smallest hole
Min.
Hole
Max.
Hole
HOLE
SHAFT
Max.
Clearance
Min.
Clearance
Min.
Shaft
Max.
Shaft

## Slide 5
2. Interference Fits
The minimum permitted diameter of the shaft is larger than the maximum diameter of the hole
3. Transition Fits
The diameter of the largest allowable hole is greater than that of the smallest shaft, but the smallest hole is smaller than the largest shaft

## Slide 6: Standard Limits and Fits -- ANSI
RC 1 Close sliding fits are intended for the accurate location of parts which must assemble without perceptible play.
RC 2 Sliding fits are intended for accurate location, but with greater maximum clearance than class RC 1. Parts made to this fit move and turn easily but are not intended to run freely, and in the larger sizes may seize with small temperature changes.
RC 3 Precision running fits are about the closest fits which can be expected to run freely, and are intended for precision work at slow speeds and light journal pressures, but are not suitable where appreciable temperature differences are likely to be encountered.
RC 4 Close running fits are intended chiefly for running fits on accurate machinery with moderate surface speeds and journal pressures, where accurate location and minimum play are desired.
RC 5
RC 6
Basic hole system. Limits are in thousandths of an inch.
Class RC 1
Limits of
Clearance
Standard
Limits
Hole
H5
Shaft
g4
Class RC 2
Limits of
Clearance
Standard
Limits
Hole
H6
Shaft
g5
Class RC 3
Limits of
Clearance
Standard
Limits
Hole
H7
Shaft
f6
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
Class RC 5
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
e7
Class RC 6
Limits of
Clearance
Standard
Limits
Hole
H9
Shaft
e8
Medium running fits are intended for higher running speeds, or heavy journal pressures, or both.
Nominal
Size Range
in
Inches
0 - 0.12 0.1 + 0.2 - 0.1 0.1 + 0.25 - 0.1 0.3 + 0.4 - 0.3 0.3 + 0.6 - 0.3 0.6 + 0.6 - 0.6 0.6 + 1.0 - 0.6
0.45 - 0 - 0.25 0.55 - 0 - 0.3 0.95 - 0 - 0.55 1.3 - 0 - 0.7 1.6 - 0 - 1.0 2.2 - 0 - 1.2
0.12 - 0.24 0.15 + 0.2 - 0.15 0.15 + 0.3 - 0.15 0.4 + 0.5 - 0.4 0.4 + 0.7 - 0.4 0.8 + 0.7 - 0.8 0.8 + 1.2 - 0.8
0.5 - 0 - 0.3 0.65 - 0 - 0.35 1.12 - 0 - 0.7 1.6 - 0 - 0.9 2.0 - 0 - 1.3 2.7 - 0 - 1.5
0.24 - 0.40 0.2 + 0.25 - 0.2 0.2 + 0.4 - 0.2 0.5 + 0.6 - 0.5 0.5 + 0.9 - 0.5 1.0 + 0.9 - 1.0 1.0 + 1.4 - 1.0
0.6 - 0 - 0.35 0.85 - 0 - 0.45 1.5 - 0 - 0.9 2.0 - 0 - 1.1 2.5 - 0 - 1.6 3.3 - 0 - 1.9
0.40 - 0.71 0.25 + 0.3 - 0.25 0.25 + 0.4 - 0.25 0.6 + 0.7 - 0.6 0.6 + 1.0 - 0.6 1.2 + 1.0 - 1.2 1.2 + 1.6 - 1.2
0.75 - 0 - 0.45 0.95 - 0 - 0.55 1.7 - 0 - 1.0 2.3 - 0 - 1.3 2.9 - 0 - 1.9 3.8 - 0 - 2.2
0.71 - 1.19 0.3 + 0.4 - 0.3 0.3 + 0.5 - 0.3 0.8 + 0.8 - 0.8 0.8 + 1.2 - 0.8 1.6 + 1.2 - 1.6 1.6 + 2.0 - 1.6
0.95 - 0 - 0.55 1.2 - 0 - 0.7 2.1 - 0 - 1.3 2.8 - 0 - 1.6 3.6 - 0 - 2.4 4.8 - 0 - 2.8
1.19 - 1.97
1.97 - 3.15
Extract from Table of Clearance Fits

## Slide 7: ISO Tolerance Designation
The ISO system provides for:
21 types of holes (standard tolerances) designated by uppercase letters A, B, C, D, E....etc. and
21 types of shafts designated by the lower case letters a, b, c, d, e...etc.
These letters define the position of the tolerance zone relative to the nominal size. To each of these types of hole or shaft are applied 16 grades of tolerance, designated by numbers IT1 to IT16 - the "Fundamental Tolerances":
ITn = (0.45 x 3 D +0.001 D) Pn
where D is the mean of the range of diameters and Pn is the progression:1, 1.6, 2.5, 4.0, 6.0, 10, 16, 25......etc. which makes each tolerance grade approximately 60% of its predecessor.

## Slide 8: For Example:
Experience has shown that the dimensional accuracy of manufactured parts is approximately proportional to the cube root of the size of the part.
Example:
A hole is specified as: 30 H7
The H class of holes has limits of . i.e. all tolerances start at the nominal size and go positive by the amount designated by the IT number.
IT7 for diameters ranging 30- 50 mm:
+ x
+ 0
Tolerance for IT7 = (0.45 x 3 40 +0.001x 40) 16 = 0.025 mm
Written on a drawing as 30 H7

## Slide 9
Graphical illustration of ISO standard fits
Hole Series – H hole Standard

## Slide 10: Selection of Fits and the ISO Hole Basis system
From the above it will be realized that there are a very large number of combinations of hole deviation and tolerance with shaft deviation and tolerance. However, a given manufacturing organization will require a number of different types of fit ranging from tight drive fits to light running fits for bearings etc. Such a series of fits may be obtained using one of two standard systems:
The Shaft Basis System:
For a given nominal size a series of fits is arranged for a given nominal size using a standard shaft and varying the limits on the hole.
The Hole Basis System:
For a given nominal size, the limits on the hole are kept constant, and a series of fits are obtained by only varying the limits on the shaft.
The HOLE SYSTEM is commonly used because holes are more difficult to produce to a given size and are more difficult to inspect. The H series (lower limit at nominal, 0.00) is typically used and standard tooling (e.g. H7 reamers) and gauges are common for this standard.

## Slide 11: ISO Standard "Hole Basis" Clearance Fits
Type of Fit
Hole
Shaft
Loose Running Fits
. Suitable for loose pulleys
and the looser fastener fits where freedom of
assembly is of prime importance
H11
c11
Free Running Fit.
Where accuracy is not
essential, but good for large temperature
variation, high running speeds, heavy journal
pressures
H9
d10
Close Running Fit.
Suitable for lubricated
bearing, greater accuracy, accurate location,
where no substantial temperature difference is
encountered.
H8
f7
Sliding Fits
. Suitable for precision location fits.
Shafts are expensive to manufacture since the
clearances are small and they are not
recommended for running fits except in
precision equipment where the shaft loadings
are very light.
H7
g6
Locational Clearance Fits
. Provides snug fit
for locating stationary parts; but can be freely
assembled and disassembled.
H7
h6

## Slide 12
ISO Standard "Hole Basis”
Transition Fits
Type of Fit
Locational Transition Fits
. for accurate
location, a compromise between clearance and
interference
Push Fits
. Transition fits averaging little or no
clearance and are recommended for location fits
where a slight interferance can be tolerated for
the purpose, for example, of eliminating vibration.
Hole
Shaft
H7
k6
H7
n6
ISO Standard "Hole Basis"
Interference Fits
Type of Fit
Press Fit
. Suitable as the standard press fit into
ferrous, i.e. steel, cast iron etc., assemblies.
Drive Fit
Suitable as press fits in
material of low modulus of elasticity such as
light alloys.
Hole
Shaft
H7
p6
H7
s6

## Slide 13
ISO Clearance Fits
Loose Running Fit
Free Running Fit
Close Running Fit
Sliding Fit
Locational Clearance

## Slide 14
Nominal Sizes
Tolerance
Over
To
H7
k6
H7
n6
mm
––
mm
3
0.001 mm
+10
0
0.001 mm
+6
+0
0.001 mm
+10
0
0.001 mm
+10
+4
3
6
+12
0
+9
+1
+12
0
+16
+8
6
10
+15
0
+10
+1
+15
0
+19
+10
10
18
+18
0
+12
+1
+18
0
+23
+12
18
30
+21
0
+15
+2
+21
0
+23
+15
30
40
+25
+18
25
+33
40
50
0
+2
0
+17
50
65
+30
+21
+30
+39
65
80
0
+2
0
+20
80
100
+35
+25
+35
+45
100
120
0
+3
0
+23
120
140
140
160
+40
0
+28
+3
+40
0
+52
+27
160
180
180
200
200
225
+46
0
+33
+4
+46
0
+60
+34
225
250
250
280
+52
-32
+52
+36
280
315
0
-
0
+4
315
355
+57
+40
+57
+73
355
400
0
+4
0
+37
400
450
+63
+45
+63
+80
450
500
0
+5
0
+40
ISO
Transition
Fits
Locational Fit
Push Fit

## Slide 15
ISO
Interference
Fits
Press Fit
Drive Fit