## Slide 1: Lecture Class Slide Presentation 3-31-2020
Carrying on with the Engineering Drawing A set of notes, today we are going start by doing another assignment to help you understand how to use International Tolerance zones (e.g. H7, f7 etc) and the use standard ISO Limits and Fits. You will again use the tables in the notes. When you come to choose what fits and tolerances to use for your projects, particularly the moving parts, you can use these tables or have Creo automatically extract the values; so you don’t have to look them up in the tables.
Lecture Class Assignment #12 takes a typical ball bearing, that you might choose from a catalog, and explains how you would follow the catalog’s technical specs to design the custom mating parts correctly.
I will start the lecture by taking you though this assignment and completing part of it for you.
Then we will take a look at assembly tolerancing and the concept of “worst case tolerances”. I will be asking you to follow this principal, and the associated axial tolerance analysis, as one of the deliverables of your project; and prove to me that your proposed assembly will go together and work as intended, taking into consideration natural variations in size as parts are manufactured.
And don’t forget to complete the Lecture Class assignment within the next 3 days for full credit – you can type within powerpoint, or print on paper then either scan it or take a picture with your smart phone

## Slide 2
Context of this weeks lecture class assignment – Purchased bearings (off-the-shelf) for a new roller blade design. What tolerances to put on the mating parts?
Roller Blade Assembly Model
Exploded View of Roller Blade Assembly

## Slide 3
The Ball Bearing specifications say that it should be assembled into the housing with an “ISO Push Fit” and that the shaft should be inserted with an “ISO Press Fit”
1. Specify the dimensions for the shaft diameter (in ISO bilateral form):
2. Specify the dimensions for housing diameter (also in bilateral form):
Lecture Class Assignment #12 – Tolerances – Ball Bearing fits
‘Shaft’ Diameter
‘Housing’ Diameter
Ball Bearing
(8mm I/D x 22mm O/D)
I have copied the assignment to the right here so that I can refer to it. And labeled the key parts that:
Determine the fit between the ‘shaft’ and the ID (inside diameter) of the bearing.
Determine the fit between the OD (outside Diameter) of the ball bearing and the Housing
The bearing is purchased with a tolerance. When you purchase a part like this, the manufacturer will include the tolerances of the part in the specifications so that design engineers, like you, know what to expect. They will generally also tell you what fit is required for the device to perform as designed. These fits for 1. and 2. above are specified as:
An ISO Press Fit
An ISO Push Fit
These fits are described in the following slide:

## Slide 4
ISO Standard "Hole Basis”
Transition Fits
Type of Fit
Locational Transition Fits
. for accurate
location, a compromise between clearance and
interference
Push Fits
. Transition fits averaging little or no
clearance and are recommended for location fits
where a slight interferance can be tolerated for
the purpose, for example, of eliminating vibration.
Hole
Shaft
H7
k6
H7
n6
ISO Standard "Hole Basis"
Interference Fits
Type of Fit
Press Fit
. Suitable as the standard press fit into
ferrous, i.e. steel, cast iron etc., assemblies.
Drive Fit
Suitable as press fits in
material of low modulus of elasticity such as
light alloys.
Hole
Shaft
H7
p6
H7
s6
Press Fit
Drive Fit
ISO
Interference
Fits
Slide 63 of Engineering Drawing A notes
Slide 66 of Engineering Drawing A notes

## Slide 5
The Ball Bearing specifications say that it should be assembled into the housing with an “ISO Push Fit” and that the shaft should be inserted with an “ISO Press Fit”
1. Specify the dimensions for the shaft diameter (in ISO bilateral form):
2. Specify the dimensions for housing diameter (also in bilateral form):
Lecture Class Assignment #12 – Tolerances – Ball Bearing fits
‘Shaft’ Diameter
‘Housing’ Diameter
Ball Bearing
(8mm I/D x 22mm O/D)
+ 0.024
+ 0.015
(
)
f8 p6
So, here’s the answer to the 1st part:
1. Specify the dimensions for the ‘shaft’ diameter (in ISO bilateral form):
This is in quotes because its probably not really what you would think of as the shaft in this assembly, however, in the context of standard “Limits and Fits” the tables, whether ANSI or ISO, uses the terms ‘Shaft’ to describe the part to be inserted INTO the receiving part or ‘Hole’.
In this ball bearing assembly, the black nylon sleeve is the ‘shaft’ as it inserted into the ID of the bearing, the ‘hole’ of the bearing.
Referring to the previous slide, we see that for the specified ‘ISO Press Fit’, the ‘hole’ should be an H7 and the ‘shaft’ should be a p6 (note: holes always use uppercase (i.e. H here) and shafts always use lowercase (i.e. p here)
The ‘hole’ is the ID of the bearing and we can assume that it was manufactured to the H7 required by the fit. The ‘shaft’ is also the diameter of the bearing but required to be p6, for the bearing to perform correctly. I have circled the relevant row and column data that provide the answer shown here. Follow the same logic to complete 2.- same format

## Slide 6
Tolerance Calculation - 'Worst Case Method'
for correct fit in all cases, if manufactured to specification
'Shaft in hole'
Shaft
Hole
Terminology

## Slide 7
Shaft in Hole
Lid on Box
Allowance = Smallest Hole Size (A) – Largest Shaft Size (B)
Clearance = Largest Hole Size (A) – Smallest Shaft Size (B)
A
A
B
B
For example: If the nominal dimension is 10mm and general tolerance invoked i.e. feature A and B (Hole & Shaft) are both:
+ 0.125
- 0.125
‘Worst Case’ Tolerance Example
General Tolerance +/- 0.125 unless otherwise specified
All units in mms
10
Then,
Clearance = 10.125 – 9.875 = 0.25
Allowance = 9.875 – 10.125 = - 0.25 *
* A negative in the result means interference
(i.e. overall tolerance of 0.25 mm)

## Slide 8
Lid on Box
Allowance = Smallest Hole Size (A) – Largest Shaft Size (B)
Clearance = Largest Hole Size (A) – Smallest Shaft Size (B)
General Tolerance +/- 0.125 unless otherwise specified
All units in mms
So,
Clearance = 10.125 – 9.875 = 0.25
Allowance = 10 – 10 = 0
No negative therefore no interference even in ‘worst case’, so lid will fit on the box relatively easily in all designed conditions.
Use Specific Tolerances as required but keep overall tolerance as loose as possible for function/aesthetic
+ 0.000
- 0.125
10
+ 0.125
- 0.000
10
+ 0.125
- 0.000
10
+ 0.000
- 0.125
10

## Slide 9
Lecture Class Assignment XXX- Worst Case Tolerance - Block and Carrier
Blocks
Carrier
1. What is the clearance between the between the blocks and the carrier _______1.2_____
2. What is the allowance between the blocks and the carrier ______0_____
2
+ 0.2
- 0.2
4
+ 0.8
+ 0.4
Name: Solution
Clearance = Largest Hole – Smallest Shaft
Allowance = Smallest Hole – Largest Shaft
A
B
A
B
Largest Hole = 4.8
Smallest Shaft = 1.8 + 1.8 = 3.6
Clearance = 4.8 – 3.6 = 1.2
Smallest hole = 4.4
Largest shaft = 2.2 + 2.2 = 4.4
Allowance = 4.4 – 4.4 = 0
A
B
A
B