## Slide 1: Lecture Class Slide Presentation 4-7-2020
Another week has gone by! Lets take a quick look at the class schedule (see below).
In lab this week, you will be learning how to create Engineering Part Drawings (aka. Detail Drawings). You will need to create engineering drawings for all your custom designed parts in your Term Design Projects. These should be fully dimensioned, and toleranced appropriately, so they can be assembled together, are fully interchangeable, and function as designed every time.
In your teams, you should be working on the CAD modeling of your product and have made some good progress. Your first, preliminary presentations are due in just a couple of weeks. You will need to send your TA and grader a few screenshots of your CAD model at that time so they can review and make sure you are on the right track. P.S. I am about to post some detailed deliverables required for your presentations and final report, on the website under in Design Project section; so look out for this; they add a little clarity to the summary version.
In lecture class, this week we will wrap up the Engineering Drawing A set of notes and take a look at the B set to understand concepts of GD&T “Geometric Dimensioning and Tolerancing”.
And don’t forget to complete the Lecture Class assignment within the next 3 days for full credit – you can type within powerpoint, or print on paper then either scan it or take a picture with your smart phone

## Slide 2
At the end of last week we looked at checking the assemblability of your design to ensure that individual part tolerances don’t “build-up”, and create a situation where parts don’t assemble and/or function correctly.
I have copied the assignment to the right here so that I can refer to it. Imagine you have designed a pulley that is mounted on a shaft with two plain bearings/bushings.
The pulley must be free to rotate between the two bushings when assembled. The 20 dimension is the dimension of the housing and I have put a tolerance on there that should allow the other parts to run freely and without causing interference.
By checking the “worst case” Clearance and Allowance (biggest and smallest gap), we can check that this will work assuming the manufacturers keep to the design tolerances of the individual mating parts. The “worst case” being when they are each manufactured at their smallest and largest conditions while still being “within tolerance”.
Assembly
1. What is the worst case Clearance ___________
2. What is the worst case Allowance ____________
2
+ 0.125
- 0.125
20
+ 0.500
+ 0.375
Reminder:
Allowance = Smallest Hole – Largest Shaft
Clearance = Largest Hole – Smallest Shaft
16
+ 0.125
- 0.125
Pulley
Solid Bronze bearings
Shaft
Housing

## Slide 3
Last 5 slides of
ENGINEERING DRAWING NOTES A
The next 5 slides cover a few additional properties and their associated symbols that you will need to consider beyond dimensions and tolerances on an Engineering Drawing:
  Surface Texture (aka: Surface Finish or Surface Roughness) - very much a function of the manufacturing process. A shaft with a plain bearing rubbing on it will need to have a good surface finish so it does not cause premature wear on the surface of the bearing.
  Hardness: Full hardness, or Surface Hardness (aka; Case Hardening) – typically the natural state of the material combined with addition hardening processes. A shaft with a bearing rubbing on it with need to have a hard surface so it doesn’t wear too fast.
  Weld Symbols: where you need to connect two parts together by welding. (p.s. generally try to avoid welding parts together; its an expensive process and prone to failure)

## Slide 4
Mike Philpott
Model Car Shaft
2/12/2008
RC102
Material: 1040 Steel
What’s this?

## Slide 5
Basic Surface Texture Symbol
With Roughness Value
(Typically Ra µm or µ”)
0.4
Material Removal by Machining
With Machining Allowance
2
Harden = HDN - may see symbol
Heat Treat = H/T
Rockwell = HRC, HRA etc or Ra or Rc
Brinell = BNL
Hardness
Surface Finish
HDN to 65 HRC 0.125 DP
0.4
Surface Properties -
Texture and Hardness

## Slide 6
Comparative Roughness Values
Roughness Ra Typical Processes
25 µm (1000 µ”) Flame Cutting
12.5 µm (500µ”) Sawing, sand casting,
6.3 µm (250µ”) forging, shaping, planing
3.2 µm (125µ”) Rough machining, milling, rough turning, drilling, and die casting
1.6 µm (63µ”) Machining, turning, milling, die and investment casting, injection molding, and stamping
0.8 µm (32µ”) Grinding, fine turning & milling, reaming, honing, injection molding, stamping, investment casting
0.4 µm (16µ”) Diamond Turning, Grinding, lapping, honing
0.2 µm (8µ”) Lapping, honing, polishing
0.1 µm (4µ”) Superfinishing, polishing, lapping

## Slide 7
Some Common Steel, Hardness and Surface Finish Specs.
Common Steel Specs: (10xx series: xx = % carbon)
Mild steel (low carbon = up to 30 %): Low cost general purpose applications, typ. hardening not required
Medium Carbon (up to 60%): requiring higher strength; e.g. gears, axles, con-rods etc.
High Carbon (> 60%): High wear, high strength; e.g. cutting tools, springs etc.
Ground Bearing Shaft Examples:
General Purpose
1060: Surface HDN to 55 HRC 0.125 mm deep min.; 0.4 µm (16 µ”)
303 Stainless: (natural surface hardness 5 HRC ); 0.4µm (16 µ”)
Better Finish, Longer Life
1020: Case HDN to 65 HRC 0.25 mm deep min.; 0.2µm (8 µ”)
440 Stainless: (natural circa 15 HRC); 0.2µm (8 µ”)
1020
1040,
1060
1080
Common
Types

## Slide 8
Specifying Welds on Drawings
Width of weld

## Slide 9
B
aka: “GD&T”
You need to understand GD&T concepts as many companies, particularly large internationals, have adopted this relatively new system. For your projects, I do not require it, but feel free to add some appropriate geometry symbols if you think it’s required.