## Slide 1: BME 680
Measurement of atmospheric pressure

## Slide 2: What is a BME680?
Temperature, humidity, pressure and gas sensor
Produced by Bosch, Distributed by Adafruit Industries
Is higher-end than BME280 atmospheric sensor

## Slide 3: Atmospheric pressure sensing capability
Measures barometric pressure to +- 1 millibar precision
  300-1100 mb
182 Hz sampling rate

## Slide 4: How does the BME measure pressure?
Modern microelectromechanical system (MEMS) technology
  “Resistive” vs. “Capacitive”
A small, flexible membrane is exposed to the atmosphere on one side
  A variable-capacitance material is attached to the opposite side and measures the force on the membrane

## Slide 5: How does the BME measure pressure?
The resistance of the strain-measuring material changes as is it compressed by the membrane
  The change in resistance is calibrated to relate to atmospheric pressure.
There is an optional IIR filter for pressure measurements
  Eliminates short term fluctuations in pressure

## Slide 6: References
https://cdn-shop.adafruit.com/product-files/3660/BME680.pdf
https://www.avnet.com/wps/portal/abacus/solutions/technologies/sensors/pressure-sensors/media-types/barometric/
https://www.hbm.com/en/7646/what-is-a-pressure-sensor/